## Slide 1: U-SIG Design for TB PPDU
Date: 2020-09-08
Authors:
Name | Affiliations | Address | Phone | Email
Alice Chen | Qualcomm |  |  | alicel@qti.qualcomm.com
Sameer Vermani |  |  |  | svermani@qti.qualcomm.com
Bin Tian |  |  |  | btian@qti.qualcomm.com
Youhan Kim |  |  |  | youhank@qti.qualcomm.com
Notes: September 2012

## Slide 2: Introduction: EHT TB PPDU
In TB PPDU, there is a 2-symbol U-SIG, and no EHT-SIG
  52 bits in U-SIG need to accommodate all the version independent fields and version dependent fields
In this presentation, we discuss the U-SIG design for TB PPDU
L-STF
L-LTF
L-SIG
RL SIG
U-SIG
TB PPDU
EHT-STF
EHT-LTFs
Data

## Slide 3: U-SIG Design in TB PPDU
U-SIG of TB PPDU contains the same version independent fields as U-SIG of the EHT MU PPDU as well as PPDU Format & EHT-SIG Compression field (+1 reserved bit)
We leave ~2 reserved bits
17 TBD bits many not be enough to satisfy all the potential needs in the following
  11ax like SR fields (e.g. 16 bits for 160MHz)
  Punctured channel information
  Additional bits needed for U-SIG version independent fields: like more bits for BSS color or TXOP
  Reserved bits for R2 features
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 2
 |  | TBD1 | 4
 | Version Dependent | PPDU format & EHT-SIG Compression | 2
 |  | Reserved | 1
 |  | TBD2 | 13
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52

## Slide 4: Punctured Channel Indication
The following IEEE motion may indicate that punctured channel indication is needed in EHT PPDU
  “802.11be signaling in U-SIG for BW/puncturing information in every non-punctured 20 MHz of an 80 MHz segment shall allow even an OBSS or unassociated device to decode the puncturing pattern of at least the specific 80 MHz that contains the 20 MHz.” ([Motion 113, [9] and [46]])
Do we really need punctured channel indication in TB PPDU?
  AP doesn’t need this info
  A version dependent field is less meaningful for bystanders
  If an OBSS or unassociated device decodes the U-SIG of TB PPDU, it doesn’t need to know the puncturing pattern of the current 80MHz
  The puncturing information comes from the content in trigger frame and may not accurately reflect the true puncturing information
We propose not to have punctured channel indication

## Slide 5: Spatial Reuse
Discussion on number of spatial reuse (SR) fields
  TB PPDU is the main use-case for spatial reuse
  The SR field(s) in U-SIG should carry SR info of entire PPDU BW
    Receiver only needs to decode U-SIG in the current 80MHz
  In 11ax, HE-SIG-A of HE TB PPDU has 16 bits for 4 SR fields
    16 bits for 11be is not realistic as it does not leave any room for other fields
  If there is only one SR field (4 bits) for entire PPDU BW, the granularity may not be good enough
We propose to use two SR fields (4 bits each, total 8 bits), with granularity of half PPDU BW, but no smaller than 20MHz
  A good compromise between SR field granularity and leaving enough bits to accommodate other functionalities

## Slide 6: U-SIG Design in TB PPDU
With our proposed two SR fields design, in addition to the 2 reserved bits we left after the version independent fields, there are other 9 reserved bits in R1
  They may be used to accommodate more bits for BSS color or TXOP, or R2 features
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 2
 |  | TBD1 | 4
 | Version Dependent | PPDU format & EHT-SIG Compression | 2
 |  | Reserved | 1
 |  | Spatial Reuse 1 | 4
 |  | Spatial Reuse 2 | 4
 |  | TBD2 | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52

## Slide 7: SP 1
Do you support not to have punctured channel indication in the U-SIG of TB PPDU?
Y/N/A

## Slide 8: SP 2
Do you support to have two SR fields (4 bits each, total 8 bits), with granularity of half PPDU BW, but no smaller than 20MHz, in the U-SIG of TB PPDU?
Y/N/A

## Slide 9: appendix

## Slide 10: Spatial Reuse Field in TB PPDU
Reuse the 4-bit table for the SR field in the 11be TB PPDU

## Slide 11: Recap: HE-SIG-A in HE TB PPDU
HE-SIG-A1 | N_bit | Field | HE-SIG-A2 | N_bit | Field
B0 | 1 | Format | B0-B6 | 7 | TXOP
B1-B6 | 6 | BSS color | B7-B15 | 9 | Reserved to UL HE-SIG-A2 reserved subfield in the trigger frame
B7-B10 | 4 | Spatial reuse 1 | B16-B19 | 4 | CRC
B11-14 | 4 | Spatial reuse 2 | B20-B25 | 6 | Tail
B15-B18 | 4 | Spatial reuse 3 |  |  | 
B19-B22 | 4 | Spatial reuse 4 |  |  | 
B23 | 1 | Reserved to 1 |  |  | 
B24-B25 | 2 | Bandwidth |  |  |