## Slide 1: TID-to-Link Mapping Negotiation
Date: 2020-09-02
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei |  |  | huangguogang1@huawei.com
Ming Gan |  |  |  | 
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Yiqing Li |  |  |  | 
Mengyao Ma |  |  |  | 
Notes: September 2012

## Slide 2: Introduction (1)
The following motion [1] is passed
  The TID-to-link mapping can be updated after multi-link setup through a negotiation, which can be initiated by any MLD.
    Format TBD.
    NOTE – When the responding MLD cannot accept the update, it can reject the TID-to-link mapping update.

## Slide 3: Introduction (2)
On the one hand, the non-AP MLD may initiate the TID-to-link mapping negotiation request for the following reason(s):
  Link unreachability
  Power save
  Bad QoS for some TID
On the other hand, the AP MLD also can initiate the TID-to-link mapping negotiation request for the following reason(s):
  Admission control based on the type of STAs, STA capabilities and so on
  Load balance
  Separation of delay-sensitive traffic and delay-tolerant traffic
  Separation of downlink traffic and uplink traffic

## Slide 4: Problem Statement
Moreover, if considering that the TID is directional, there are 16 TIDs and each TID may have the different link set
However, the responder may reject or accept with/without a minor change to the proposed mapping
So the question is how to reduce the number of TID-to-link mapping negotiation and speed up the convergence of the final TID-to-link mapping scheme
TID-to-link Mapping Response
TID-to-link Mapping Request
Non-AP MLD (AP MLD)
AP MLD (Non-AP MLD)
Time

## Slide 5: Proposed Solution (1)
Some auxiliary information can be provided by non-AP MLD to assist the AP MLD to decide whether to reject or accept with/without a minor change to the TID-to-link mapping, e.g.
  Info on link RSSI or disable link set if the TID-to-link mapping negotiation is initiated due to the link unreachability
  Info on max number of enable links or disable link set if the TID-to-link mapping negotiation is initiated due to the power save
  Info on QoS of TID(s) if the TID-to-link mapping negotiation is initiated due to the bad QoS of delay-sensitive TID(s)

## Slide 6: Proposed Solution (2)
Since these auxiliary information is optional, there are two options to signal whether the corresponding info is present
  Option 1. Use a control bit to indicate whether the corresponding info field is present
  Option 2. Define the corresponding info as optional Report elements

## Slide 7: Summary
This contribution proposes that the non-AP MLD provides some auxiliary information to assist the AP MLD to decide whether to reject or accept with/without a minor change to the TID-to-link mapping
  Info on link RSSI or disable link set if the TID-to-link mapping negotiation is initiated due to the link unreachability or some reason
  Info on max number of enable links or disable link set if the TID-to-link mapping negotiation is initiated due to the power save
  Info on QoS of TID(s) if the TID-to-link mapping negotiation is initiated due to the bad QoS of delay-sensitive TID(s)

## Slide 8: Reference
[1] 11-20-0566-69-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx

## Slide 9: SP
Do you support that the non-AP MLD provides some auxiliary information to assist the AP MLD to decide the final TID-to-link mapping?
  Yes
  No
  Abstain