## Slide 1
Multilink Management for
Non-STR Soft AP
Date: 2020-10-06
Authors:

## Slide 2: Introduction
Soft AP for MLD operation has been defined in SFD [1]
  802.11be defines mechanisms to support the operation of a Non-STR AP MLD in R1. The mechanisms are limited to instantiate a Non-STR Non-AP MLD as a Soft AP that could utilize all its links under TBD conditions. The exact language to govern such scope is TBD.
Non-STR AP MLD has not been fully considered
  In [2], Non-STR AP MLD’s operation is discussed
    Soft AP can be a non-STR MLD and power saving operation may impact the other link’s normal operation.
  NSTR link pair for Soft AP should be considered for various scenarios including tethering with AP
  In [3], restricted TWT is proposed to reduce the delay and can be applied to Soft AP
    However, restricted TWT does not fully consider NSTR link pair issue of soft AP
This contribution discusses NSTR link pair issues for two possible Soft AP use cases

## Slide 3: Recap: Definition of soft AP [4]
Soft access point (AP) multi-link device (MLD): An AP MLD with restricted capabilities that is in a battery powered (other characteristics TBD) device.
Non Simultaneous Transmit and Receive (NSTR) soft access point (AP) multi-link device (MLD): A soft AP MLD having at least one non-STR link pair.

## Slide 4: Soft AP MLD multi-link use cases
Soft AP can act as a STA and / or an AP
In a certain scenario, Soft AP should be able to operate as a STA and an AP at the same time
  Case 1: Shared multi-link case
    All links are used for communication with an AP and with STAs
    Links utilization is high but link management complexity is also high
  Case 2: Separated multi-link case
    Separated links from the link(s), which are used for communication with an AP, are used for communication with STAs
    For simplicity, this might be a preferred use case

## Slide 5: Case 1: Shared multi-link
No distinction of links for communication with AP and STAs
  All STAs shall be aware of NSTR link pair and monitor all links
  STAs shall not transmit to Soft AP during the deaf period
  For power saving, TWT based solution proposed [2] might resolve this issue.

## Slide 6: Case 2: Separated multi-link
Links are separated for communication with AP and STAs
  All STAs associated with Soft AP are not aware of the link status of the NSTR link pair
  Need a mechanism for Soft AP to inform STAs of ongoing traffic on the NSTR link pair

## Slide 7: Conclusion
In this contribution, two possible Soft AP use cases are considered
  Case 1: Shared multi-link
  Case 2: Separated multi-link
For NSTR link pair issue, NSTR AP multi-link operation shall be defined
  Case 1: Shared multi-link
    All STAs shall monitor all links (new rule for STAs)
    Soft AP can inform STAs of the other links status
  Case 2: Separated multi-link
    Soft AP shall inform STAs of the other links status
In order to proceed the Soft AP procedure development further, allowable Soft AP use cases shall be decided

## Slide 8: Reference
[1] 11-20/0566r70, “Compendium of straw polls and
potential changes to the Specification Framework Document”
[2] 11-20/1402r0, “Issues on MLD Power Saving”
[3] 11-20/1046r5, “Prioritized EDCA channel access – slot management”
[4] 11-20/1407r12 “Proposed Draft Text for MLO: Soft AP MLD Operation”

## Slide 9: Straw Poll #1
Which Soft AP use case is allowable?
  Option 1: Shared multi-links
    No distinction between links used for communication with AP and links used for communication with STAs
  Option 2: Separated multi-links
    Certain links are designated for communication with AP
    Some links are only used for communication with STAs
  Option 3: Both
  Option 4: Neither