## Slide 1: Multi-AP Coordination: Recap and Additional Considerations
Date: 2020-10-28
Authors:

## Slide 2: Abstract
This contribution recaps the various topics discussed for multi-AP coordination before going on to highlight some concerns regarding incorporation of multi-link devices/operation in the coordination process. Moreover, a general (high-level) process for group formation and coordination scheme selection is also discussed.

## Slide 3: Multi-AP Coordination Revisited (1/6)
Topic | Ref | Key Contribution
Basic definition, setup, and transmission procedure | [1] | Candidate/operation sets along with are roles (sharing/shared, coordinator/coordinated APs) are defined, and stages of multi-AP operation procedures (setup, coordination, transmission) are discussed.
 | [2] | A method is described where AP establishes link with its neighboring AP to acquire information about STA.
 | [3] | STA-triggered synchronous multi-AP transmission is proposed. Correspondingly master and slave AP terminologies are suggested
 | [4] | A unified transmission procedure is presented. A (slave) trigger frame is proposed to provide synchronization and resource allocation
 | [5] | The multi-AP procedure is divided into sounding, selection and transmission stages. Regarding the selection process, buffer state and bandwidth can be helpful in resource allocation.
 | [6] | General transmission procedure is discussed with emphasis on flexibility

## Slide 4: Multi-AP Coordination Revisited (2/6)
Topic | Ref | Key Contribution
Operation | [7] | Data transmission (after successful sounding) is considered. Procedure of multi-AP selection is discussed where the M-AP sends a selection frame to selected APs and the selected S-APs respond to it. If a S-AP is unable to respond, the M-AP selects other S-AP(s).
 | [8] | The multi-AP architecture is discussed considering the multi-AP set with/without anchor, data and control channel interfaces for inter-AP communication, backhaul options (dedicated or not).
Virtual BSS | [9] | Two-level BSS is discussed where the STA only switches from member BSS (no coordinated transmission) to virtual BSS (using coordinated transmission) when link quality degrades beyond a threshold.
 | [10] | 802.11r is used as a reference. Infrastructure BSS with a group of APs coordinated by V-BSS coordinator is described. Can enable single association and authentication state maintenance.

## Slide 5: Multi-AP Coordination Revisited (3/6)
Topic | Ref | Key Contribution
Sounding | [11] | Sequential sounding with explicit CSI feedback is discussed.
 | [12] | Code-based multi-AP joint sounding is proposed, and some initial simulation results are provided comparing code-based approach with sequential sounding.
 | [13] | Performance of code-based joint sounding (all APs send the NDPA and NDP simultaneously) is shown via simulation. Code-based method is better than tone selection in low SNR region.
 | [14] | Implicit sounding is discussed. Centralized & sequential approaches are proposed.
 | [15] | For MU-MIMO implicit sounding might not provide good enough quality. Therefore, joint explicit sounding is proposed as an option for 802.11be.
 | [16] | A method for selective feedback of BFR by STA(s) is discussed. Only if the channel quality between STA and AP is good does the STA feedback BFR to the AP.
 | [17] | Synchronized and independent NDP transmissions are considered for JT and CBF, respectively.

## Slide 6: Multi-AP Coordination Revisited (4/6)
Topic | Ref | Key Contribution
Group formation | [18] | Concept of static and dynamic groups is presented where the latter is a subset of the former. Furthermore, the STA(s) may recommend the candidate APs.
 | [19] | A relatively manageable environment (enterprise/factory) seems a practical scenario. Metric-based and dynamic coordinator AP selection approaches are discouraged due to associated overhead. Should it be defined in the standard or left to implementation?
 | [20] | Candidate set is defined according to boundary of trust. Multiple APs may be capable of acting as a sharing AP within the candidate set.
 | [21] | Boundary of coordination functions is discussed. Some cases where you would NOT want the APs to coordinate with each other (similar to SRG group defined in 11ax). Authentication of MAP trigger frames is highlighted. All or some selected APs may be able to initiate/trigger coordination

## Slide 7: Multi-AP Coordination Revisited (5/6)
Topic | Ref | Key Contribution
Schemes | [22] | OTA synchronization is proposed between APs to announce upcoming transmissions. Frist, the announced SR frame describes the transmission with Tx power constraints, TXOP information and UL/DL nature, followed by transmission of APs to their respective STAs. At the end, the STAs respond with their acknowledgment.
 | [23] | Transmitter nulling/ZF and scheduling at each AP is considered with MMSE receivers. Results show CBF provides significant gains as compared to single AP and CSR.
 | [24] | Results show that using Co-OFDMA with higher probability does not provide much performance gain regarding burst throughput and latency, conversely, using co-OFDMA with lower probability is better.
Data Sharing and Backhaul | [25] | Unicast, broadcast and multi-cast approaches for data sharing are considered for JT over wireless links.
 | [26] | Impact of backhaul rate and discussion of in-channel vs. off-channel backhaul are provided. The backhaul rate needs to be much higher than RMU to avoid degradation of effective throughput.

## Slide 8: Multi-AP Coordination Revisited (6/6)
Topic | Ref | Key Contribution
MLO | [27] | Unified reference model to support both ML and MAP features is discussed. The authors propose grouping of AP MLD instances into forming an AP MLD group.
 | [28] | Expansion of multi-link to multi-AP for stability and the different between single-AP multi-link and multi-AP multi-link is highlighted. Authors argue that multi-AP provides a more stable link capacity. Moreover, in the multi-AP multi-link case the MAC entities on APs cannot be directly coordinated as in the single-AP multi-link case.

## Slide 9: Group Formation
Obtain characteristics of different links between STAs and APs
  Distance, SINR, RSRP, RSSI
Depending upon the obtained characteristics, determine candidate APs for coordination
  Per-user based, network-based
Verify if the selected APs can fulfil the coordination requirement
  Min SINR, Rx Power, etc.
If yes, this is the coordination group/cluster
Receive channel characteristic(s)
Determine candidate group(s)
Coordination requirement met?
Select group(s)
Control coordinated communication
NoO
Yes

## Slide 10: Coordination Scheme Selection
Check user requirements
  AC or UP information can be used
Obtain characteristics of different links between STAs and APs
  Distance, SINR, RSRP, RSSI
Evaluate performance of coordination scheme
Check feasibility
  Backhaul bandwidth, latency, etc.
If satisfied, proceed with coordinated transmission
Check STA requirments (throughout, latency, jitter...)
Check link quality between different APs and STAs
Evaluate performance of coordination scheme(s)
User requirements met?
Check feasibility of coordination scheme
Proceed with coordinated transmission

## Slide 11: Multi-link Operation
Multi-link and/or multi-band operation
  2.4, 5 and 6 GHz bands may be used simultaneously by some devices.
  Potential difference in coverage areas for multi-band operation.
  For MLDs, it might be challenging to coordinate over multiple bands
    Backhaul usage for different bands/links

## Slide 12: Multi-link Operation
Multi-link (Information) Element [29]
  Advertising multi-link capabilities and information of other STA(s) of MLD
  Can be used in the context of discovery
  Can be included in the probe response frame
  Can be used for (re)association response frame
  A STA of an MLD may provide complete or partial information of another STA of its MLD in the per-STA profile sub-element of the Multi-Link element that it transmits
  An AP of an AP MLD shall include complete profile of another AP of its MLD in its (re)association response frame
  A STA of a non-AP MLD shall include complete profile of another STA of its MLD in its (re)association request frame

## Slide 13: Multi-link Operation
Multi-AP (Information) Element?
  How to advertise the multi-AP capabilities of different APs?
    An information element similar to ML element?
    Can ML element carry this additional information?
      Unnecessary overhead for MLDs that are not coordinating?

## Slide 14: Straw Poll # 1
Should the group formation process and its underlying steps be defined in the standard or left to implementation?
Yes
No
Abstain

## Slide 15: Straw Poll # 2
Should the coordination scheme selection process and its underlying steps be defined in the standard or left to implementation?
Yes
No
Abstain

## Slide 16: Straw Poll # 3
Which of the following should be considered for advertising/sharing the coordination capabilities of APs:
Modifying multi-link element to contain the multi-AP coordination capabilities?
Designing a different information element/container to advertise coordination capabilities?
Something else

## Slide 17: References
Multi-AP Operation - Basic Definition, IEEE 802.11-20/0617r3
Setup for Multi-AP coordination, IEEE 802.11-19/1895r2
Multi-AP Transmission procedure, IEEE 802.11-19/1652r1
A Unified Transmission Procedure for Multi-AP Coordination, IEEE 802.11-19/1102r0
Multi-AP Transmission Procedure, IEEE 802.11-19/0804r0
Consideration on Multi-AP Coordination, IEEE 802.11-19/1129r2
Efficient Operation for Multi-AP Coordination, IEEE 802.11-19/1143r3
Overview of Multi-AP Operation in 11be, IEEE 802.11-20/0064r1
Operation of Virtual BSS Architecture for Multi-AP Coordination, IEEE 802.11-19/1972r1
Virtual BSS for Multi-AP Coordination Follow-Up, IEEE 802.11-19/
Channel Sounding for Multi-AP CBF, IEEE 802.11-20/123r2

## Slide 18: References
Multi-AP Sounding Discussion, IEEE 802.11-20/0052r0
Multi-AP Sounding Discussion Follow Up, IEEE 802.11-20/0502r0
Multi-AP Implicit Channel Sounding, IEEE 802.11-20/0089r1
Joint Sounding for Multi-AP Systems, IEEE 802.11-19/1593r3
One Channel Information Feedback Method for Multi-AP Coordination, IEEE 802.11-19/1573r0
Consideration of Multi-AP Sounding, IEEE 802.11-19/1134r1
Multi-AP Group Establishment, IEEE 802.11-19/1961r4
Multi-AP Group Formation, IEEE 802.11-19/1616r1
AP Candidate Set Follow Up, IEEE 802.11-20/0596r1
Multi-AP Group Formation Follow-up, IEEE 802.11-19/1931r2
Multi-AP Coordination for Spatial Reuse, IEEE 802.11-20/0107r1

## Slide 19: References
Multi-AP Collaborative BF in IEEE 802.11, IEEE 802.11-19/0772r1
Simulation Results for Coordinated OFDMA in Multi-AP Operation, IEEE 802.11-19-1592r0
Data Sharing for Multi-AP Coordination, IEEE 802.11-19/1554r1
Multi-AP Backhaul Analysis, IEEE 802.11-19/1588r0
Multi-link and Multi-AP Reference Model Discussion, IEEE 802.11-20/0068r0
Discussion on Expansion of Multi-Link Aggregation to Multi-AP, IEEE 802.11-20/0035r0
Amendment 8: Enhancements for Extremely High Throughput (EHT), IEEE P802.11beTM/D0.1