## Slide 1: 802.11bd NGV Ranging Status and Types
Date: 2020-11-03
Authors:

## Slide 2: Abstract
We review contributions on ranging for 802.11bd NGV and summarize the different ranging types. This leads to straw polls asking:
What preferences does the group have on the different ranging types?

## Slide 3: 802.11bd NGV Documents Addressing Ranging
PAR/FRD [1], [2]: “amendment defines procedures for at least one form of positioning in conjunction with V2X communications”
UC Doc [3]: UC5 Vehicular Positioning & Location, UC8 Train-to-Train, UC9 Vehicle-to-Train
SFD [4]: “11bd supports round-trip-time (RTT) ranging for 10 MHz and 20 MHz bandwidth PPDUs.”
Draft 0.4: “An NGV PHY shall support the following features:
  Round trip time (RTT) based ranging using 10 and 20 MHz bandwidth PPDUs”

## Slide 4: 802.11bd NGV Contributions Addressing Ranging
Positioning Use Cases for NGV [5]
NGV Ranging Discussions [6]: FTM, NTB, TB, and passive TB ranging
Ranging Performance in 11bd [7] : Performance results NTB ranging
Considerations on Ranging in NGV [8]: Performance results one-way TOF & RTT ranging, 60 GHz
On ranging methods for NGV [9]: First comparison one-way TOF, two-way RTT, FTM EDCA, and NTB ranging
Ranging Protocol in 11bd [10]: Ranging advertisement & NTB ranging
Influence of Delay-Close Multi Path Components on FTM-RTT [11]: Performance results RTT ranging

## Slide 5
Ranging type | One-Way TOF [8,9] | Two-way RTT [8,9,11] | FTM EDCA [6,9,11] | NTB [6,7, 9,10] | Passive TOF/RTT/ FTM EDCA /NTB | TB [6] | Passive TB [6]
Standard | - | - | 802.11-2016 | 802.11az | - | 802.11az | 802.11az
Challenges | accurate absolute timing at each STA; TOD (sub ns accuracy) & TX location included in measurement frame | TODs (sub ns accuracy) & TX location included in measurement frame and/or fixed timing for reply ACK | high channel load (≥ 6 frames), 30 ms  100 ms position (no parallel ex-change) | 1 request + ACK frame, 5 frames in one TXOP, 0.6 ms,  2 ms position | additional measurement reports depending on ranging type | 9-11 frames in one TXOP, AP based, spatial streams UL and DL, not OCB | 15 frames in one TXOP, based on TB
Transmitted frames | 1 | 2 | ≥ 6 | 6-7 | 1-2 add. meas. report | 9-11 | ≥ 15
Security/ Privacy | - | - | - | optionally | depending on type | optionally | No
11bd Changes | strict timing synchronization, TOD in measure-ment frame | TOD in measurement frame, exchange in one TXOP | None, optional: reduce frames, parallel ranging ex-change | NDPA/NDP frame using NGV PPDU | depending on type | adaptation to OCB | Only with TB, adaptation to OCB

## Slide 6
Ranging type | One-Way TOF [8,9] | Two-way RTT [8,9,11] | FTM EDCA [6,9,11] | NTB [6,7, 9,10] | Passive two-way RTT/ FTM EDCA /NTB | TB [6] | Passive TB [6]
Standard | - | - | 802.11-2016 | 802.11az | - | 802.11az | 802.11az
Challenges | accurate absolute timing at each STA; TOD (sub ns accuracy) & TX location included in measurement frame | TODs (sub ns accuracy) & TX location included in measurement frame and/or fixed timing for reply ACK | high channel load (≥ 6 frames), 30 ms  100 ms position (no parallel ex-change) | 1 request + ACK frame, 5 frames in one TXOP, 0.6 ms,  2 ms position | additional measurement reports depending on ranging type | 9-11 frames in one TXOP, AP based, spatial streams UL and DL, not OCB | 15 frames in one TXOP, based on TB
Transmitted frames | 1 | 2 | ≥ 6 | 6-7 | 1-2 add. meas. report | 9-11 | ≥ 15
Security/ Privacy | - | - | - | optionally | depending on type | optionally | No
11bd Changes | strict timing synchronization, TOD in measure-ment frame | TOD in measurement frame, exchange in one TXOP | None, optional: reduce frames, parallel ranging ex-change | NDPA/NDP frame using NGV PPDU | depending on type | adaptation to OCB | Only with TB, adaptation to OCB
Not feasible time sync
OCB requires significant rework

## Slide 7
Ranging type | One-Way TOF [8,9] | Two-way RTT [8,9,11] | FTM EDCA [6,9,11] | NTB [6,7, 9,10] | Passive FTM EDCA /NTB | TB [6] | Passive TB [6]
Standard | - | - | 802.11-2016 | 802.11az | - | 802.11az | 802.11az
Challenges | accurate absolute timing at each STA; TOD (sub ns accuracy) & TX location included in measurement frame | TODs (sub ns accuracy) & TX location included in measurement frame and/or fixed timing for reply ACK | high channel load (≥ 6 frames), 30 ms  100 ms position (no parallel ex-change) | 1 request + ACK frame, 5 frames in one TXOP, 0.6 ms,  2 ms position | additional measurement reports depending on ranging type | 9-11 frames in one TXOP, AP based, spatial streams UL and DL, not OCB | 15 frames in one TXOP, based on TB
Transmitted frames | 1 | 2 | ≥ 6 | 6-7 | 1-2 add. meas. report | 9-11 | ≥ 15
Security/ Privacy | - | - | - | optionally | depending on type | optionally | No
11bd Changes | strict timing synchronization, TOD in measure-ment frame | TOD in measurement frame, exchange in one TXOP | None, optional: reduce frames, parallel ranging ex-change | NDPA/NDP frame using NGV PPDU | depending on type | adaptation to OCB | Only with TB, adaptation to OCB
Not feasible time sync
OCB requires significant rework
Feasibility not tested

## Slide 8
Ranging type |  |  | FTM EDCA [6,9,11] | NTB [6,7, 9,10] |  |  | 
Standard |  |  | 802.11-2016 | 802.11az |  |  | 
Challenges |  |  | high channel load (≥ 6 frames), 30 ms  100 ms position (no parallel ex-change) | 1 request + ACK frame, 5 frames in one TXOP, 0.6 ms,  2 ms position |  |  | 
Transmitted frames |  |  | ≥ 6 | 6-7 |  |  | 
Security/ Privacy |  |  | - | optionally |  |  | 
11bd Changes |  |  | None, optional: reduce frames, parallel ranging ex-change | NDPA/NDP frame using NGV PPDU |  |  | 
Highly dynamic V2X environment: latency critical
High channel load: DCC may delay next TXOP by 1 second [12]
 NTB measurement exchange including LMRs in one TXOP only 0.6 ms  Low latency
Highly dynamic V2X environment: latency critical
High channel load: DCC may delay next TXOP by 1 second [12]
FTM EDCA: 3 separate frames with ACKs  FTM measurement exchange including LMRs several seconds
 High latency
Support for authentication, integrity check, and privacy of ranging message

## Slide 9: Passive Ranging
11az defines passive TB ranging:
Relative range (TDOA) of arbitrary number of passive STAs (PSTAs)
No additional measurement exchanges needed
In addition to LMR reports two RSTA broadcast passive TB ranging measurement report frames
 Scalability

## Slide 10: Passive Ranging Proposal
Passive NTB ranging:
Relative range (TDOA) of arbitrary number of passive STAs (PSTAs)
No additional measurement exchanges needed
In addition to LMR reports two report frames e.g.
  LCI or
  R/ISTA broadcast passive ranging measurement
 Scalability
NDP Announcement

## Slide 11: Multi-channel 11az Ranging [13]
Leveraging higher layer (1609/ITS-G5) multi-channel operation
Capability discovery handled via higher layer mechanisms through 11bd
Flexible and low-overhead application of 11az in 11bd and OCB mode
Ranging can occur through multi-channel operation
  inside 5.9 GHz ITS band:  NTB ranging (NGV NDP/NDPA and LMR frames)  802.11 security using 11az pre-association security negotiation (PASN)
  outside 5.9 GHz ITS band  Enables use of higher BW channels for higher accuracy ranging where applicable  Use of 11az PHY security and different 11az ranging options possible
Minimal changes/spec work required in 11bd

## Slide 12: Mandatory vs. Optional Ranging Types
Optional ranging types
  Need for advertisement and negotiation
  Higher flexibility for different applications
Mandatory ranging type(s)
  All NGV devices possible I/RSTA
  No need for advertisement and negotiation  E.g. NTB ranging advertisement unnecessary
  Mandatory capture of accurate TOA/TOD of frames  E.g. FTM EDCA Ranging FTM Request unnecessary
 Faster ranging and positioning

## Slide 13: Conclusions
11bd NGV ranging: Two out of five ranging types plus passive methods
  One-way TOF: time synchronization and fast time stamp
  Two-way RTT: fast time stamp and fixed timing for ACK (processing time)
  FTM EDCA: easily adapted for 11bd, 3 separate frames + ACK  high latency
  NTB: define additional frames, one TXOP measurement exchange and reporting  low latency
  Passive NTB(/FTM EDCA): In addition to LMR reports two LCI reports  scalability
  TB and passive TB: Significant changes to work OCB
  Multi-channel 11az ranging: 11bd STAs negotiate 11az ranging outside 5.9 GHz band
Mandatory vs. optional ranging type(s):
  Flexibility
  Reduced channel use
  Faster ranging and positioning

## Slide 14: References
[1] Project Authorization Request (PAR) 11-18-0861r9
[2] TGbd Functional Requirements Document (FRD) 11-19-0495r3
[3] TGbd Use Case Document 11-19-1342r1
[4] TGbd Spec Framework Document (SFD) 11-19-11-19-0497r7
[5] Location use cases for NGV 11-18-1221r0
[6] NGV ranging discussion 11-18-1250r0
[7] Ranging Performance in 11bd 11-19-0859r0
[8] Considerations on Ranging in NGV 11-19-0788r3
[9] On ranging methods for NGV 11-19-1892r0
[10] Ranging Protocol in 11bd 11-19-2011r0
[11] Influence of Delay-close Multi Path Components on FTM-RTT 11-19-1929r1
[12] ETSI EN 302 571 V2.1.1 (2017-02), ITS; Radiocommunications equipment operating in the 5 855 MHz to 5 925 MHz frequency band
[13] Ranging in 11bd 11-20/1761r2

## Slide 15: SP #1
Do you agree to add in the SFD “11bd supports distance measurement using NTB ranging for 10 MHz and 20 MHz bandwidth PPDUs in the 5.9 GHz band. This feature is optional.“
Yes/No/Abstain/No Vote: 21/0/5/26
Motion passe by unanimous consent
Yes/No/Abstain/No Vote: ///

## Slide 16: SP #2
Do you agree to add to the SFD
“11bd supports hyperbolic positioning using differential time of arrival for 10 MHz and 20 MHz bandwidth PPDUs in the 5.9 GHz band. This feature is optional.”
Yes/No/Abstain:

## Slide 17: SP #3
Do you agree to add to the SFD
“11bd supports negotiation of ranging features using higher layer mechanisms.”
Yes/No/Abstain: