## Slide 1: PDT-TBD-EMLSR mode operation
Date: 2020-11-30
Authors:

## Slide 2: Introduction
In 802.11be D0.1, the following details of the EMLSR mode operation were not decided and left as TBDs:
  Indication of the limitations of the initial Control frame of a frame exchange sequence
    “The initial Control frame of a frame exchange sequence may have one or more limitations for the following parameters: the number of spatial streams, MCS(s) (or data rate(s) for non-HT PPDU), PPDU type(s), and frame type(s).”
  Link switch delay signaling and values
    “The non-AP MLD may indicate its link switch delay in a TBD management frame”
In this presentation, we propose details for the TBDs in Subclause 35.3.13 Enhanced multi-link single radio operation of 802.11be Draft 0.1

## Slide 3: Indication of the limitations of the initial Control frame
Discussions during the D0.1 PDT writing
  For a simple implementation and clear operation of the EMLSR mode, instead of each non-AP MLD indicating the limitations to an AP MLD, it is better to have a set of limitations defined in the spec
  Link switch delay should be considered and frames that can accommodate MAC padding should be used
Proposed set of limitations for the initial Control frame
Parameters | Limitations
Number of spatial streams | 1
PPDU type | OFDM PPDU Non-HT or non-HT duplicate PPDU
Data rate | 6, 12, 24 Mbps
Frame type | MU-RTS and BSRP Trigger frames (Note 1: mandatory or optional support for the non-AP MLD of reception of MU-RTS and BSRP Trigger frames is TBD) (Note 2: optional support for the non-AP MLD of reception of Basic Trigger frame is TBD)

## Slide 4: Link switch delay signaling and values
The Padding field in a Trigger frame can be used to add the additional time needed by the non-AP MLD to operate in the EMLSR mode
We propose to define a field (EMLSR Delay field) in a TBD (MLD-level) element
  The field indicates the MAC padding duration of the Padding field for the initial Control frame for the additional time needed by the non-AP MLD when operating in the EMLSR mode
The EMLSR Delay field is 3 bits and encoded as follows
  0: 0 usec
  1: 32 usec
  2: 64 usec
  3: 128 usec
  4: 256 usec
  5-7: reserved

## Slide 5: Comment/resolution 1
Comment 1: non-HT PPDU includes not only Clause 17 but also Clause 15, 16, and 18 PHYs. Is this the intention?
Response 1: The intention was to support the OFDM PPDU defined in Clause 17. Suggested change is to replace the non-HT PPDU with the OFDM PPDU. Non-HT duplicate PPDU doesn’t have this issue. Please see below definitions in 802.11md D5.0.
Definitions in 802.11md D5.0:
  non-high-throughput (non-HT) physical layer (PHY) protocol data unit (PPDU): A PPDU that is transmitted by (#1455)a Clause 15 (DSSS PHY specification for the 2.4 GHz band designated for ISM applications), Clause 16 (High rate direct sequence spread spectrum (HR/DSSS) PHY specification), Clause 17 (Orthogonal frequency division multiplexing (OFDM) PHY specification), or Clause 18 (Extended Rate PHY (ERP) specification) PHY, or not using a TXVECTOR FORMAT parameter equal to HT_MF, HT_GF or VHT.
  non-high-throughput (non-HT) duplicate physical layer (PHY) protocol data unit (PPDU): A PPDU transmitted by a Clause 19 (High-throughput (HT) PHY specification) or Clause 21 (Very high throughput (VHT) PHY specification) PHY with the TXVECTOR FORMAT parameter equal to NON_HT and the CH_BANDWIDTH parameter equal to NON_HT_CBW40, CBW40, CBW80, CBW160, or CBW80+80.
  orthogonal frequency division multiplexing (OFDM) physical layer (PHY) protocol data unit (PPDU): A Clause 17 (Orthogonal frequency division multiplexing (OFDM) PHY specification) PPDU.

## Slide 6: Comment/resolution 2
Comment 2: Shouldn’t the rate be one of the rates in the BSSBasicRate parameter?
Response 2: The baseline standard (802.11md D5.0) already defines the rate selection rules for Control frames as shown below and doesn’t need to duplicate the same behavior in the eMLSR operation.
Definitions in 802.11md D5.0:
  “10.6.6.2 Rate selection for Control frames that initiate a TXOP … If a Control frame is(#57) carried in a non-HT PPDU, the transmitting STA shall transmit the frame using one of the rates in the BSSBasicRateSet parameter or a rate from the mandatory rate set of the attached PHY if the BSSBasicRateSet is empty(#57).”

## Slide 7: Proposed changes to the draft text in 35.3.13 Enhanced multi-link single radio operation of 802.11be Draft 0.1
TGbe editor: make the following changes to the paragraph in P104L6 of subclause 35.3.13 Enhanced multi-link single-radio in 802.11be Draft 0.1:
35.3.13 Enhanced multi-link single radio operation
…
When a non-AP MLD is operating in the EMLSR mode with an AP MLD supporting the EMLSR mode the following applies:
— The non-AP MLD shall be able to listen on the enabled links, by having its affiliated STA(s) corresponding to those links in the awake state. The listening operation includes CCA and receiving the initial Control frame of a frame exchange sequence that is initiated by an AP MLD.
— The initial Control frame of a frame exchange sequence shall be sent in the OFDM PPDUnon-HT or non-HT duplicate PPDU format using a rate of 6 Mbps, 12 Mbps, or 24 Mbps.
— The initial Control frame shall be an MU-RTS Trigger frame or a BSRP Trigger frame. (Note 1: mandatory or optional support for the non-AP MLD of reception of MU-RTS and BSRP Trigger frames is TBD) (Note 2: optional support for the non-AP MLD of reception of Basic Trigger frame is TBD) may have one or more limitations for the following parameters: the number of spatial streams, MCS(s) (or data rate(s) for non-HT PPDU), PPDU type(s), and frame type(s).
— The non-AP MLD may indicate the delay time needed by the non-AP MLD in the EMLSR Delay field in the TBD element, which is the MLD level capabilities element. its link switch delay in a TBD management frame. The value in the EMLSR Delay field indicates the MAC padding duration of the Padding field of the initial Control frame. The EMLSR Delay field is 3 bits and set to 0 for 0 µsec, set to 1 for 32 µsec, set to 2 for 64 µsec, set to 3 for 128 µsec, set to 4 for 256 µsec, and the values 5 to 7 are reserved.

## Slide 8: Straw Poll 1
Do you support the text changes proposed in Slide 7 of this presentation [11-20/1743r2] for the next revision of 802.11be draft?