## Slide 1: Proxy ARP Service in MLO
Date: 2020-10-28
Authors:

## Slide 2: Recap: Proxy ARP Service
When the AP sets the Proxy ARP field to 1 in the Extended Capabilities element, the AP shall maintain a Hardware Address to Internet Address mapping for each associated station, and shall update the mapping when the Internet Address of the associated station changes.
When the IPv4 address being resolved in the ARP request (IETF RFC 826) is used by a non-AP STA currently associated to the BSS, the proxy ARP service shall respond on behalf of the STA to an ARP request or an ARP probe (IETF RFC 5227).

## Slide 3: Recap: Proxy ARP Service
When an AP receives an ARP request from one associated STA or from the DS with a Target IP Address that corresponds to a second associated STA, the AP shall insert the second STA MAC address as the Sender’s MAC Address in the ARP response packet.
When an IPv6 address is being resolved, the Proxy ARP service shall respond with a Neighbor Advertisement message (Section 4.4, IETF RFC 4861) on behalf of an associated STA to an Internet Control Message Protocol version 6 (ICMPv6) Neighbor Solicitation message (Section 4.3, IETF RFC 4861). When MAC address mappings change, the AP may send unsolicited Neighbor Advertisement Messages on behalf of a STA.

## Slide 4: Proxy ARP Service on MLO
When an AP MLD sets the Proxy ARP field to 1 in the Extended Capabilities element, the AP MLD shall maintain a MLD MAC Address to Internet Address mapping for each associated non-AP MLD, and shall update the mapping when the Internet Address of the associated non-AP MLD changes.

## Slide 5: Proxy ARP Service on MLO
When the IPv4 address being resolved in the ARP request is used by a non-AP STA MLD currently associated to the BSS, the proxy ARP service shall respond on behalf of the non-AP MLD to an ARP request or an ARP probe.
When an AP in an AP MLD receives an ARP request from one associated STA or from the DS with a Target IP Address that corresponds to a second associated non-AP MLD, the AP shall insert the MLD MAC Address of the second non-AP MLD as the Sender’s MAC Address in the ARP response packet.

## Slide 6: Proxy ARP Service on MLO
When an IPv6 address is being resolved, the Proxy ARP service shall respond with a Neighbor Advertisement message on behalf of an associated non-AP MLD to a Neighbor Solicitation message. In which case an AP shall insert the MLD MAC Address of the associated non-AP MLD as the sender’s MAC address in the Neighbor Advertisement packet.
When the Internet Address of the associated non-AP MLD changes, the AP may send unsolicited Neighbor Advertisement Messages on behalf of a non-AP STA MLD.

## Slide 7: Straw Poll 1
Do you support the following proxy ARP service in MLO?
  When an AP MLD sets the Proxy ARP field to 1 in the Extended Capabilities element, the AP MLD shall maintain a MLD MAC Address to Internet Address mapping for each associated non-AP MLD, and shall update the mapping when the Internet Address of the associated non-AP MLD changes.
  When an AP in an AP MLD receives an ARP request from one associated STA or from the DS with a Target IP Address that corresponds to a second associated non-AP MLD, the AP shall insert the MLD MAC Address of the second non-AP MLD as the Sender’s MAC Address in the ARP response packet.
  When an IPv6 address is being resolved, the Proxy ARP service shall respond with a Neighbor Advertisement message on behalf of an associated non-AP MLD to a Neighbor Solicitation message. In which case an AP shall insert the MLD MAC Address of the associated non-AP MLD as the sender’s MAC address in the Neighbor Advertisement packet.