## Slide 1: Passive TB Ranging TOA Timestamp Bit Savings
Date: Nov 3, 2020
Authors:

## Slide 2: Issue with current Passive TB Ranging time-stamp reporting
Passive TB Ranging broadcasting large number of 48 bit timestamps occupying many OFDM symbols.
Mainly this is an issue with the TOA timestamps as they are more numerous due to the ISTA cross-reporting.

## Slide 3: Passive TB Ranging Timestamps
Max time we need to cover is, say, 5 ms.
However, may want to keep track of timestamps from availability window to availability window, that may be separated by, say 1s.
Solution:
  Keep 48 bits - 1ps, representation of TOD timestamps covering 218 seconds
  Use 32 bits - 16 ps, representation of more numerous TOA timestamps, covering 69 ms.
RSTA
ISTA
t2
t1
t4
t3
R2I NDP
I2R NDP
PSTA
t5
t6
Max, say. 5 ms
Max, say, 5 ms

## Slide 4
Example Passive TB Ranging AP RSTAs and Client Anchor ISTAs Deployment
AP RSTA
Client Anchor ISTA
When an AP runs its Passive TB Ranging, all 21 ISTAs and 1 RSTA exchange NDPs.
=> 903 TOA OR 1785 TOA+PSTOA timestamps to report!!!,
Example NDP exchanges

## Slide 5: Timestamp Reporting Overheads
N_ISTA | BW [MHz] | N_bits | Total preambles length [ms] | Timestamp reporting overhead [ms] | Overhead over preambles
21 | 40 | 48 | 3.1 | 1.99 | 63%
21 | 40 | 32 | 3.1 | 1.36 | 43%
21 | 40 | 24 | 3.1 | 1.04 | 33%
21 | 40 | 16 | 3.1 | 0.73 | 23%
21 | 20 | 48 | 3.1 | 4.10 | 133%
21 | 20 | 32 | 3.1 | 2.84 | 90%
21 | 20 | 24 | 3.1 | 2.17 | 69%
21 | 20 | 16 | 3.1 | 1.51 | 48%
Approximate timestamp overhead in ms and percentage of the complete Passive TB Ranging exchange.
Parameters used:
Broadcast MCS - BPSK rate 1/2
Unicast MCS - 16QAM rate ¾
All ISTA report TOAs for the NDPs from all other ISTAs
For the percentage overhead, only the preambles and the SIFS for the frames in the sequence has been used as the base.

## Slide 6: Timestamp Reporting Overheads – w PSTOA
N_ISTA | BW [MHz] | N_bits | Total preambles length [ms] | Timestamp reporting overhead [ms] | Overhead over preambles
21 | 40 | 48 | 3.1 | 3.82 | 122%
21 | 40 | 32 | 3.1 | 2.56 | 83%
21 | 40 | 24 | 3.1 | 1.96 | 63%
21 | 40 | 16 | 3.1 | 1.33 | 43%
21 | 20 | 48 | 3.1 | 7.94 | 254%
21 | 20 | 32 | 3.1 | 5.36 | 171%
21 | 20 | 24 | 3.1 | 4.07 | 130%
21 | 20 | 16 | 3.1 | 2.78 | 88%
Approximate timestamp overhead in ms and percentage of the complete Passive TB Ranging exchange.
Parameters used:
PSTOA feedback
Broadcast MCS - BPSK rate 1/2
Unicast MCS - 16QAM rate ¾
All ISTA report TOAs for the NDPs from all other ISTAs
For the percentage overhead, only the preambles and the SIFS for the frames in the sequence has been used as the base.

## Slide 7: Strawpoll
How many bits in the Passive TB Ranging TOA timestamps do you support?
Option 1: 32 bits - Spanning 69 ms.
Option 2: 48 bits - Spanning 218 seconds.
Abstain

## Slide 8
Thank You!