## Slide 1: Ranging in 11bd
Date: 2020-11-6
Authors:
Name | Affiliation | Address | Phone | Email
Bahar Sadeghi | Intel Corp. |  | 503-803-2471 | Bahareh.sadeghi@intel.com
Qinghua Li |  |  |  | 
Jonathan Segev |  |  |  | 

## Slide 2: Background
11bd PAR [1]:
“This amendment defines procedures for at least one form of positioning in conjunction with V2X communications”
Use Case (UC) baseline document [2]:
  UC5 Vehicular Positioning & Location
  UC8 Train-to-Train
  UC9 Vehicle-to-Train
There have been multiple ranging contributions in TGbd [2][3][4][5][6][7]
  Various techniques have been studied [8]
  Ranging performance of C2C channel model and free-space LOS path loss model simulated/analyzed  sub-meter accuracy is possible
Draft 1.0:
  Optional feature: RTT based ranging using 10 and 20 MHz bandwidth PPDUs

## Slide 3: Abstract
This submission proposes ranging protocol for 11bd
  RTT based
  Reuse 11az ranging protocol
leveraging1609 multi-channel operation
  Flexible and low-overhead application of 11az in 11bd
  Ranging can occur in ITS band or other 802.11 bands
    Enables use of higher BW channels for higher accuracy ranging where applicable
  Use of 11az PHY security and different options possible
  Minimal changes/spec work required in 11bd

## Slide 4: 11az Ranging Overview
11az ranging includes three parts:
  Capability discovery
    During which a ranging responder advertises ranging capability in beacon (indicating whether it supports secured or non-secured, bi-directional measurement report feedback or not, trigger based or non-trigger based)
  Ranging parameter negotiation
    Initiator and responder use FTM request/response to negotiate number of spatial time streams, bandwidth, LTF format and location measurement report (LMR) feedback type, etc.
  Measurement sequence exchange
    Responder and Initiator exchange NDP frames and the location measurement report (LMR) using trigger-based sequence (MU scenario) or non-trigger based sequence (SU scenario) )
  Tear down
    May be implicit or explicit
11az defines ranging solution for both associated and non-associated STAs.
  11az un-associated solution applies better to 11bd

## Slide 5: 1609 Multi-Channel Operation
1609.4 specifies the multi-channel operation for 802.11p/bd
  A STA using “alternating mode” monitors the Control Channel (CCH) until a Service Advertisement is received for a Service Channel (SCH), or the device decides to utilize the SCH based on its announcements
To offer a service on a SCH, a service-provider STA transmits WAVE Service Advertisements (WSAs) on CCH
  Broadcast messages
A service-user STA receives the WSA and switches to the announced SCH to communicate with the provider STA
  Can be either unicast or multicast
Provider/user relationship
  Supports WSMP or IP packet
  Occurs only on SCH

## Slide 6: Multi-channel 11az Ranging in 11bd
RSTA
ISTA
Wave Service Advertisement frame(s)
CCH
Ranging Service Negotiation
11az capability discovery
SCH rendezvous
  May be a channel in 5.9 GHz band May be a channel outside 5.9 GHz band
  May be the same channel
5.9 GHz band
Switch to SCH
Switch to SCH
NTB ranging sequence
Non 5.9 GHz IEEE band
RSTA
ISTA
Option A
Option B
11az ranging sequence
RSTA
ISTA
Ranging Service measurement
11az Pre-association security negotiation (optional)
11az parameter negotiation
NTB measurement sequence
  No PHY security
11az termination (may be implicit)
Ranging Service measurement
11az PASN (optional)
11az parameter negotiation
11az measurements
  PHY security (optional)
11az termination (may be implicit)

## Slide 7: Benefits of multi-channel 11az ranging
11az defines the latest ranging solution for 802.11 including PHY security
Multi-channel adaptation of 11az for 11bd enables 11az features for OCB and more
  Capability discovery is handled via 1609.4 mechanisms
  Flexible channelization operation
    If non-ITS 802.11 channels available, higher BW can be used for higher ranging accuracy
    If limited to ITS channels, then 1609.4 multi-channel enables flexible and efficient operation
  Minimum changes required in 11bd specification
    NDP and 11az control frames definition for 11bd (similar to other signal formats already defined in 11bd) for ranging in ITS band

## Slide 8: 11bd spec work required (1/2)
Capability Discovery:
  Using higher layer messages
  Spec work: indication of possibility of this option.
    Parameters to be either fixed or negotiated at the end of the procedure TBD.
Unassociated security context establishment
  Can be skipped per higher layer exchanges i.e., capability/use case/policy
  Needs PMK to be provided by the higher layers.
    Can be provided as “ranging certificate” similar to how it is done for other use cases
  3 frame exchange:
    Use of 11az messages.
    Spec work: 11az PASN text updated for two non-AP STAs (12.13.3.2)
      5.9 GHz band: 11az Management frames carried in NGV PPDU format
      non-5.9 GHz band: no change

## Slide 9: 11bd spec work required (2/2)
11az parameter negotiation
  2 frames
  Spec work:
      5.9 GHz band: 11az frames carried in NGV PPDU format
      non-5.9 GHz band: no change
11az measurement sequence
  NTB in 5.9 GHz band
  All of 11az measurements sequence available on regular Wi-Fi bands
  Spec work: definition of
      NGV NDP: NGV PPDU – Data
      NGV NDPA: NGV PPDU version
      LMR: management frame carried in NGV PPDU format
Secure LTF
  Available as is on non-ITS bands. Not supported on ITS bands.
  Spec work: none

## Slide 10: References
[1] 11-18/0861r9 TGbd PAR
[2] 11-19/1342r1 TGbd Use Case Document
[3] 11-19/788r3 considerations on ranging in NGV
[4] 11-19/859r0 ranging performance in 11bd
[5] 11-19/1892r0 on ranging methods for NGV
[6] 11-19/2011r0 ranging protocols in 11bd
[7] 11-19/1929r1 influence of delay-close multi-path components on FTM-RTT
[8] 11-20/1728r0 802.11bd ranging status and types

## Slide 11: Backup

## Slide 12: Non-trigger Based Ranging Sequence
11az non-trigger based (NTB) measurement sequence with bidirectional LMR is shown below
  Applied to peer-to-peer ranging scenario (initiator and responder)
  The measurement sequence is initiated by initiator STA
  After measurement report exchange, both of initiator and responder obtain range estimation
NDPA
Initiator
Responder
SIFS
SIFS
NDP1
NDP2
LMR1
(t2, t3)
SIFS
LMR2
(t1, t4)
SIFS