## Slide 1: Reduced BlockAck
Date: 2020-11-04
Authors:
Name | Affiliations | Address | Phone | email
Shawn Sanghyun Kim | WILUS Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0524 | shawn.kim@wilusgroup.com
Greg Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Hanseul Hong |  |  |  | hanseul.hong@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 2: Introduction
802.11be supports 512/1024 BA in R1:
  To indicate the received status of up to 512 or 1024 MPDUs, length of the Block Ack Bitmap subfields in the Compressed BA and the M-BA are extended
    Compressed BlockAck and Multi-STA BlockAck frames may contain 64/128-octet Bitmap subfield(s)
The extended BlockAck Bitmap subfield may cause additional overhead
  Several contributions have provided analysis on the overhead from the 512/1024 BA and proposed methods for reducing the overhead
This contribution proposes Reduced BlockAck to reduce BA overhead
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 3: Motivation
Length of a Bitmap subfield is getting longer to indicate received status of more MPDUs through a BA frame
It is not desirable to increase a Bitmap size in proportion to the number of indicated MPDUs
  Increase in BA length may consume longer airtime, because MCS applied to BA may still be low
It is necessary to consider a new BA mechanism to indicate a larger number of MPDUs with a limited Bitmap size
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 4: Proposal: Reduced BlockAck (R-BA)
Each single bit in the Bitmap subfield of a Reduced BlockAck (R-BA) indicates the “Representative value” of the received status for multiple MPDUs
Method to determine “Representative value” for each single bit
  When all multiple MPDUs corresponding to a single bit were successfully received
    The single bit is determined as “1”
  When at least one MPDU corresponding to a single bit was failed to receive successfully
    The single bit is determined as “0”
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 5: R-BA Bitmap construction
Example
  When a single bit of the R-BA represents receiving status of 4 MPDUs
    NOTE: Each bit of the R-BA can be obtained by bitwise operation over the 4 bits in the scoreboard
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 6: Additional information in the Bitmap subfield
Per-MPDU Ack regarding the MPDUs corresponding to “0”-valued bits of R-BA can be added at the end of the Bitmap subfield
  The Per-MPDU Ack clarifies which MPDU(s) was failed to receive among the corresponding MPDUs.
A Bitmap subfield of the R-BA consists of two parts
  1st part (static bit-width)
    Reduced length of bitmap
    Bit-width is reduction ratio-dependent
  2nd part (variable bit-width)
    Additional Per-MPDU Ack bits
    Bit-width depends on the number of “0”-valued bits in the 1st part
    Additional padding bits can be present to align bitmap size to byte boundary
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 7: R-BA with the 2nd part
Example
  R-BA may convey 33-byte Bitmap subfield to indicate received status of 1024 MPDUs
    32 bytes R-BA + 4 bits per-MPDU Ack + 4 bits padding
Nov 2020
Sanghyun Kim (WILUS), et al.
Data
R-BA
Bitmap size = (256 + 8)-bit
EHT AP
EHT STA
1 | 1 | 0 | … | 1
1st part of the R-BA
(256 bits)
1 | 1 | 0 | 1
SSN to SSN + 4*(1) -1
“Per-MPDU Ack” for
SSN+4*(2) to SSN + 4*(3) -1
0 | 0 | 0 | 0
Padding
(to meet byte boundary)
“Representative value” for
SSN+4*(2) to SSN + 4*(3) -1
    1st part of the Bitmap subfield
      Reduction ratio: 4
        Each single bit in the 1st part of the Bitmap subfield indicates received status of 4 MPDUs
      The 1st part has a “0”-valued bit
2nd part of the R-BA
(8 bits)

## Slide 8: Implicit zero bits indication for R-BA
A BA may include many “0” bits in the Bitmap subfield [2]
  Difference between the Bitmap size and the number of MPDUs to be acknowledged makes “0”-valued bits in the Bitmap
    There are at least 224 “0”-valued bits in the 1024-bit Bitmap used to carry BA for 800 MPDUs
    The 224 “0”-valued bits are represented as 56 “0”-valued bits in the 1st part of the R-BA
      If the Reduction ratio 4 was applied
No need for additional information (per-MPDU Ack) that corresponds to the “0”-valued bits due to the difference in length
  When 2nd part of the Bitmap subfield has no additional bits for some “0”-valued bits in 1st part, an originator interprets that all the additional bits of the “0”-valued bits are “0” and omitted
Nov 2020
Sanghyun Kim (WILUS), et al.
1 | … | 0 | 0 | 1 | 0 | … | 0
256-bit R-BA
(BA bits regarding to 800 MPDUs)
1 | 1 | 0 | 1
0 | 1 | 1 | 0
Per-MPDU Ack info
corresponding to 0
Per-MPDU Ack info
corresponding to 0
0
0
0
0
…
56x4 bits are omitted
(“0”-valued bits)
56-bit
(“0”-valued bits to make 256-bit width)

## Slide 9: Signaling for the R-BA
Nov 2020
Sanghyun Kim (WILUS), et al.
Current BA frame formats (Compressed BA and Multi-STA BA) can be used for R-BA
  Replace Bitmap subfield in the current BA frame formats to Bitmap subfield of the R-BA
  Necessary information to interpret the Bitmap subfield can be carried using Reserved or redundant subfield in the current BA frame formats
    To interpret a Bitmap subfield of the R-BA correctly, an originator needs to know applied Reduction ratio (1st part) and length of the Bitmap subfield
      Example: Reduction ratio is 4 and length is 33(-octet) for the example in the slide 7
  Details are in the next slide

## Slide 10: R-BA in the Compressed BA frame format
Reduction ratio
  Indicated by reserved combination of the Fragment Number subfield
Length (of the Bitmap subfield)
  Indicated by the reserved subfield in the BA Control field
    If needed, we can use only a part of the reserved bits to keep some reserved bit(s)
Nov 2020
Sanghyun Kim (WILUS), et al.
Fragment Number subfield |  |  | Fragmentation Level 3 (ON/OFF) | Block Ack Bitmap subfield length (octets) | Maximum number of MPDUs/A-MPDUs that can be acknowledged | Reduction ratio
B3 | B2 B1 | B0 |  |  |  | 
0 | 0-3 | 0-1 | ON/OFF | 8, 32 or Reserved | 16, 64, 256 or Reserved | 1
1 | 0 | 0 | OFF | 64 | 512 | 1
1 | 1 | 0 |  | 128 | 1024 | 1
1 | 2 | 0 |  | 32+(a) | 512 | 2
1 | 3 | 0 |  | 32+(a) | 1024 | 4
1 | Any | 1 | ON | Reserved | Reserved | -
BA Ack Policy | BA Type | Reserved (Length indication in octet) | TID_INFO
Bits:
1
4
7
4
B0
B1 B4
B5 B11
B12 B15

## Slide 11: R-BA in the Multi-STA BA frame format
It is better to consider legacy compatible signaling method for the M-BA, because HE STA may try to parse the M-BA frame to find their AID
  Even if R-BA is applied, it is recommended to keep the length of the Bitmap subfield as 0/4/8/16/32 octets for each Per AID TID Info subfield
Bitmap subfield of the R-BA can be indicated using two consecutive Per AID TID Info subfields
  The first Per AID TID Info subfield conveys 1st part of the R-BA
  The second Per AID TID Info subfield with the same AID/TID pair conveys 2nd part of the R-BA, and Reduction ratio
    Starting Sequence Number (SSN) subfield of the second Per AID TID Info subfield is redundant, so it can indicate Reduction ratio
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 12: R-BA in the Multi-STA BA frame format (cont.)
Nov 2020
Sanghyun Kim (WILUS), et al.
Interpretation method
  Reduction ratio is indicated by the SSN subfield in the second Per AID TID Info subfield
  The length of the Bitmap subfield in the 1st and 2nd Per AID TID Info subfield are indicated by the Fragment Number subfields same as 11ax
    An HE STA can parse each Per AID TID Info subfield correctly (only pre-defined(in 11ax) Fragment Number subfield combinations are used)
AID TID Info | Block Ack Starting Sequence Control | 1st part of the R-BA (32-octet)
AID TID Info | Block Ack Starting Sequence Control | 2nd part of the R-BA (4-octet)
1st Per AID TID Info subfield
for an AID/TID pair
2nd Per AID TID Info subfield
for the AID/TID pair
Fragment Number (BA bitmap length = 32-octet) | Starting Sequence Number
Fragment Number (BA bitmap length = 4-octet) | Reduction ratio

## Slide 13: Summary
Reduced BlockAck (R-BA) to reduce BA overhead was proposed
It is proposed to reuse current BlockAck frame formats for the R-BA
Nov 2020
Sanghyun Kim (WILUS), et al.

## Slide 14: SP1
Nov 2020
Sanghyun Kim (WILUS), et al.
Do you agree that 11be shall define at least an overhead reduction mechanism for large size BA (e.g., 512/1024 BA) in R1?

## Slide 15: SP2
Nov 2020
Sanghyun Kim (WILUS), et al.
Do you support that a single bit in a Bitmap subfield can be used to indicate received status of multiple MPDUs?

## Slide 16: SP3
Nov 2020
Sanghyun Kim (WILUS), et al.
Do you agree to define Reduce BlockAck as the following:
  The Block Ack Bitmap subfield of the Reduced BlockAck is used to indicate received status of up to TBD entries, where each entry represent multiple number of MSDUs or A-MSDUs. The number of MSDUs or A-MSDUs corresponding to each entry is determined based on the Reduction ratio applied to the Bitmap subfield.
  Additional entries to indicate the received status of MSDUs or A-MSDUs corresponding to entries that have 0 value, can be presented after the entries corresponding to the multiple MSDUs or A-MSDUs.
    NOTE: TBD is 256 for R1.
      To indicate received status of 1024 MSDUs or 1024 A-MSDUs with Reduction ratio 4.

## Slide 17: References
[1] 11-20/201 Multi-Link BA compression (Girigh Madpuwar, Broadcom)
[2] 11-20/294 EHT Block ACK Optimization (Zhou Lan, Broadcom)
[3] 11-20/397 Sequence number and BA operation with larger BA buffer size (Liwen Chu, NXP)
[4] 11-20/441 Block Acknowledgment for EHT (Duncan Ho, Qualcomm)
[5] 11-20/462 11be BA Indication (Po-Kai Huang, Intel)
Nov 2020
Sanghyun Kim (WILUS), et al.