## Slide 1: Backward compatible EHT trigger frame follow up
Date: 2020-11-01
Authors:

## Slide 2: Background
We agree that the trigger frame in 802.1be shall be backward compatible
  The same Trigger frame can be used to solicit the TB PPDU from both the HE STA(s) and EHT STA(s)
  All the Per User Info fields in a Trigger frame other than MU-BAR Trigger shall have the same size.
  One unified RU allocation table (for both SU and MU) for the RU allocation field in the User Info field of the Trigger frame
  Some remaining issue are still TBD for the trigger frame
  HE/EHT indication, a signalling that indicates TB PPDU format
  UL BW extension
  RU allocation table and SS allocation in the user info field
In this contribution, we try to address the above remaining issues for backward compatible trigger frame

## Slide 3: Recap-HE trigger frame
HE trigger frame is shown as below
  Common Info field and a list of User Info fields

## Slide 4: Trigger frame
For the common part, it is easy for find the reserved bits by using the UL HE SIG-A reserved field or a special User Info field
However, User Info field needs careful design since there is only one clean reserved bit now
Subfield | HE Bits | EHT Bits Opt 2 [2] | EHT Bits Opt 1 [1] | EHT Bits Opt 1’ [1] and [3]
AID12 | 12 | 12 | 12 | 12
RU Allocation | 8 | 8 | 8 | 8
UL FEC Coding Type | 1 | 1 | 1 | 1
MCS | 4 | 4 | 4 | 4
DCM | 1 | 0 (Merges DCM with MCS) | 0 (Merges DCM with MCS) | 0 (Merges DCM with MCS)
SU/MU | 0 | 0 | 0 | 1(0)
SS Allocation | 6 | 6 (4+2, only 4 ss for SU) | 6 (4+2, only 4 ss for SU) | 6 (4+2 for MU-MIMO, 4 for SU)
UL Target RSSI | 7 | 7 | 7 | 7
HE/EHT Format |  | 1 | 0 (move to Common) | 0 (move to Common)
P/S160 MHz or L/H 160 MHz |  | 1 | 1 | 0 (by using a special user info)
Reserved | 1 | 0 | 1 | 1(2)

## Slide 5: UL BW
BW Expansion [3]
  This bit can be combined with the two-bit BW Field
  Possible bit mapping (on right)
However, the simple bw extension can not work
One example
  Simple extension can not cover the following solicited transmission
  80 MHz for HE TB PPDU, 80 MHz for EHT TB PPDU
BW Expansion (B59) | BW | Bandwidth
0 | 0 | 20 MHz
0 | 1 | 40 MHz
0 | 2 | 80 MHz
0 | 3 | 80+80 MHz or 160 MHz
1 | 0 | 320 MHz
1 | 1 | Reserved
1 | 2 | Reserved
1 | 3 | Reserved
Trigger frame
TB PPDU
Non-HT
Non-HT
Non-HT
Primary
80MHz
Secondary
80MHz
trigger
HE M-BA
EHT M-BA
L-P+RL
L-P+RL
L-P+RL
L-P+RL
L-P+RL
U-SIG
U-SIG
SIG-A
SIG-A
SIG-A
Non-HT
L-P+RL
SIG-A
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG

## Slide 6: UL BW
Another example
  Simple extension can not cover the following solicited transmission
  160 MHz for HE TB PPDU and 80 MHz for EHT TB PPDU
Trigger frame
TB PPDU
Non-HT
Non-HT
Non-HT
Primary
80MHz
Secondary
80MHz
trigger
HE M-BA
L-P+RL
L-P+RL
L-P+RL
SIG-A
SIG-A
SIG-A
Non-HT
L-P+RL
SIG-A
Non-HT
Non-HT
Non-HT
trigger
Non-HT
EHT M-BA
L-P+RL
L-P+RL
U-SIG
U-SIG
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
HE M-BA
L-P+RL
L-P+RL
L-P+RL
SIG-A
SIG-A
SIG-A
L-P+RL
SIG-A
Punctured 80MHz channel
Secondary
160MHz

## Slide 7: UL BW
Moreover, we agreed that we need differentiate 320-1 from 320-2 for BW in DL PPDU [4]
  To help spatial reuse (identify OBSS PPDU) and intra-PPDU power save
  For unassociated STA (random access or the third party STA), this info is also needed
To keep consistent with U-SIG in DL PPDU, 320-1/2 indication in the trigger frame is also needed
UNII5 |  |  |  |  |  | UNII6 | UNII6/7 | UNII7 |  |  | UNII7 /8 | UNII8 | 
80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80
160 |  | 160 |  | 160 |  | 160 |  | 160 |  | 160 |  | 160 | 
320-1 |  |  |  | 320-1 |  |  |  | 320-1 |  |  |  |  | 
 |  | 320-2 |  |  |  | 320-2 |  |  |  | 320-2 |  |  | 

## Slide 8: UL BW
Two possible UL BW extension indications
  The left figure needs 1 bit , but can not cover 320-1/320-2 and can not reflect the real BW of HE PPDU and EHT PPDU in some cases
  The right figure works well, but it needs two bits
  The other way is to have another BW field, it requires 3 bits
  No benefit compared with 2 bits UL BW extension but with more overhead
UL BW Extension (2 bits) | UL BW | Bandwidth for EHT TB PPDU , MHz | Bandwidth for HE TB PPDU, MHz
reserved | 0 | 20 | 20
reserved | 1 | 40 | 40
0 | 2 | 80 | 80
1 | 2 | 160 | 80
2 | 2 | 320 -1 | 80
3 | 2 | 320-2 | 80
0 | 3 | 80 | 160
1 | 3 | 160 | 160
2 | 3 | 320 -1 | 160
3 | 3 | 320-2 | 160
UL BW Extension (1 bit) | BW | Bandwidth for EHT TB PPDU, MHz | Bandwidth for HE TB PPDU, MHz
0 | 0 | 20 | 20
1 | 0 | 320 | 20
0 | 1 | 40 | 40
1 | 1 | 320 | 40
0 | 2 | 80 | 80
1 | 2 | 320 | 80
0 | 3 | 160 | 160
1 | 3 | 320 | 160

## Slide 9: HE/EHT indication
HE/EHT indication is used to indicate which TB PPDU format the EHT STA is solicited to transmit
There are two options
  Opt1: HE/EHT indication is in the Common part of the Trigger frame, that is per 80MHz segment [1]
  2 or 4 bits for HE/EHT indication. It has two bits if we limit to HE PPDU only on Primary 160 MHz
  Opt2: HE/EHT indication is in the User Info field of the Trigger frame [2]
  1 bit in each User Info field
For EHT STA | Opt 1 | Opt 2
Overhead | Small, only 2 or 4 bits | Large, depending on the number of user fields
Reserved bit | At least one clean reserved bit | No clean reserved bit (MSB of AID 12 field is debatable)
Extensible | Yes, it is easy to find bits in the common part | No, there exists extensible signaling issue if it is in User Info field with fixed length, i.e., no space to accommodate EHT/EHT+/EHT++ indication

## Slide 10: Update: HE/EHT indication and PHY Version
Since HE PPDU could only be transmitted in Primary 160 MHz based HE STA’s capability, that means
  EHT STA could send either HE TB PPDU or EHT TB PPDU in primary 160 MHz
  EHT STA could only send EHT TB PPDU in secondary 160 MHz
  Hence, HE/EHT indication could only applies to Primary 160MHz
  If the granularity is 80 MHz, then it requires 2 bits, may meets the issue of 160 MHz capable legacy device
  If the granularity is 160 MHz, then it requires 2 bits
  In R1, we focus on non A-PPDU, but the HE/EHT indication does not conflict this requirement. To guarantee non A-PPDU in r1，we have the following setting
  In R1, if an EHT AP solicits an EHT STA or HE STA to transmit HE TB PPDU, then HE/EHT is set to all 0
  In R1, if an EHT AP solicits an EHT STA to transmit EHT TB PPDU, then HE/EHT is set to all 1. And an EHT AP shall not solicit a HE STA in the same trigger frame

## Slide 11: Update: HE/EHT indication and PHY Version
In R2, we could have flexible HE/EHT indication setting to make A-PPDU
Moreover, HE/EHT indication also can function as enhanced trigger frame flag indication [2]
  In this way, the redundant info-enhanced trigger frame flag indication could be removed
PHY version in the trigger frame has overlapped function as HE /EHT indication and it is not needed
  Once one of them is known is by EHT STA, it could set the PHY version field in U-SIG of TB PPDU correctly
  PHY version just functions as 1 bit to EHT STA
  We only need the following fields in the common part now, about 3~8 bits
  UL BW extension field, 2 bits
  HE/EHT indication field： 1~2 bits
  Spatial Reuse field: 0 or 4 bits

## Slide 12: Summary
We propose a backward compatible trigger frame by adding the following fields
  HE/EHT indication per 80 MHz in the common part
  UL BW extension

## Slide 13: References
[1] 11-20-0840-03-00be-backward-compatible-eht-trigger-fram
[2] 11-20-1429-03-00be-enhanced-trigger-frame-for-eht-support
[3] 11-20-1669-02-00be-spatial-stream-allocation-in-trigger-frames
[4] 11-20-1467-00-00be-bw320-signaling

## Slide 14: SP 1
Do you agree to add the UL BW Extension field to the common part of the Trigger frame in R1?
  The UL BW Extension field and the UL BW field together indicate the bandwidth of the EHT TB PPDU solicited by the Trigger frame

## Slide 15: SP1A
Do you agree to include 320-1 MHz and 320-2 MHz for the EHT TB PPDU BW in the trigger frame

## Slide 16: SP 2
Do you agree to add the following UL BW Extension field to the common part of the Trigger frame in R1?
UL BW Extension (2 bits) | UL BW | Bandwidth for EHT PPDU, MHz | Bandwidth for HE TB PPDU, MHz
0 | 0 | 20 | 20
1 | 0 | reserved | 20
2 | 0 | reserved | 20
3 | 0 | reserved | 20
0 | 1 | 40 | 40
1 | 1 | reserved | 40
2 | 1 | reserved | 40
3 | 1 | reserved | 40
0 | 2 | 80 | 80
1 | 2 | 160 | 80
2 | 2 | 320 -1 | 80
3 | 2 | 320-2 | 80
0 | 3 | 80 | 160
1 | 3 | 160 | 160
2 | 3 | 320 -1 | 160
3 | 3 | 320-2 | 160

## Slide 17: SP 3
Do you agree to include a 2-bit (1-bit) HE/EHT indication where each bit corresponds to an 80 (160) MHz within primary 160 MHz in the common part of the Trigger frame, indicating to the EHT STA whether to transmit an HE or EHT TB PPDU in R1?
  It is TBD whether HE/EHT indication has 1 bit or 2 bits

## Slide 18: Appendix

## Slide 19: User Info field in trigger frame
The following subfields in the User Info field may be impacted by the new features in EHT
  RU allocation subfield
  SS allocation subfield
  However, there is only one reserved bit in User Info field. From the philosophy of design, it is better to keep it.
  We propose to have a special User Info field to divide the User Info fields into two categories
  Keep the existing 8-bit RU allocation subfield, and add MRU mode and large RUs to 7-bit table (refer to appendix)
  RU allocation subfield in the 1st part indicates a RU within or larger than primary160 MHz
  RU allocation subfield in the 2nd part indicates a RU within or larger than second 160 MHz
User Info 1
User Info 2
User Info X
…
User Info X+1
User Info X+2
User Info X+n
…
Special User Info
The first part, the assigned RU is within or larger than primary 160 MHz
The second part, the assigned RU is within or larger than secondary 160 MHz

## Slide 20: HE/EHT indication
Example for Opt 1
  An EHT AP sends non-HT duplicated trigger frame: two user info fields are for two EHT STAs, respectively. Both of these two User Info fields are EHT format
  HE/EHT=10 in the common part （ 1-HE 0-EHT）
  Case 1: If EHT STA is assigned to some certain RU in S80/second 80 MHz, then it is solicited to send EHT TB PPDU
  Case 2: If EHT STA is assigned to some certain RU in P80/first 80 MHz, then it is solicited to send HE TB PPDU
Non-HT
Non-HT
Non-HT
Primary
80MHz
Secondary
80MHz
trigger
HE M-BA
EHT M-BA
L-P+RL
L-P+RL
L-P+RL
L-P+RL
L-P+RL
U-SIG
U-SIG
SIG-A
SIG-A
SIG-A
Non-HT
L-P+RL
SIG-A
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
Trigger frame
TB PPDU-UL

## Slide 21: HE/EHT indication
Another example for Opt 1
  An EHT AP sends non-HT duplicated trigger frame: two user info fields are for two EHT STAs, respectively. One user info field is EHT format， the other one is HE format
  HE/EHT=10 in the common part （ 1-HE 0-EHT）
  Case 1: If EHT STA is assigned to some certain RU in S80, then it is solicited to send EHT TB PPDU
  Case 2: If EHT STA is assigned to some certain RU in P80, then it is solicited to send HE TB PPDU
Non-HT
Non-HT
Non-HT
Primary
80MHz
Secondary
80MHz
trigger
HE M-BA
EHT M-BA
L-P+RL
L-P+RL
L-P+RL
L-P+RL
L-P+RL
U-SIG
U-SIG
SIG-A
SIG-A
SIG-A
Non-HT
L-P+RL
SIG-A
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
Trigger frame
TB PPDU-UL