## Slide 1: Low-Latency Triggered TWT
Date: 2020-11-11
Authors:

## Slide 2: Abstract
Discuss a solution to support low-latency (LL) traffics and peer-to-peer (P2P) communications based on TWT feature.
Proposal :
  Define a Low Latency Service Period (LL SP) based on TB TWT dedicated to LL traffics (Slide 4)
  LL SP protection mechanisms (Slide 6 )

## Slide 3: Background
The TWT feature is a mechanism where a set of Service Periods (SPs) are defined and shared between AP and non-AP STAs to reduce medium contention and improve the power efficiency of STAs.
Broadcast TWT: AP can schedule TWT SP(s) with supporting STAs and shares schedule info in Beacon/Probe Response frames.
Doc11-20/1046: introduced protected TWT Enhancement mechanism for Latency Sensitive Traffic to:
  Enhance the channel access for restricted TWT SPs
  Extend the use of Broadcast TWT signaling
  Extend the usage of such TWT SPs
  for low latency P2P communications

## Slide 4: Low-Latency Service Period (LL SP) 1/2
Define a broadcast TWT dedicated to low-latency traffics
Define a new value for the « Broadcast TWT Recommendation» field value for Low-Latency traffics in the TWT Information Element
Restrict the TWT service period to only low-latency traffic transmission.
Support Direct link (P2P) communications (see doc 813r7):
TWT IE
Broadcast TWT Recommandation | Definition
0 | No constraints
1 | PS-Poll, QoS Null, BQR, BSRs frames
2 | PS-Poll, QoS Null, BQR, BSRs frames with TF containing RA-RUs
3 | No constraints on the frames except that the AP transmits a TIM frame
4 | Low Latency
5-7 | Reserved
Slide 4

## Slide 5: Low-Latency Service Period 2/2
Set « Trigger » field to 1
  Use trigger frame, during the broadcast TWT SP, avoids collision among STAs participating to the broadcast TWT.
    EDCA mode needs to be stabilized to be efficient. When the number of registered STAs increases, the collisions exponentially increase.
  Advantages :
    AP is the TxOp owner and controls the QoS.
The TF reserves a TXOP time greater than the Low Latency SP
  If the AP access the medium during a MaxProvisionTime (TBD) before the start of the LL SP, it reserves a TXOP time that encompasses the next LL SP.
  Advantages :
    This sets the NAV of non-scheduled STAs ( 11be and legacy, but also OBSS stations).

## Slide 6: LL SP protection
TXOPAP
LL SP
Reservation by the AP of the TXOPAP Duration
Transmission not restricted to Low Latency
Transmission restricted to Low Latency
Transmission not restricted to Low Latency
Transmission not restricted to Low Latency
TXOPSTA
TXOPSTA
ProvisionPeriod
MaxProvisionTime
Time
T1
T2
T3
T0
EDCA
SIFS
SIFS
STA with no LL traffic (including legacy and OBSS STAs)
STA with LL traffic
NAV duration

## Slide 7: LL SP Example
AP
STA1
STA2
(LL)
STA3
(LL)
STA4
TF
TF
TB PPDU
TB PPDU
SIFS
SIFS
SIFS
TXOPAP
LL SP
MSTA BA
SIFS
TB PPDU
TB PPDU
MSTA BA
UL_Length 1
UL_Length 2
SIFS
ProvisionPeriod
T1
T2
T3
T1bis
EDCA

## Slide 8: Summary
A new triggered LL SP is defined.
This ensures:
  The cancellation of collisions among STAs acting inside the LL SPs
  The AP keeps the control of the medium during all the LL SP
  The QoS is driven by the AP.
  This guarantees a more predictive access to the medium for low-latency traffics and peer-to-peer communications.

## Slide 9
Straw Poll #1
Do you support that 11be defines in R1 a broadcast TWT Service Period for low-latency flows ?
Results: Y/N/A

## Slide 10
Straw Poll #2
Do you support that a broadcast TWT for low-latency flows restricts the TWT service period to only low-latency traffic transmission.
Results: Y/N/A

## Slide 11
Straw Poll #3
Do you support that the broadcast TWT for low-latency flows :
  Is identified by adding a new value in the “Broadcast TWT Recommandation» field.
  Has the « Trigger » field set to 1 to restrict the medium access of the STAs during the broadcast TWT SP.
Results: Y/N/A

## Slide 12: Reference
[1]. 11-20-1046: Protected TWT Enhancement for Latency Sensitive Traffic.