## Slide 1: TGbf Motions List
Date: 2021-07-13
Author:
Name | Affiliation | Address | Phone | Email
Tony Xiao Han | Huawei Technologies Co., Ltd. | F3, Huawei Base, Shenzhen, China |  | Tony.hanxiao@huawei.com

## Slide 2: IEEE 802.11 Task Group bf WLAN Sensing
Motion list
Chair: Tony Xiao Han (Huawei)
Vice Chair: Sang Kim (LG Electronics)
Assaf Kasher (Qualcomm)
Secretary: Leif Wilhelmsson (Ericsson)
Technical Editor: Claudio Da Silva (Meta Platforms)

## Slide 3
Motions on November 3, 6, 9.

## Slide 4
Approve SENS SG and TGbf meeting minutes
Move to approve SENS SG and TGbf minutes of meetings and teleconferences from September 2020 meeting to today:
  September interim: https://mentor.ieee.org/802.11/dcn/20/11-20-1465-00-SENS-wlan-sensing-sg-september-2020-interim-meeting-minutes.docx
  Teleconferences September-October: https://mentor.ieee.org/802.11/dcn/20/11-20-1729-00-00bf-ieee-802-11bf-teleconference-meeting-minutes-september-and-october-2020.docx
Move: Claudio da Silva Second: Sang Kim
Result: Approved by unanimous consent
Notes: Approved by unanimous consent

## Slide 5
Motion 1 Timeline Motion
Move to adopt the following timeline for TGbf.
  PAR approved Sep, 2020
  First TG meeting Oct, 2020
  D0.1 Jan, 2022
  Initial Letter Ballot (D1.0) Jul, 2022
  Recirculation LB (D2.0) Jan, 2023
  Recirculation LB (D3.0) May, 2023
  Initial SA Ballot (D4.0) Sep 2023
  Final 802.11 WG approval July 2024
  802 EC approval July 2024
  RevCom and SASB approval Sep 2024
  Move: Oscar Au Second: Assaf Kasher
  Result: Approved by unanimous consent
  Note： Related document 20/1746r1

## Slide 6
Motion 2a
Move to confirm Sang Kim as TGbf Vice-Chair.
  Move: Oscar Au Second: Jinsoo Choi
  Result: Approved by unanimous consent

## Slide 7
Motion 2b
Move to confirm Assaf Kasher as TGbf Vice-Chair.
  Move: Oscar Au Second: Jinsoo Choi
  Result: Approved by unanimous consent

## Slide 8
Motion 3
Move to confirm Claudio Da Silva as TGbf Technical Editor.
  Move: Edward Au Second: Oscar Au
  Result: Approved by unanimous consent

## Slide 9
Motion 4
Move to confirm Leif Wilhelmsson as TGbf Secretary.
  Move: Oscar Au Second: Sang Kim
  Result: Approved by unanimous consent

## Slide 10
Motions on December 8.

## Slide 11
Motion 5
Move to adopt 11-20/1812r0 as the selection procedure document for TGbf.
  Move: Claudio Da Silva Second: Assaf Kasher
  Result: Approved by unanimous consent

## Slide 12
Motion 6
Move to adopt 11-20/1813r0 as the functional requirement document for TGbf. The Functional Requirements document may be modified at any time by a 75% approval vote.
  Move: Claudio Da Silva Second: Sang Kim
  Result: Approved by unanimous consent

## Slide 13
Motions on January 12, 13, 14.

## Slide 14
Approve TGbf meeting minutes
Move to approve TGbf minutes of meetings and teleconferences from November 2020 meeting to today:
  November plenary: https://mentor.ieee.org/802.11/dcn/20/11-20-1834-00-00bf-ieee-802-11bf-november-2020-plenary-meeting-minutes.docx
  Teleconferences November - January:
  https://mentor.ieee.org/802.11/dcn/20/11-20-1909-00-00bf-802-11bf-teleconference-minutes-november-2020.docx
  https://mentor.ieee.org/802.11/dcn/20/11-20-1955-01-00bf-802-11bf-teleconference-minutes-december-2020.docx
  https://mentor.ieee.org/802.11/dcn/21/11-21-0038-00-00bf-802-11bf-teleconference-minutes-january-2021.docx
Move: Leif Wilhelmsson Second: Claudio Da Silva
Result: Approved by unanimous consent

## Slide 15
Motion 7
Move to adopt 11-20/-1712r2 as the use cases document for TGbf.
  Move: Assaf Kasher Second: Rui Du
  Result: Approved by unanimous consent

## Slide 16
Motions on February 2.

## Slide 17
Motion 8
Move to add the following to 11bf SFD:
  A sensing procedure allows a STA to perform WLAN sensing and obtain measurement results. A sensing session is an instance of a sensing procedure with associated operational parameters of that instance.
  Move: Cheng Chen Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note： Related document 20/1849r4

## Slide 18
Motion 9
Move to add the following to 11bf SFD:
  Sensing initiator and sensing responder
    Sensing initiator: a STA that initiates a WLAN sensing session
    Sensing responder: a STA that participates in a WLAN sensing session initiated by a sensing initiator
  Sensing transmitter and sensing receiver
    Sensing transmitter: a STA that transmits PPDUs used for sensing measurements in a sensing session
    Sensing receiver: a STA that receives PPDUs sent by a sensing transmitter and performs sensing measurements in a sensing session
  A STA can assume multiple roles in one sensing session.
  Move: Cheng Chen Second: Edward Au
  Result: Approved by unanimous consent
  Note： Related document 20/1849r4

## Slide 19
Motions on February 23.

## Slide 20
Motion 10a
Move to add the following to 11bf SFD:
  A sensing initiator might be neither a sensing transmitter nor a sensing receiver.
  Move: Rui Du Second: Claudio da Silva
  Result:

## Slide 21
Motion 10b Motion to amend
Change the previous motion to:
Move to add the following to 11bf SFD:
  In a sensing session, a sensing initiator might be a sensing transmitter, a sensing receiver, both or neither.
  Move: Edward Au Second: Assaf Kasher
  Preliminary Result: Motion Passes (24Y, 4N, 1A)
  Result*: Motion Passes (21Y, 4N, 1A)
  Note：
  * Amended result accounts for removal of 3 votes of non-voting members.
  Related document 21/0147r3

## Slide 22
Motion 10c
Move to add the following to 11bf SFD:
  In a sensing session, a sensing initiator might be a sensing transmitter, a sensing receiver, both or neither.
  Move: Edward Au Second: Assaf Kasher
  Preliminary Result: Motion Passes (22Y, 0N, 4A)
  Result*: Motion Passes (21Y, 0N, 4A)
  Note：
  * Amended result accounts for removal of 1 votes of non-voting members.
  Related document 21/0147r3

## Slide 23
Motion 11
Move to add the following to 11bf SFD:
  Results of measurement performed in a sensing session should be obtained by or reported to its initiator.
  Move: Rui Du Second: Cheng Chen
  Preliminary Result: Motion Passes (21Y, 0N, 3A)
  Result*: Motion Passes (20Y, 0N, 2A)
  Note：
  * Amended result accounts for removal of 2 votes of non-voting members.
  Related document 21/0147r3

## Slide 24
Motion 12
Move to add the following to 11bf SFD:
  The 11bf amendment may define more than one type of sensing measurement results.
  Move: Rui Du Second: Oscar Au
  Result: Approved by unanimous consent
  Note： Related document 21/0147r3

## Slide 25
Motion 13
Move to add the following to 11bf SFD:
  The type of measurement result reported in a sensing session shall be decided by its initiator.
  Move: Rui Du Second: Assaf Kasher
  Preliminary Result: Motion Passes (20Y, 1N, 3A)
  Result*: Motion Passes (18Y, 1N, 2A)
  Note：
  * Amended result accounts for removal of 3 votes of non-voting members.
  Related document 21/0147r3

## Slide 26
Motions on March 9, 12, 15 (Plenary)

## Slide 27
Approve TGbf meeting minutes
Move to approve TGbf minutes of meetings and teleconferences from January 2021 meeting to today:
  January plenary: https://mentor.ieee.org/802.11/dcn/21/11-21-0120-01-00bf-meeting-minutes-january-2021.docx
  Teleconferences January - March:
  https://mentor.ieee.org/802.11/dcn/21/11-21-0227-01-00bf-802-11bf-teleconference-minutes-february-2021.docx
Move: Leif Wilhelmsson Second: Rui Yang
Result: Approved by unanimous consent
Notes: Approved by unanimous consent

## Slide 28
Motion 14
Move to add the following to 11bf SFD:
  A sensing session may be comprised of multiple burst instances.
  Move: Sang Kim Second: Cheng Chen
  Preliminary Result: Motion Passes (65Y/2N/14A)
  Result*: Motion Passes (58Y/2N/11A)
  Note：
  * Amended result accounts for removal of 10 votes of non-voting members.
  Related document 21/0145r4

## Slide 29
Motions on March 23.

## Slide 30
Motion 15
Move to add the following to 11bf SFD:
  A sensing session is composed of one or more of the following phases: setup phase, measurement phase, reporting phase, and termination phase.
    In the setup phase, a sensing session is established, and operational parameters associated with the sensing session are determined and may be exchanged between STAs.
    In the measurement phase, sensing measurements are performed.
    In the reporting phase, sensing measurement results are reported.
    In the termination phase, STAs stop performing measurements and terminate the sensing session.
  Move: Cheng Chen Second: Rajat Pushkarna
  Preliminary Result: Motion Passes (24Y/1N/5A)
  Result*: Motion Passes (21Y/1N/5A)
  Note：
  * Amended result accounts for removal of 3 votes of non-voting members.
  Related document 21/01851r4

## Slide 31
Motions on April 6.

## Slide 32
Motion 16
Move to add the following to 11bf SFD:
  More than one sensing responder may participate in the measurement phase and reporting phase.
  Move: Sang Kim Second: Rajat Pushkarna
  Preliminary Result: Motion Passes (35Y/0N/5A)
  Result*: Motion Passes (35Y/0N/4A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 21/0145r5

## Slide 33
Motion 17
Move to add the following to 11bf SFD:
  11bf shall define an optional negotiation process in the sensing setup phase for a sensing initiator and sensing responder(s) to exchange and agree on operational parameters associated with a sensing session.
  Move: Cheng Chen Second: Jinsoo Choi
  Result: Approved by unanimous consent
  Note： Related document 21/0370r1

## Slide 34
Motions on May 11, 14, 17 (Interim)

## Slide 35
Approve TGbf meeting minutes
Move to approve TGbf minutes of meetings and teleconferences from March 2021 meeting to today:
  March plenary: https://mentor.ieee.org/802.11/dcn/21/11-21-0476-00-00bf-meeting-minutes-march-2021.docx
  Teleconferences March - April:
  https://mentor.ieee.org/802.11/dcn/21/11-21-0547-00-00bf-802-11bf-teleconference-minutes-march-2021.docx
  https://mentor.ieee.org/802.11/dcn/21/11-21-0645-03-00bf-802-11bf-teleconference-minutes-april-2021.docx
Move: Leif Wilhelmsson Second: Claudio Da Silva
Result: Approved by unanimous consent
Notes: Approved by unanimous consent

## Slide 36
Motion 18
Move to add the following to 11bf SFD:
  The 11bf amendment defines an optional threshold based measurement and reporting procedure in which
  • The difference between the current measured CSI and the previous measured CSI is quantified. The difference is referred to as CSI variation.
  • A threshold value to be used by the sensing receiver in the threshold based procedure is defined.
  • By comparing the CSI variation with the threshold, the sensing receiver can send a feedback resulting from the large CSI variation to the sensing transmitter.
  • Whether the threshold is predefined, or defined by the sensing receiver, transmitter, initiator or responder is TBD.
  • The threshold based procedure is not always required (Procedure A in 21/0351r5 is not always required).
  Move: Mengshi Hu Second: Junghoon Suh
  Preliminary Result: Motion Passes ( 21 Y/ 7N/ 11A)
  Result*: Motion Passes (21Y/6N/10A)
  Note：
    * Amended result accounts for removal of 2 votes of non-voting members.
    Related document 21/0351r5

## Slide 37
Motions on June 1, 8.

## Slide 38
Motion 19
Move to adopt the document (21-0782r2) as the initial official Channel Models document for IEEE 802.11bf.
  Move: Meihong Zhang Second: Rui Du
  Preliminary Result: Motion Passes ( 26Y/ 1N/ 17A)
  Result*: Motion Passes (26Y/1N/16A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 21/0782r2

## Slide 39
Motions on July Plenary

## Slide 40
Approve TGbf meeting minutes
Move to approve TGbf minutes of meetings and teleconferences from May 2021 meeting to today:
  May Interim: https://mentor.ieee.org/802.11/dcn/21/11-21-0870-02-00bf-meeting-minutes-may-2021.docx
  Teleconferences May - July:
  https://mentor.ieee.org/802.11/dcn/21/11-21-0914-03-00bf-ieee-802-11bf-teleconference-minutes-may-july-2021.docx
Move: Leif Wilhelmsson Second: Assaf Kasher
Result: Approved by unanimous consent
Notes: Approved by unanimous consent

## Slide 41
Motion 20
Move to add the following to 11bf SFD:
  CSI (that is, the channel measured during the training symbols of a received PPDU) is a type of sensing measurement result for sub-7 GHz WLAN sensing.
  Move: Claudio Da Silva Second: Assaf Kasher
  Result: Approved by unanimous consent
  Note：
    Related document 21/0908r2
    SP Result: 36/0/5 ( Y/ N/ A)

## Slide 42
Motion 21
Move to add the following to 11bf SFD:
  To enable sub-7 GHz WLAN sensing, an RXVECTOR parameter CSI_ESTIMATE is defined that contains the channel measured during the training symbols of the received PPDU.
  A Sensing Measurement Report frame, which allows a sensing receiver to report sensing measurements, is defined. This new frame contains at least the following two fields:
    Measurement report control field: Contains information necessary to interpret the measurement report field.
    Measurement report field: Carries CSI measurements obtained by a sensing receiver.
  The format of CSI_ESTIMATE is the same one used in the measurement report field within the Sensing Measurement Report frame. The format of CSI_ESTIMATE is TBD.
  Transmission of the Sensing Measurement Report frame is initiated by an MLME primitive. Both immediate and delayed reporting are acceptable.
  Move: Claudio Da Silva Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 21/0908r2
    SP Result: 22/6/8 ( Y/ N/ A)

## Slide 43
Motion 22
Move to add the following to 11bf SFD:
  measurement phase of sensing session, the NDP can be used for the channel measurement (e.g. CSI) between sensing transmitter and sensing receiver(s) in sub 7Ghz band.
  NDP format for sensing is TBD.
  Move: Dongguk Lim Second: Sang Kim
  Result: Approved by unanimous consent
  Note：
    Related document 21/1015r1
    SP Result: 26/0/8 ( Y/ N/ A)

## Slide 44
Motion 23
Move to add the following to 11bf SFD:
  The Sensing Session is pairwise and is identified by MAC addresses and/or associated AID/UID.
  11bf shall define an optional negotiation process in the sensing setup phase for a sensing initiator and a sensing responder to exchange and agree on operational parameters associated with a sensing session. The initiator may maintain multiple sensing sessions.
  Move: Solomon Trainin Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 21/0644r4
    SP Result: 19/3/15 ( Y/ N/ A)

## Slide 45
Motion 24
Move to add the following to 11bf SFD:
  The Measurement Setup ID may be used to identify attributes of the sensing measurement instances
  The Measurement Instance ID may be used to identify the sensing measurement instance that utilizes attributes of the same Measurement Setup ID
  The Dialog Token field may be a possibility to contain both IDs
  Move: Solomon Trainin Second: Cheng Chen
  Result: Approved by unanimous consent
  Note：
    Related document 21/0644r4
    SP Result: 20/1/11 ( Y/ N/ A)

## Slide 46
Motions on August 17.

## Slide 47
Motion 25
Move to add the following to 11bf SFD:
  11bf shall define a Trigger-based sensing measurement instance including the following:
    A polling process where an AP sends a Trigger frame to check the availability of STAs. If a STA is available, it responds with a CTS-to-self..
    UL sounding, in which an AP sends a Trigger frame to solicit NDP transmission(s) from STA(s), shall be present if at least one STA that is a sensing transmitter responds in the polling.
    DL sounding, in which an AP sends NDPA frame followed by NDP to STA(s), shall be present if at least one STA that is a sensing receiver responds in the polling.
    The order of the UL and DL sounding is TBD.
    The details of the format of the Trigger frame and the NDPA frame are TBD.
  Note: This is for HE/EHT STAs. Methods to support other STAs are TBD.
  Move: Cheng Chen Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 21/0990r2
    SP Result: 26/0/13 ( Y/ N/ A)

## Slide 48
Motion 25a
Move to add the following to 11bf SFD:
  11bf shall define a Trigger-based sensing measurement instance including the following:
    A polling process where an AP sends a Trigger frame to check the availability of STAs. If a STA is available, it responds with a CTS-to-self..
    UL sounding, in which an AP sends a Trigger frame to solicit NDP transmission(s) from STA(s), shall be present if at least one STA that is a sensing transmitter responds in the polling.
    DL sounding, in which an AP sends NDPA frame followed by NDP to STA(s), shall be present if at least one STA that is a sensing receiver responds in the polling.
    The order of the UL and DL sounding is TBD.
    The details of the format of the Trigger frame and the NDPA frame are TBD.
  Note: This is for HE/EHT STAs. Methods to support other STAs are TBD.
  Move: Cheng Chen Second: Ali Raissinia
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 21/0990r2
    SP Result: 26/0/13 ( Y/ N/ A)

## Slide 49
Motion 25b Motion to amend
Change the previous motion to:
Move to add the following to 11bf SFD:
  11bf shall define a Trigger-based sensing measurement instance including the following:
    A polling phase where an AP sends a Trigger frame to check the availability of STAs. If a STA is available, it responds with a CTS-to-self..
    TF sounding, in which an AP sends a Trigger frame to solicit NDP transmission(s) from STA(s), shall be present if at least one STA that is a sensing transmitter responds in the polling.
    NDPA sounding, in which an AP sends NDPA frame followed by NDP to STA(s), shall be present if at least one STA that is a sensing receiver responds in the polling.
    The order of the TF sounding and NDPA sounding is TBD.
    The details of the format of the Trigger frame and the NDPA frame are TBD.
  Note: This is for HE and/or EHT STAs. Methods to support other STAs are TBD.
  Move: Cheng Chen Second: Junghoon Suh
  Approved by unanimous consent
  Note：
    Related document 21/0990r2
    SP Result: 26/0/13 ( Y/ N/ A)

## Slide 50
Motion 25c
Move to add the following to 11bf SFD:
  11bf shall define a Trigger-based sensing measurement instance including the following:
    A polling phase where an AP sends a Trigger frame to check the availability of STAs. If a STA is available, it responds with a CTS-to-self..
    TF sounding, in which an AP sends a Trigger frame to solicit NDP transmission(s) from STA(s), shall be present if at least one STA that is a sensing transmitter responds in the polling.
    NDPA sounding, in which an AP sends NDPA frame followed by NDP to STA(s), shall be present if at least one STA that is a sensing receiver responds in the polling.
    The order of the TF sounding and NDPA sounding is TBD.
    The details of the format of the Trigger frame and the NDPA frame are TBD.
  Note: This is for HE and/or EHT STAs. Methods to support other STAs are TBD.
  Move: Cheng Chen Second: Junghoon Suh
  Approved by unanimous consent
  Note：
    Related document 21/0990r2
    SP Result: 26/0/13 ( Y/ N/ A)

## Slide 51
Motions on August 31.

## Slide 52
Motion 26a
Move to add the following to 11bf SFD:
  The NDPA sounding defined in 11bf consists of:
    The measurement is initiated by an NDP Announcement frame.
    The transmitter shall transmit an NDP SIFS after transmitting the NDP Announcement frame.
    The detailed definition of the NDP Announcement frame is TBD.
    The process to validate the STA(s) participation is TBD
  Note : This can be applied to pre-HE STAs (i.e. not limited to HE and/or EHT STAs)
  Move: Dongguk Lim Second: Claudio da Silva
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 21/1015r2
    SP Result: 28Y/1N/9A

## Slide 53
Motion 26b Motion to amend
Change the previous motion to:
Move to add the following to 11bf SFD:
  The NDPA sounding defined in 11bf consists of:
    A transmission of an NDP Announcement frame
    A transmission of an NDP SIFS after transmitting the NDP Announcement frame
  Note : The detailed definition of the NDP Announcement frame is TBD.
  Note : This may be applied to pre-HE STAs (i.e. not limited to HE and/or EHT STAs)
  Move: Rui Yang Second: Solomon Trainin
  Result*: Approved by unanimous consent
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 21/1015r2
    SP Result: 28Y/1N/9A

## Slide 54
Motion 26c
Move to add the following to 11bf SFD:
  The NDPA sounding defined in 11bf consists of:
    A transmission of an NDP Announcement frame
    A transmission of an NDP SIFS after transmitting the NDP Announcement frame
  Note : The detailed definition of the NDP Announcement frame is TBD.
  Note : This may be applied to pre-HE STAs (i.e. not limited to HE and/or EHT STAs)
  Move: Dongguk Lim Second: Claudio da Silva
  Result*: Approved by unanimous consent
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 21/1015r2
    SP Result: 28Y/1N/9A

## Slide 55
Motions on September 7.

## Slide 56
Motion 27
Move to add the following to 11bf SFD:
  The TF sounding defined in 11bf consists of followings:
    The Trigger frame is used to solicit the NDP transmission(s).
    The transmitter(s) shall transmit an NDP SIFS after receiving the Trigger frame.
  Note :The detailed definition of the Trigger frame is TBD.
  Note : This is for HE and/or EHT STAs. Supporting other STAs are TBD.
  Move: Dongguk Lim Second:
  Result*: Approved by unanimous consent
  Note：
    Related document 21/1015r2
    SP Result: 29Y/0N/7A ( Y/ N/ A)

## Slide 57
Motions on September Interim.

## Slide 58
Approve TGbf meeting minutes
Move to approve TGbf minutes of meetings and teleconferences from July 2021 meeting to today:
  July Plenary: https://mentor.ieee.org/802.11/dcn/21/11-21-1306-00-00bf-ieee-802-11bf-july-2021-plenary-meeting-minutes.docx
  Teleconferences July - September:
  https://mentor.ieee.org/802.11/dcn/21/11-21-1314-04-00bf-ieee-802-11bf-teleconference-minutes-july-september-2021.docx
Move: Leif Wilhelmsson Second: Rojan Chitrakar
Result: Approved by unanimous consent
Notes: Approved by unanimous consent

## Slide 59
Motion 28
Move to modify the initial official channel model document IEEE 802.11 (21-0782r2) as IEEE 802.11 (21-1409r1) by adding the chapter 5 – Channel Model - Data-driven Hybrid Channel Model’ and chapter 7 - Appendix?
  Move: Yan Xin Second: Junghoon Suh
  Result: Approved by unanimous consent
  Note：
    Related document 21/1409r1
    SP Result: 22Y/2N/24A

## Slide 60
Motion 29
Motion to modify the SFD as defined in pages 5-7 of 11-21/1543r1 and to incorporate the figures in pages 2-3 of 11-21/1543r1 into the SFD.
  Move: Solomon Trainin Second: Cheng Chen
  Result: Approved by unanimous consent
  Note：
    Related document 21/1543r1
    SP Result: Y/N/A

## Slide 61
Motions on October 12.

## Slide 62
Motion 30
  Move to adopt the document (21/0876r3) as the official Evaluation Methodology and Simulation Scenarios document for IEEE 802.11 bf.
  Simulation is not mandatory for any contributions.
  Move: Rui Du Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 21/0876r3
    SP Result: 20Y/ 0N/ 6A

## Slide 63
Motion 31
  Move to adopt Truncated Channel Impulse Response(TCIR) described as follows as one optional type of the sensing measurement results for sub-7GHz sensing
  Calculating the CIR (time domain) from CSI/CFR (frequency domain) through IFT(usually, IFFT) .
  Reporting the subset of complex samples corresponding to the range of interest of the entire CIR .
  Note: the size of the subset is TBD.
  Move: Rui Du Second: Junghoon Suh
  Preliminary Result: (22Y/ 16N/ 9A)
  Result*: Motion Fails (21Y, 16N, 9A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 21/1288r2
    SP Result: 24Y/ 6N/ 16A

## Slide 64
Motion 32
  Move to add the following to 11bf SFD:
  In the threshold based measurement instance, the estimation of CSI variation is implementation specific, but it shall follow the following rules:
  The degree of the estimated CSI variation shall be represented by a value in the closed interval [0, 1].
  A larger degree shall reflect a larger estimated CSI variation.
  The degree of 0 indicates the smallest degree of the estimated CSI variation.
  The degree of 1 indicates the largest degree of the estimated CSI variation.
  Note: Which CSI variation corresponds to the degree of 0 or 1 is implementation specific.
  Move: Mengshi Hu Second: Rajat Pushkarna
  Preliminary Result: ( 18Y/ 7N/ 13A)
  Result*: Motion Fails (17Y, 7N, 13A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 21/1364r3
    SP Result: 14Y/ 5N/ 6A

## Slide 65
Motion 33
  Move to add the following to 11bf SFD:
  In the threshold based measurement instance, the threshold for each responder to be compared with the CSI variation value is determined by the initiator.
  Move: Mengshi Hu Second: Chenchen Liu
  Result: Approved by unanimous consent
  Note：
    Related document 21/1364r3
    SP Result: 16Y/ 1N/ 6A

## Slide 66
Motions on November Plenary.

## Slide 67
Motion 34
  Move to add the following to 11bf SFD:
  In reporting phase, the measurement results from multiple measurement setups of a sensing responder may be included in a single measurement report frame for delayed reporting.
    Support for obtaining more than one measurement results in a single measurement report frame sent by the responder is optional for the initiator.
    Support for buffering more than one measurement result and sending it in a single measurement report frame to the initiator is optional for the responder.
  Move: Chaoming Luo Second: Lei Huang
  Result: Approved by unanimous consent
  Note：
    Related document 21/1438r1
    SP Result: 16Y/ 5N/ 13A

## Slide 68
Motion 35
  Motion to incorporate the text on slides 5, 6 of 11-21-1701-01-00bf Measurement setup termination into the SFD.
  Move: Solomon Trainin Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 21/1701r1
    SP Result: 32Y/ 4N/ 59A

## Slide 69
Motion 36
  Move to add the following to 11bf SFD:
  During a sensing measurement setup, role(s) of a sensing responder shall be determined as one of followings:
    – Sensing Receiver
    – Sensing Transmitter
    – Sensing Transmitter and Receiver
  Move: Insun Jang Second: Sang Kim
  Result: Approved by unanimous consent
  Note：
    Related document 21/1736r2
    SP Result: 34Y/ 6N/ 23A

## Slide 70
Motion 37
  Move to add the following to 11bf SFD:
  The transmitter and receiver role(s) of a STA corresponding to a sensing measurement setup ID until the measurement setup is terminated shall be fixed as determined during the measurement setup.
  Move: Insun Jang Second: Dongguk Lim
  Result: Approved by unanimous consent
  Note：
    Related document 21/1736r2
    SP Result: 35Y/ 7N/ 22A

## Slide 71
Motions on December 21 (Tuesday).

## Slide 72
Motion 38
  Move to add the following to the TGbf SFD:
An optional sensing by proxy (SBP) procedure is defined in which:
An “SBP request” consists of a non-AP STA sending an SBP Request frame to an SBP-capable AP STA.
  A STA that sends an SBP Request frame to invoke SBP (and, as a result, WLAN sensing) is denoted by “SBP requesting STA”.
  The format and contents of the SBP Request frame are TBD.
An AP STA that receives an SBP request shall send to the SBP requesting STA an SBP Response frame to accept or reject the request.
  The format and contents of the SBP Response frame are TBD.
An AP STA that accepts an SBP request shall initiate a WLAN sensing procedure with one or more non-AP STAs using operational parameters derived from those indicated within the SBP Request frame.
Whether the SBP requesting STA participates or not in the WLAN sensing procedure as a sensing responder is TBD.
Measurement results obtained in a WLAN sensing procedure resultant from an SBP request shall be reported to the SBP requesting STA.
  Move: Claudio Da Silva Second: Chaoming Luo
  Result: Approved by unanimous consent
  Note：
    Related document 21/1692r4
    SP Result: 30Y/ 2N/ 8A

## Slide 73
Motion 39
  Move to add the following to the TGbf SFD:
  11bf shall define a non-Trigger based (non-TB) sensing measurement instance as follows:
    One non-AP STA is the sensing initiator and one AP is the sensing responder.
    Once the non-AP STA obtains a TXOP, it initiates a non-TB sensing measurement instance by transmitting an NDPA frame to the AP followed by an Initiator-to-Responder (I2R) NDP after SIFS. SIFS after the I2R NDP, the AP shall transmit a Responder-to-Initiator (R2I) NDP to the non-AP STA.
    If the non-AP STA is only the sensing transmitter, then the NDPA frame should configure the R2I NDP to be transmitted with minimum possible length with one LTF symbol.
    If the non-AP STA is only the sensing receiver, then the NDPA frame should configure the I2R NDP to be transmitted with minimum possible length with one LTF symbol.
    The details of the NDPA frame are TBD.
    I2R/R2I NDP formats are TBD.
  Move: Cheng Chen Second: Jinsoo Choi
  Result: Approved by unanimous consent
  Note：
    Related document 21/1433r2
    SP Result: 19Y/ 4N/ 13A

## Slide 74
Motion 40
  Move to add the following to the TGbf SFD:
  DMG/EDMG-based WLAN sensing supports both monostatic sensing and monostatic sensing with coordination configurations.
  In the monostatic sensing with coordination configuration, the transmissions of one or more devices that perform monostatic sensing are coordinated by a PCP/AP.
  Move: Rui Du Second: Claudio Da Silva
  Result*: Approved by unanimous consent
  Note：
    Related document 21/1914r0
    SP Result: 23Y/ 0N/ 14A

## Slide 75
Motions on January 11 (Tuesday).

## Slide 76
Motion 41 (January 11)
  Do you support to add to the 11bf SFD that sensing measurement setup request and response frames, which allow to perform a sensing measurement setup, are defined, and the following mechanism is enabled?
  A sensing initiator transmits a sensing measurement setup request frame to a sensing responder with which it intends to perform a sensing measurement setup
  The sensing responder, which receives the sensing measurement setup request frame, shall transmit a sensing measurement setup response frame to the sensing initiator which transmitted the sensing measurement setup request frame to accept or reject the sensing measurement setup
  The subtype of sensing measurement setup request and response frames are Action and those are individually addressed
  Formats of the sensing measurement setup request and response frames are TBD
  Move: Insun Jang Second: Sang Kim
  Result: Approved by unanimous consent
  Note：
    Related document 21/1735r3
    SP Result: 25Y/ 0N/ 9A

## Slide 77
Motion 42
  Move to add the following to the TGbf SFD:
  The 11bf amendment shall define at least one measurement report type for 2D, 3D and 4D filtered maps, for DMG/EDMG.
  This measurement report type is an optional feature.
  Supporting 2D, 3D and 4D are each optional feature
  The details of the measurement report format is TBD
  2D is a two-dimensional map, where the two dimensions are any from: Range, Azimuth, Elevation & Doppler.
  3D is a three-dimensional map, where the three dimensions are any from: Range, Azimuth, Elevation & Doppler.
  4D is a four-dimensional map, where the four dimensions are: Range, Azimuth, Elevation & Doppler.
  Move: Alecsander Eitan Second: Assaf Kasher
  Preliminary Result: ( 14Y/ 4N/ 21A)
  Result*: Motion Passes ( 12Y/ 4N/ 21A)
  Note：
    * Amended result accounts for removal of 2 votes of non-voting members.
    Related document 21/1801r2
    SP Result: 8Y/ 4N/ 21A

## Slide 78
Motion 43
  Move to add the following to the TGbf SFD:
  The 11bf amendment shall define at least one measurement report type for targets, for DMG/EDMG.
  (“Target” is a detected object)
  This measurement report type is an optional feature.
  The details of the measurement report format is TBD
  Move: Alecsander Eitan Second: Assaf Kasher
  Result: Approved by unanimous consent
  Note：
    Related document 21/1801r2
    SP Result: 8Y/ 10N/ 16A

## Slide 79
Motion 44
  Move to add the following to the TGbf SFD:
  A timestamp reflecting a time-of-measurement shall be included as part of a Measurement Result for both MLME and the Sensing Measurement Report.
  Move: Chris Beg Second: Rajat Pushkarna
  Preliminary Result: ( 15Y/ 12N/ 7A)
  Result*: Motion Fails (14Y/ 12N/ 7A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 21/1924r0
    SP Result: 18Y/ 7N/ 17A

## Slide 80
Motion 45
  Move to add the following to the TGbf SFD:
  EDMG transmitter initiator bi-static sensing is based on a BRP request in a BRP-RX/TX, BRP-TX, BRP-RX PPDU as defined in Clause 28 of 802.11 specifications and the BRP response
  Feedback for the measurement is carried in the BRP response
    Feedback may be delayed
    Feedback may be aggregated (single feedback for some measurements, to facilitate doppler measurement)
  Move: Assaf Kasher Second: Solomon Trainin
  Preliminary Result: ( 16Y/ 1N/ 13A), request to record in minutes
  Result*: Motion Passes ( 16Y/ 1N/ 13A)
  Note：
    * Amended result accounts for removal of 0 votes of non-voting members.
    Related document 21/1865r1
    SP Result: 12Y/ 1N/ 22A

## Slide 81
Motion 46
  Move to add the following to the TGbf SFD:
  EDMG/DMG sensing receiver initiator bi-static sensing is based on a BRP request frame that includes a request for the responder to transmit a BRP-RX/TX, BRP-TX, BRP-RX PPDU as defined in Clause 28 of 802.11 specifications .
  Move: Assaf Kasher Second: Claudio da Silva
  Result*: Approved by unanimous consent
  Note：
    Related document 21/1865r1
    SP Result: 11Y/ 0N/ 8A

## Slide 82
Motion 47
  Move to add the following to the TGbf SFD:
  EDMG/DMG Bi/multi-static sensing capability set may include (at least):
    TRN field Golay sequence lengths supported
    Maximum number of directions in Tx and Rx (Number of Tx/RX AWV sets used for sensing)
    Beam sets in which every beam has direction, gain, and beam width.
  Move: Assaf Kasher Second: Rui Du
  Result: Approved by unanimous consent
  Note：
    Related document 21/1865r1
    SP Result: 12Y/ 0N/ 18A

## Slide 83
Motion 48
  Move to add the following to the TGbf SFD:
  In an EDMG/DMG Bi/Multi-static measurement setup exchange (at least) the following parameters may be exchanged:
    set of beam directions in TX (sets of TX AWV settings to be used in the measurements)
    set of beam directions in RX (sets of RX AWV settings to be used in the measurements)
    beamforming TRN field information such as TRN-P, TRN-M, TRN-N
    location and orientation of each of the STAs
      coordinates can be local or earth coordinates
      relative locations orientation may be estimated using TGaz based exchanges or available from management layer
    Scheduling
  Move: Assaf Kasher Second: Alecsander Eitan
  Result: Approved by unanimous consent
  Note：
    Related document 21/1865r1
    SP Result: 10Y/ 1N/ 21A

## Slide 84
Motion 49
  Move to add the following to the TGbf SFD:
  Truncated Channel Impulse Response(TCIR) described as follows should be considered as one optional type of the sensing measurement results for sub-7GHz sensing.
    Calculating the CIR (time domain) from frequency domain CSI through IDFT(usually, IFFT) .
    Reporting the subset of complex samples corresponding to the range of interest of the entire CIR .
    Note: the size of the subset is TBD
  Move: Rui Du Second: Oscar Au
  Preliminary Result: ( 17Y/ 8N/ 14A)
  Result*: Motion Fails ( 17Y/ 8N/ 14A)
  Note：
    * Amended result accounts for removal of 0 votes of non-voting members.
    Related document 21/1288r4
    SP Result: 12Y/ 3N/ 20A

## Slide 85
Motion 50
  Move to add the following to the TGbf SFD:
  The 11bf amendment shall define a new subclause under 6.3 (MLME SAP interface) that specifies request, confirm, indication, and response primitives for WLAN sensing.
  Move: Claudio Da Silva Second: Cheng Chen
  Result: Approved by unanimous consent
  Note：
    Related document 21/1949r0
    SP Result: 28Y/ 0N/ 6A

## Slide 86
Motions on January Interim.

## Slide 87
Motion 51 (January 21 Interim)
  Move to add the following to the TGbf SFD:
  The sensing measurement setup procedure consists of
  the transmission of a sensing measurement setup request frame by the sensing initiator followed by the transmission of an Ack frame by the intended sensing responder; and
  the transmission of a sensing measurement setup response frame by the intended sensing responder followed by the transmission of an Ack frame by the sensing initiator.
  Move: Chaoming Luo Second: Pei Zhou
  Result: Approved by unanimous consent
  Note：
    Related document 21/ 1828r4
    SP Result: 20Y/ 1N/ 15A

## Slide 88
Motion 52
  Move to add the following to the TGbf SFD:
  In a sensing measurement setup procedure, if the sensing responder intends to reject the assigned operational parameters included in the sensing measurement setup request frame, it may provide its preferred operational parameters in the sensing measurement setup response frame.
  For the accept case, whether the responder may provide its preferred operational parameters or not is TBD.
  Move: Chaoming Luo Second: Insun Jang
  Preliminary Result: ( 34 Y/ 2 N/ 19 A) Record
  Result*: Motion Passes (34Y, 2N, 18A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 21/ 1828r4
    SP Result: 14Y/ 6N/ 14A

## Slide 89
Motion 53 (Defer)
  Move to add the following to the TGbf SFD:
  11bf shall define both public and protected action frames, which include sensing measurement setup request/response, sensing measurement report, sensing measurement setup termination, and SBP request/response frames.
  Note: Other public and protected action frames for sensing are TBD.
  Move: Chaoming Luo Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 21/ 1828r4
    SP Result: 23Y/ 0N/ 8A

## Slide 90
Motion 54
  Move to add the following to the TGbf SFD:
  Measurement Setup ID is set by Sensing Initiator, the tuple <Sensing Initiator’s MAC address, Measurement Setup ID> is used to identify a specific Measurement Setup.
  How the SBP Requesting STA identifies the sensing measurement setup ID is TBD.
  Move: Pei Zhou Second: Chaoming Luo
  Preliminary Result: ( 28 Y/ 3 N/ 26 A)
  Result*: Motion Passes (28Y, 3N, 25A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 21/ 1941r1
    SP Result: 20Y/ 4N/ 16A

## Slide 91
Motion 55
  Move to append the text on page 2 and the figures of the 11-21-2015-04-00bf-DMG-Sensing-procedure to the SFD
  Move: Solomon Trainin Second: Alecsander Eitan
  Result: Approved by unanimous consent
  Note：
    Related document 21/ 2015r4
    SP Result: 18Y/ 4N/ 18A

## Slide 92
Motion 56
  Move to append the text of the “11-22-0031-00-00bf-DMG Sensing procedure part two” to the SFD
  The text does not include the references
  Move: Solomon Trainin Second: Assaf Kasher
  Result: Approved by unanimous consent
  Note：
    Related document 22/ 0031r0
    SP Result: 12Y/ 7N/ 16A

## Slide 93
Motion 57
  Move to add the following to the TGbf SFD:
  DMG passive sensing is enabled by
  • A capability bit in the beacon
  • Sensing information request and response that will provide information about the beacon
  • Sensing information may include:
  a. azimuth and elevation for each sector id (of beacons)
  b. location information of the PCP/AP
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/ XXXX r0
    SP Result: Y/ N/ A

## Slide 94
Motion 58
  Move to add the following to the TGbf SFD:
  A multi-static EDMG sensing measurement instance has the following parts:
  • An instance request frame (frame type TBD) sent to each STA sequentially, and each STA responds to it.
  • A multi-static EDMG sensing PPDU. The format of the EDMG sensing PPDU is undefined.
  • A feedback part in which the initiator polls each responding STA for a report and the responders respond with a report.
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/ XXXX r0
    SP Result: Y/ N/ A

## Slide 95
Motion 59
  Move to add the following to the TGbf SFD:
  A multi-static EDMG sensing PPDU is an EDMG BRP-RX, BRP-TX, BRP-RX/TX PPDU with an addition of sync fields between the data and the TRN field
  Move: Assaf Kasher Second: Alecsander Eitan
  Result: Approved by unanimous consent
  Note：
    Related document 22/ XXXX r0
    SP Result: Y/ N/ A

## Slide 96
Motion 60
  Move to add the following to the TGbf SFD:
  For the case when the sensing initiator is the sensing transmitter, the reporting of sensing measurement results to the sensing initiator is optional.
  Move: Oscar Au Second: Claudio da Silva
  Result: Approved by unanimous consent
  Note：
    Related document 22/ 0038 r2
    SP Result: 43Y/ 2N/ 21A

## Slide 97
Motions on February 22.

## Slide 98
Motion 61
  Move to add the following to the TGbf SFD:
  11bf shall define both public and protected action frames, which include sensing measurement setup request/response, sensing measurement report, sensing measurement setup termination, and SBP request/response/termination frames.
  Note: Other public and protected action frames for sensing are TBD.
  Move: Chaoming Luo Second: Pei Zhou
  Result: Approved by unanimous consent
  Note：
    Related document 21/ 1828r4
    SP Result: 23Y/ 0N/ 8A
    This motion is the former deferred Motion 53.

## Slide 99
Motion 62
  Move to add the following to the TGbf SFD:
  PASN for unassociated STA is used in sensing.
  Move: Chaoming Luo Second: Oscar Au
  Result: Approved by unanimous consent
  Note：
    Related document 22/ 0286r1
    SP Result: 18Y/ 3N/ 15A

## Slide 100
Motion 63
  Move to add the following to the TGbf SFD:
  A new action category of robust ‘Protected Sensing Frame’ is defined to separate PN segment.
  Move: Chaoming Luo Second: Pei Zhou
  Result: Approved by unanimous consent
  Note：
    Related document 22/ 0286r1
    SP Result: 14Y/ 3N/ 18A

## Slide 101
Motion 64
  Move to add the following to the TGbf SFD:
  The method of assigning Measurement Setup ID for the SBP Requesting STA in Sensing by proxy (SBP) procedure is that AP assigns the Measurement Setup ID in its SBP Response frame.
  Move: Pei Zhou Second: Chaoming Luo
  Result: Approved by unanimous consent
  Note：
    Related document 22/ 0125r3
    SP Result: 20Y/ 2N/ 17A

## Slide 102
Motions on March 1.

## Slide 103
Motion 65
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0170r3, Sensing Measurement Instance: Reporting
  Move: Rajat PUSHKARNA Second: Claudio da Silva
  Result: Approved by unanimous consent
  Note：
    Related document 22/ 0170r3
    SP Result: 15Y/ 1N/ 10A

## Slide 104
Motion 66 (Defer)
  Move to add the following to the TGbf SFD:
  Truncated Channel Impulse Response(TCIR) described as follows should be considered as an optional type of the sensing measurement results for sub-7GHz sensing.
    The CIR is defined as the output of IDFT of frequency domain CSI.
    The TCIR is a subset of CIR around the largest magnitude tap of the CIR.
    Note: the method of selecting TCIR taps from the CIR is TBD.
  Move: Rui Du Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 21/ 1288r4
    SP Result: Y/ N/ A

## Slide 105
Motions on March 8.

## Slide 106
Motion 67
  Move to add the following to the TGbf SFD:
  Enhance the sensing procedure initiated by an AP to optionally allow sensing responder to sensing responder NDP measurement.
  Move: Sang Kim Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/ 0312r2
    SP Result: 26Y/ 2N/ 10A

## Slide 107
Motion 68
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0172r3 PDT Sensing Measurement Instance: General
  Move: Cheng Chen Second: Oscar Au
  Result: Approved by unanimous consent
  Note：
    Related document 22/0172r3
    SP Result: 26Y/ 0N/ 7A

## Slide 108
Motion 69
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0174r3 PDT Non-TB Sensing Measurement Instance
  Move: Cheng Chen Second: Oscar Au
  Result: Approved by unanimous consent
  Note：
    Related document 22/0174r3
    SP Result: 25Y/ 0N/ 10A

## Slide 109
Motion 70
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0233r3: Proposed Draft Text for MLME
  Move: Claudio da Silva Second: Cheng Chen
  Result: Approved by unanimous consent
  Note：
    Related document 22/0233r3
    SP Result: 30Y/ 0N/ 5A

## Slide 110
Motion 71
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0079r2: Proposed Draft Text for SENS Procedure Overview
  Move: Claudio da Silva Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 22/0079r2
    SP Result: 31Y/ 0N/ 2A

## Slide 111
Motion 72
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0235r5 Proposed Draft Text for Sensing Measurement Report frame (excl. format)
  Move: Claudio da Silva Second: Alecsander Eitan
  Result: Approved by unanimous consent
  Note：
    Related document 22/0235r5
    SP Result: 28Y/ 0N/ 8A

## Slide 112
Motion 73 (Record)
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0134r4 PDT Threshold-based Sensing Procedure
  Move: Mengshi Hu Second: Jinsoo Choi
  Preliminary Result: ( 51 Y/ 5 N/ 24A)
  Result*: Motion Passes (51Y/5N/23A)
  Note：
    * Amended result accounts for removal of 1 votes of non-voting members.
    Related document 22/0134r4
    SP Result: 35Y/ 6N/ 9A

## Slide 113
Motion 74
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0229r7 PDT for Sensing Measurement Setup
  Move: Insun Jang Second: Dongguk Lim
  Result: Approved by unanimous consent
  Note：
    Related document 22/0229r7
    SP Result: 22Y/ 0N/ 15A

## Slide 114
Motion 75
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0243r6 PDT DMG Sensing procedure
  Move: Solomon Trainin Second: Assaf Kasher
  Result: Approved by unanimous consent
  Note：
    Related document 22/0243r6
    SP Result: unanimous consent

## Slide 115
Motion 76
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0181r1 pdt-sensing-session-setup
  Move: Chaoming Luo Second: Mike Montemurro
  Result: Approved by unanimous consent
  Note：
    Related document 22/0181r1
    SP Result: unanimous consent

## Slide 116
Motion 77
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0182r0 pdt-sensing-session-termination
  Move: Chaoming Luo Second: Pei Zhou
  Result: Approved by unanimous consent
  Note：
    Related document 22/0182r0
    SP Result: unanimous consent

## Slide 117
Motion 78
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0173r5 PDT TB Sensing Measurement Instance
  Move: Cheng Chen Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 22/0173r5
    SP Result: unanimous consent

## Slide 118
Motion 79
  Move to add the following to the TGbf SFD:
  The STA info field in sensing NDPA includes the following information.
    AID11 (11bits)
    I2R NDP NSTS (3bits)
    R2I NDP NSTS (3bits)
  Move: Dongguk Lim Second: Jinsoo Choi
  Preliminary Result: ( 27 Y/ 30 N/ 23A)
Result*: Motion Fails (26 Y, 29N, 22A)
  Note：
    * Amended result accounts for removal of 3 votes of non-voting members.
    Related document 22/ 0338r1
    SP Result: 22Y/ 6N/ 9A

## Slide 119
Motion 80
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0126r5 Proposed Draft Text for Sensing measurement setup termination
  Move: Pei Zhou Second: Chaoming Luo
  Result: Approved by unanimous consent
  Note：
    Related document 22/0126r5
    SP Result: unanimous consent

## Slide 120
Motion 81
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0223r5 pdt-sbp-frames
  Move: Chaoming Luo Second: Pei Zhou
  Result: Approved by unanimous consent
  Note：
    Related document 22/0223r5
    SP Result: 23Y/ 2N/ 15A

## Slide 121
Motions on March 14.

## Slide 122
Motion 82
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0234r6 Proposed Draft Text for the SBP Procedure
  Move: Claudio da Silva Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 22/0234r6
    SP Result: Unanimous consent

## Slide 123
Motion 83
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0251r4 PDT DMG Sensing Report IE
  Move: Alecsander Eitan Second: Assaf Kasher
  Result: Approved by unanimous consent
  Note：
    Related document 22/0251r4
    SP Result: Unanimous consent

## Slide 124
Motions on March 31.

## Slide 125
Motion 84
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/240r5 PDT-DMG-Sensing-Capability
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/240r5
    SP Result: Unanimous consent

## Slide 126
Motion 85
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/241r7 PDT-DMG-Passive-sensing
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/241r7
    SP Result: Unanimous consent

## Slide 127
Motion 86
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/295r5 PDT-DMG-Measurement-Setup-frames
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/295r5
    SP Result: Unanimous consent

## Slide 128
Motion 87
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0327r1 PDT-Bi-Static-Sounding-and-BPR-Frame
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/0327r1
    SP Result: Unanimous consent

## Slide 129
Motions on April 12.

## Slide 130
Motion 88
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0370r3 PDT-DMG-Multi-Static-Instance
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/0370r3
    SP Result: 17/6/17

## Slide 131
Motion 89
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0524r1 Proposed Draft Text for SBP and Motion 60
  Move: Claudio da Silva Second: Jinsoo Choi
  Result: Approved by unanimous consent
  Note：
    Related document 22/0524r1
    SP Result: Unanimous consent

## Slide 132
Motion 90
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0521r1 PDT STA to STA Sensing
  Move: Sang Kim Second: Dongguk Lim
  Result: Approved by unanimous consent
  Note：
    Related document 22/0521r1
    SP Result: Unanimous consent

## Slide 133
Motion 91
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0513r2 Proposed Draft Text for MLME - Part II
  Move: Rui Du Second: Claudio da Silva
  Result: Approved by unanimous consent
  Note：
    Related document 22/0513r1
    SP Result: Unanimous consent
Notes: Naren

## Slide 134
Motion 92
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0132r6 PDT for DMG sensing monostatic configurations
  Move: Rui Du Second: Yan Xin
  Result: Approved by unanimous consent
  Note：
    Related document 22/0132r6
    SP Result: Unanimous consent

## Slide 135
Motion 93
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0555r1 Proposed Draft Text for SBP Procedure Enhancement
  Move: Enrico Rantala Second: Sang Kim
  Result: Approved by unanimous consent
  Note：
    Related document 22/0555r1
    SP Result: Unanimous consent

## Slide 136
Motion 94 (Record)
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  22/0464r2 PDT EDMG Multi-Static PPDU structure
  Move: Assaf Kasher Second: Solomon Trainin
  Preliminary Result: ( 12Y/ 7 N/ 21A)
  Result*: Motion Fails (12Y, 7N, 21A)
  Note：
    * Amended result accounts for removal of 0 votes of non-voting members.
    Related document 22/0464r2
    SP Result: 12Y / 10N / 23A

## Slide 137
Motions on April 14.

## Slide 138
Motion 95 (Comment collection on TGbf D0.1)
  Move to instruct the TGbf editor to prepare TGbf D0.1 and launch a 30-day comment collection on TGbf D0.1.
  Move: Claudio Da Silva Second: Cheng Chen
  Preliminary Result: ( 42 Y/ 0N/ 7 A)
  Result*: Motion Passes (42 Y/ 0N/ 7 A)
  Note：
    * Amended result accounts for removal of 0 votes of non-voting members.
    SP Result: 33Y/ 0N/ 3A

## Slide 139
Motions on May interim.

## Slide 140
Approve TGbf meeting minutes
Move to approve TGbf minutes of meetings and teleconferences from March 2022 meeting to today:
  March Plenary: https://mentor.ieee.org/802.11/dcn/22/11-22-0499-00-00bf-ieee-802-11bf-march-2022-plenary-meeting-minutes.docx
  Teleconferences March- May:
  https://mentor.ieee.org/802.11/dcn/22/11-22-0512-19-00bf-ieee-802-11bf-teleconference-minutes-march-may-2022.docx
Move: Leif Wilhelmsson Second: Alecsander Eitan
Result: Approved by unanimous consent
Notes: Approved by unanimous consent

## Slide 141
Motion 96 (May 10)
  Move to add the following to the TGbf SFD:
  In the formatting of the Sensing Measurement report all the in-phase and quadrature components of each of the tones of the CSI from a given measurement instance for a given TX/RX antenna pair, shall be scaled with the same value.
  Move: Steve Shellhammer Second: Oscar Au
  Result: Approved by unanimous consent
  Note：
    Related document 22/0533r3
    SP Result: Unanimous consent

## Slide 142
Motion 97
  Move to add the following to the TGbf SFD:
  If a STA supports the Sensing Measurement report, then the conditionally mandatory and optional supported values of Ng in the Sensing Measurement report shall depend on the number of transmit antennas and the NDP bandwidth according to the following table:
  • Note, this is relative to a 4x LTF
  • The indices for the Ng = 8 for a 160 MHz NDP are specified in the following table:
  Note: the maximum number of transmit antennas is 8.
  Move: Steve Shellhammer Second: Cheng Chen
  Preliminary Result: ( 32Y/ 6N/ 11A)
  Result*: Motion Passes (29Y, 6N, 11A)
  Note：
    * Amended result accounts for removal of 3 votes of non-voting members.
    Related document 22/0533r3
    SP Result: 45Y/ 13N/ 12A
Condition | Conditionally Mandatory Ng Support | Optional Ng Support
 | 4 | 16
 | 4 | 16
 | 8 | 16
Condition | Conditionally Mandatory Ng Support | Optional Ng Support
 | 4 | 16
 | 4 | 16
 | 8 | 16
Channel Width | Ng | Indices
160 MHz | 8 | -1012, -1004, … -20, -12, 12, 20, … 1004, 1012

## Slide 143
Motion 98
  Move to add the following to the TGbf SFD:
  The Sensing Measurement report shall support word size values for the in-phase and quadrature components of the scaled CSI of both Nb = 8 and Nb = 10 bits.
  Move: Steve Shellhammer Second: Oscar Au
  Result: Approved by unanimous consent
  Note：
    Related document 22/0533r3
    SP Result: Unanimous consent

## Slide 144
Motion 99: Vice Chair/Secretary election/reaffirmation
(May 11)
Move to reaffirm Sang Kim and Assaf Kasher as TGbf Vice-Chairs, and reaffirm Leif Wilhelmsson as TGbf Secretary.
  Move: Jinsoo Choi Second: Oscar Au
  Result: Approved by unanimous consent
  Note: the number of attendee is 57

## Slide 145
Motions on June 20.

## Slide 146
Motion 100
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  11-22-0798-02-00bf-pdt-updates-on-measurement-setup-termination-frame
  Move: Pei Zhou Second: Chaoming Luo
  Result: Approved by unanimous consent
  Note：
    Related document 22/0798r2
    SP Result: 17Y/ 5N/ 5A

## Slide 147
Motion 101
  Move to add the following to the TGbf SFD:
  Both Control mode PPDU and SC mode PPDU could be adopted in DMG bistatic sensing, coordinated bistatic sensing, passive sensing, monostatic sensing, coordinated monostatic sensing.
  Move: Rui Du Second: Yan Xin
  Preliminary Result: ( 16Y/ 5N/ 16A)
  Result*: Motion Passes (16Y, 4N, 14A)
  Note：
    * Amended result accounts for removal of 2 votes of non-voting members, and 1 change request from “No” to “Abstain” (the member clicked the wrong option, and sent the request during the meeting)
    Related document 22/0799r1
    SP Result: Unanimous consent

## Slide 148
Motion 102
  Move to add the following to the TGbf SFD:
  TRN based sensing should be adopted as one of the operating modes in DMG monostatic sensing and coordinated monostatic sensing.
  TRN based sensing is an optional operating mode for DMG monostatic sensing and coordinated monostatic sensing.
  Move: Rui Du Second: Yan Xin
  Preliminary Result: ( 15Y/ 2N/ 18A)
  Result*: Motion Passes (15Y, 2N, 18A)
  Note：
    * Amended result accounts for removal of 0 votes of non-voting members.
    Related document 22/0799r1
    SP Result: Unanimous consent

## Slide 149
Motions on July Plenary.

## Slide 150
Approve TGbf meeting minutes
Move to approve TGbf minutes of meetings and teleconferences from May 2022 meeting to today:
  May Interim:
  https://mentor.ieee.org/802.11/dcn/22/11-22-0811-00-00bf-ieee-802-11bf-may-2022-interim-meeting-minutes.docx
  Teleconferences May - July:
  https://mentor.ieee.org/802.11/dcn/22/11-22-0812-14-00bf-teleconference-minutes-may-july-2022.docx
Move: Leif Wilhelmsson Second: Sang Kim
Result: Approved by unanimous consent
Notes: Approved by unanimous consent

## Slide 151
Motion 103 (July 12)
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  111, 370, 412
  In 22/852r2 Comment Resolution for CIDs related to 4.3.21.25
  Move: Rajat PUSHKARNA Second: Rojan Chitrakar
  Result: Approved by unanimous consent
  Note：
    Related document 22/0852r2
    SP Result: Unanimous consent

## Slide 152
Motion 104
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  022, 148, 149, 150, 180, 186, 188, 189, 190, 196, 197, 198, 210, 216, 217, 220, 231, 232, 233, 234, 257, 269, 335, 342, 344, 401, 455, 461, 462, 464, 465, 473, 524, 533, 584, 605, 608, 609, 610, 629, 646, 675, 691, 692, 695, 696, 711, 713, 742, 745,746, 812, 819, 828, 830, 831, 832, 835, 850, 851,860, 861, 865, 876, 900, 901
  In 22/0877r2, Resolutions for Editorial Comments in CC40 - Part 1
  Move: Claudio Da Silva Second: Alecsander Eitan
  Result: Approved by unanimous consent
  Note：
    Related document: 0877r2
    SP Result: Unanimous consent

## Slide 153
Motion 105
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  025, 074, 183, 201, 227, 235, 440, 441, 683, 685, 686, 687, 693, 703, 707, 723, 727, 728, 842, in 22/0907r1, Resolutions for Editorial Comments in CC40 - Part 3
  023, 229, 429, 665, 841, 848, 852, 853, 854, 856, 858, 859, 894, in 22/0889r3, Resolutions for Editorial Comments in CC40 - Part 2
  Move: Claudio Da Silva Second: Yan Xin
  Result: Approved by unanimous consent
  Note：
    Related document: 22/0907r1, 22/0889r3
    SP Result: Unanimous consent

## Slide 154
Motion 106
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  133, 199, 255, 392, 393, 488, 522, 587, 680, 681, 709, 710, 837, 843, 844, 874, 902, in 22/0931r2, Resolutions for Editorial Comments in CC40 - Part 4
  Move: Claudio Da Silva Second: Oscar Au
  Result: Approved by unanimous consent
  Note：
    Related document: 22/0931r2
    SP Result: Unanimous consent

## Slide 155
Motion 107 (Defer)
  Move to add the following to the TGbf SFD:
  The SBP initiator shall be able to request the SBP responder to restrict the sensing procedure in the SBP to a list of selected non-AP STAs as sensing responders. Each selected non-AP STA shall be specified in terms of its MAC address. When requested, the SBP responder shall not include any non-selected non-AP STAs as sensing responders in the sensing procedure in the SBP.
  Note: SBP initiator can include itself as one of the sensing responders.
  Move: Oscar Au Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/0670r1
    SP Result: Unanimous consent

## Slide 156
Motion 108 (July 14)
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  330, 656, 414, 225, 657, 679, 652, 649, 109
  In 11-22-918r2, CC40-DNG-sensing-req-CIDs
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/0918r2
    SP Result: Unanimous consent

## Slide 157
Motion 109
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  45, 107, 397, 339, 329, 223, 372 (In 11-22-0943-01-00bf CC40-comments DMG comments resolution part one)
  215, 219, 262, 263, 377 (In 11-22-0944-02-00bf CC40-comments DMG comments resolution part two)
  Move: Solomon Trainin Second: Claudio da Silva
  Result: Approved by unanimous consent
  Note：
    Related document 22/0943r1, 22/0944r2
    SP Result: Unanimous consent

## Slide 158
Motion 110
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  106, 67, 68, 84, 396, 86, 87, 73
  as specified in 11-22-901r0 (CC40-Resolution of CIDs in clause 9.4.2 part 1)
  Move: Alecsander Eitan Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/0901r0
    SP Result: Unanimous consent

## Slide 159
Motion 111
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  702, 70, 71, 72, 69, 85
  as specified in 11-22-922r1 (CC40-Resolution of CIDs in clause 9.4.2 part 2)
  Move: Alecsander Eitan Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/0922r1
    SP Result: Unanimous consent

## Slide 160
Motion 112
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  103, 104, 669, 54, 667, 222, 394, 402, 140, 804, 604, 805, 391, 224, 607, 36, 37, 38
  as specified in 11-22-0985-03-00bf-resolutions-for-editorial-comments-in-cc40-part-5
  Move: Claudio da Silva Second: Sang Kim
  Result: Approved by unanimous consent
  Note：
    Related document 22/0985r3
    SP Result: Unanimous consent

## Slide 161
Motion 113
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  2, 228,729, 781
  as specified in 11-22-0934r4, Comment resolution for CIDs 2, 228 and 729
  Move: Anirudha Sahoo Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/0934r4
    SP Result: Unanimous consent

## Slide 162
Motion 114
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  341, 90, 237, 350, 352, 353, 354, 437, 438, 439, 444, and 336
  as specified in 11-22-1095-01-00bf cc40-comments DMG comments resolution part three
  Move: Solomon Trainin Second: Assaf Kasher
  Result: Approved by unanimous consent
  Note：
    Related document 22/1095r1
    SP Result: Unanimous consent

## Slide 163
Motion 115
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  331, 332, 643, 420, 653, 839, 648, 333, 240, 258, 395, 651, 424, 425, 259, 421, 422, 423, 840, 426, 514, 427, as specified in 11-22-947r3, CC40-DMG-informtion-elements-CIDs
  763, 366, 361, 448, 357, 358, 359, 360, 362, 363, 364, 869, 450, 451, 870, 871, 872, as specified in 11-22-966r1, CC40-DMG-clasue-11-CIDs-part-1
  Move: Assaf Kasher Second: Solomon Trainin
  Result: Approved by unanimous consent
  Note：
    Related document 22/947r3, 22/966r1
    SP Result: Unanimous consent

## Slide 164
Motion 116
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  290, 458
  as specified in 11-22-988r2, Comment Resolutions for CC40 11bf D0.1 SBP MLME CIDs
  Move: Rojan Chitrakar Second: Rajat Pushkarna
  Result: Approved by unanimous consent
  Note：
    Related document 22/988r2
    SP Result: Unanimous consent

## Slide 165
Motions on August 16 or 18.

## Slide 166
Motion 117
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  CIDs 1, 589, 647
  as specified in 11-22-0829r3
  Move: Ning Gao Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/0829r3
    SP Result: Unanimous consent

## Slide 167
Motion 118
  Move to add the following to the TGbf SFD:
  The measurement report type described in the PDT Formatting of CSI 22/1020 is the only one defined for the TGbf sub-7 GHz WLAN sensing.
    Signaling of the measurement report type is for further discussion
    Reporting of per-RX antenna gain, RSSI or SNR is for further discussion and it is not a standalone report type
  Move: Junghoon Suh Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/1158r1
    SP Result: 23Y/ 3N/ 8A

## Slide 168
Motion 119
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  CIDs 221, 265
  as specified in 11-22-1176r2
  Move: Ning Gao Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/1176r2
    SP Result: Unanimous consent

## Slide 169
Motion 120
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  CIDs 18, 97, 200, 282, 499, 558, 562, 628, 910
  as specified in 11-22-976r4
  Move: Mengshi Hu Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/0976r4
    SP Result: Unanimous consent

## Slide 170
Motion 121
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  CIDs 11, 46, 75, 76, 77, 80, 260, 261, 378, 492, 515 and 518
  as specified in 11-22/1168r5
  Move: Pei Zhou Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/1168r5
    SP Result: Unanimous consent

## Slide 171
Motion 122
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  CIDs 132, 138, 184 and 275
  as specified in 11-22/1170r2
  Move: Pei Zhou Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/1170r2
    SP Result: 14Y/ 3N/ 9A

## Slide 172
Motion 123
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  CIDs 110, 177, 239, 317, 770
  as specified in 11-22-1175r1
  Move: Anirudha Sahoo Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/1175r1
    SP Result: Unanimous consent

## Slide 173
Backup

## Slide 174
Backup
  Move to add the following to the TGbf SFD:
  Move: Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/XXXXrX
    SP Result: Y/ N/ A
Notes: Approved by unanimous consent
Motion Passes (Y, N, A)
Motion Fails (Y, N, A)

## Slide 175
Backup
  Move to include the text proposed in the following document into the IEEE 802.11bf draft amendment:
  Move: Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/XXXXrX
    SP Result: Y/ N/ A
Notes: Approved by unanimous consent
Motion Passes (Y, N, A)
Motion Fails (Y, N, A)

## Slide 176
Backup
  Move to approve resolutions to the following CIDs listed in the following document and incorporate the text changes into the latest TGbf draft:
  CID, in DCN + title
  Move: Second:
  Preliminary Result: ( Y/ N/ A)
  Result*:
  Note：
    * Amended result accounts for removal of X votes of non-voting members.
    Related document 22/XXXXrX
    SP Result: Y/ N/ A
Notes: Approved by unanimous consent
Motion Passes (Y, N, A)
Motion Fails (Y, N, A)