## Slide 1: SR Field in TB PPDU
Date: 2020-11-18
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Zhou Lan | Broadcom |  |  | 
Notes: September 2012

## Slide 2: Summary
PSR based spatial reuse was discussed in 11ax [1][2] and accepted in the TB PPDU
  Also discussed in the context of SU/MU PPDU
We have experimented with this new technology and would like to reiterate here the proposal in [3] for two SR fields in the TB PPDU
  Although OBSS_PD is mainstream, this is a more surgical approach to SR, targeting a specific recipient.
This will enable continuity of this technology from 11ax to 11be
In release 2 could further discuss this technology in the context of MU PPDU

## Slide 3: 11ax PSR based Spatial Reuse
AP
SR initiator
BSS_B
SR responder
HE TB PPDU
Trigger frame
BSS_G
Non-AP STA
Scenario 1: SR Opportunity identified from Trigger frame
Scenario 2: SR opportunity identified from HE TB PPDU
  Trigger not heard/decoded by SR initiator
  (e.g., if trigger is carried in MU PPDU)
Trigger frame
HE TB PPDU
SR Duration in Trigger frame Common info
TX PowerSR Initiator < PSR – RSSITrigger frame
HE TB PPDU
SR Duration in L-SIG of HE TB PPDU
TX PowerSR Initiator < PSR – RSSIprevious frame from AP with same color
If a PSR opportunity is identified by decoding the SIG A of HE TB PPDU, then the RSSI of previous frame from AP with the same color received (e.g. a beacon frame) can be used to determine the TX power of the SR transmission
Spatial Reuse field in HE TB PPDU is required for the missing trigger scenario
Trigger frame

## Slide 4: Spatial Reuse Field Values in 11ax
  PSR = AP_TXPWR + Acceptable_interference_level
  (normalized to 20MHz)
  For example, with AP power at 10dBm can allow SR with as low as -90dBm interference level or higher.
  Two SR fields enable the AP to allow two different interference levels in each half of the BW

## Slide 5: Reference
https://mentor.ieee.org/802.11/dcn/17/11-17-0075-08-00ax-srp-based-sr-summary-and-update.pptx
https://mentor.ieee.org/802.11/dcn/16/11-16-1216-02-00ax-sr-field-srp-table-for-he-trigger-based-ppdu.pptx
https://mentor.ieee.org/802.11/dcn/20/11-20-1546-00-00be-u-sig-design-for-tb-ppdu.pptx

## Slide 6: SP 1 from [3]
Do you support to have two SR fields (4 bits each, total 8 bits), with granularity of half PPDU BW, but no smaller than 20MHz, in the U-SIG of TB PPDU?

## Slide 7: SP 2
Do you support to have populate the SR field values as in 11ax?