## Slide 1: RU Adaptation in TB UL MU Transmission
Date: 2020-11-27
Authors:
Name | Affiliation | Address | Phone | Email
Yanyi Ding | Panasonic Corporation |  |  | yanyi.ding@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 
Rajat Pushkarna |  |  |  | 

## Slide 2
TB UL MU transmission problem
In TB UL MU transmission, if CS requirement is indicated in the Trigger frame, ED is used to sense the medium by STAs on 20MHz subchannels overlapping the allocated RU/MRU.
If any of the 20MHz subchannels is indicated as busy by ED-based CCA or virtual CS, the STA does not transmit TB PPDU at the allocated RU/MRU.
Whole allocated large-size RU/MRU is wasted even if only a small number of 20MHz subchannels are detected as busy, which would degrade system throughput.

## Slide 3
RU Adaptation
We propose an RU Adaptation procedure to avoid such waste.
  Not applicable to MU-MIMO transmission.
In an RU adaptation procedure, a STA may adapt allocated RU/MRU according to the state of the medium.
  Example RU adaptation
Note: there may be many other possible options of adapted RU/MRU.
Only the size of RU/MRU is adapted, other parameters for TB UL transmission remain unchanged.

## Slide 4
Signaling options
The AP may indicate whether RU adaptation procedure is enabled in the User Info field to the STA.
There are several options for the EHT TB PPDU to indicate the adapted RU/MRU.
  Without explicit signaling
    Decoding may be performed based on blind decoding or signal detection of pre-EHT modulated fields in all 20MHz subchannels.
  Explicit signaling
    Adapted RU/MRU is explicitly signaled in U-SIG field of EHT TB PPDU
Only small changes are needed.
Notes: Only large size RU is indicated, few bits are enough.

## Slide 5
Conclusion
Large-size RU/MRU may be wasted in UL MU transmission when CS is required.
In this contribution, we propose the RU adaptation procedure to improve throughput of TB UL MU transmission with large-size RU/MRU.
  STA may adapt allocated RU/MRU according to the state of medium.
  Only small changes are needed for AP to decode the EHT TB PPDU transmitted on adapted RU/MRU.

## Slide 6
SP#1
Do you think that further investigation on RU adaptation concept for TB UL transmission should be considered?
  Note: not for SFD
Y/N/A:

## Slide 7
Annex:
details about RU Adaptation

## Slide 8
RU Adaptation
Define Associated RU/MRU for each large-size RU/MRU
  Associated RU/MRU is a set of possible options of adapted RU/MRU where the STA shall choose from when a large-size RU/MRU is allocated.
  Some restrictions may be enforced, for example, set a threshold for the size.
Example (the size of associated RU/MRU shall not be smaller than 50% of the size of allocated RU/MRU)
BW (MHz) | RU/MRU Larger Than 242 Tones | Associated RU/MRU
40, 80, 160/80+80, 320/160+160 | RU484 | RU484, RU242 (two options)
80, 160/80+80, 320/160+160 | RU242+RU484 | RU242+RU484, RU484
80, 160/80+80, 320/160+160 | RU996 | RU996, RU242+RU484 (4 options), RU484 (2 options)
160/80+80, 320/160+160 | RU484+RU996 | RU484+RU996, RU996, RU484+RU242 (4 options)
… | … | ...
* When part of the allocated RU/MRU which is detected as idle does not match or cover any of its associated RU/MRU, the allocated RU/MRU is not adapted.