## Slide 1: Random Access for 11be
Date: 2021-04-23
Authors:

## Slide 2: Outline
Key Points on Random Access
Proposal: Random-Access NFRP (RA-NFRP) for 802.11be
  RA-NFRP Principle
  Illustration
  RA-NFRP Efficiency versus UORA
  Scalability towards 802.11 technologies or services
Annex
  Legacy 802.11ax UORA procedure
  Legacy 802.11ax NFRP procedure
  Details on RA-NFRP (advantages, example format)

## Slide 3: Key points
UORA provides low efficiency [1]:
  empty RUs 37%, collision 26%, efficiency 37%
  lost random RUs (either unused or collided) occur on large transmission durations
Random Access still required for 11be !
  Many contributions in 11be report that random-access support becomes now difficult but still required :
    11-20-831r2, 11-20-1192r1, 11-20-1902r0, 11-21-428r0, 11-21-0400r1 …
This contribution proposes a Random-Access mechanism based on NFRP:
  The “Triggered PPDU” is quite universal, as only energy in RU Tone set
    Some vendors have already support NFRP: 11-21-0362r1
  By offering greater efficiency (74%)

## Slide 4: Proposal: Random-Access NFRP (RA-NFRP)
RA-NFRP Principle:
  Reuse the 802.11ax NFRP design, with following modifications :
  AP provides a NFRP request with Random allocations
    RA-NFRP TF identified by predefined Starting_AID value (Typically value 0)
  Random Access to access a RU Tone allocation, by a STA :
    1st random phase: STA randomly selects a RU Tone Set Index
    2nd random phase: STA randomly selects a Feedback Status (response Y or N)
  AP then schedules with Basic TF :
    Schedules a Responding STA by using a sort of temporary AID that corresponds to the RU tone set allocation the STA used
      By the indexes of RU Tone Sets that correspond to RU Tone Set with a single feedback
    Easy Collision detection
      AP considers as correct only a single feedback (responses Y and N means collision, thus no scheduling for such index)
Top Benefits
  Greater efficiency (see next slides), changes limited to MAC.

## Slide 5: RA-NFRP Illustration
NDP (sent by STA1)
NFRP Trigger
Frame
(starting AID = 0)
AP
collided
SIFS
Primary 20MHz
channel
(242 tones)
NDP (sent by STA2)
NDP (sent by STA20)
Data frame (sent by STA1)
Basic Trigger
Frame
(schedule RUs by using RU_TONE_SET_INDEX )
AP
SIFS
SIFS
Multi-STA BA
AP
SIFS
26 tone RU
26 tone RU
RA-NFRP identification :
starting AID = 0, 2047, …
A
B
C
D
Random access:
- select random RU Tone Set index (e.g. using backoff)
- FEEDBACK_STATUS is random
Basic TF scheduling:
AP schedules STAs using RU Tone Set index
Case | NDP Feedback detection by AP | Comment
A | correct (single feedback) | One single STA transmits a TB NDP Feedback
B | Not used (no feedback) | No further RU scheduled
C | correct !! (2 STAs use same feedback value) | RA-NFRP can not detect the error ! : collided data will not be acknowledged
D | Error (two feedbacks) | 2 tone sets used as Feedback (tones for 0 and 1, so feedback=3)
Collided Data frame
(sent by at least 2 STAs)

## Slide 6: RA-NFRP Efficiency
RA-NFRP is a very efficient RA mechanism :
  Early Collision detection:
    performed on NDP feedback (not during Data transmission) : reduce wasted data RUs
  Enhanced collision detection:
    half of collisions are detected (e.g. when RU Tone Sets made of two groups of tones)”
  Detection of Empty NDP RU will avoid having empty data RU
 |  |  | Efficiency for RA scheme |  | 
 | Empty NDP RUs | Collided NDP RUs | Empty data RUs | Collided data RUs | Global efficiency
UORA | - | - | 37% | 26% | 37%
RA-NFRP + Basic TF | 37% | 26% | 0 | 26% / 2 = 13% | 74%
The 37% of empty NDP Tones are not scheduled for data
26% of Aloha collision, halfed by 2-bit feedback
= 37 / (37 + 26/2)

## Slide 7: RA-NFRP scalability
As only energy is received as NFRP feedback, AP needs to know what kind of station it will address.
There is room in ‘User Info’ field of NFRP format to signal the technologies to schedule/trigger subsequent transmissions:
  9 bits in the reserved field (see examples in Annex slide 15)
  Could be used to signal a given technology …
    Basic 11ax TF, Basic 11be TF, future version, …
    or given service or usage :
    multi-AP TF…

## Slide 8: Summary
This document presented a Random Access procedure for 11be, on top of NFRP mechanism.
Efficiency is close to 74%, extremely greater than the legacy UORA (37%).
Scalable to future versions of the 802.11 standard
We think 802.11be would largely benefit from such mechanism.

## Slide 9
Straw Poll #1
Do you support that 802.11be allows NFRP mechanism to support a Random-Access allocation ?
  STAs randomly select an RU Tone Set Index and a Feedback Status
  STAs that win NFRP contention are then scheduled by their RU Tone set Index.
  Note: This is an R2 feature.
Results: Y/N/A

## Slide 10
Annex

## Slide 11: Recall: UL OFDMA-based Random Access (UORA)
UORA allows a non-AP HE STA to access one of a number of resource units designated for random access by the HE AP [1].
UORA provides low efficiency:
  theoretical probability for random access distributions (Slotted-Aloha type):
    empty RUs 37%, collision 26%, efficiency 37%
  lost random RUs (either unused or collided) occur on large transmission durations !
  802.11be needs a more efficient RA mechanism !

## Slide 12: Recall : 802.11ax NFRP procedure
NDP Feedback Report Poll (NFRP) TF is used to collect feedback from a range of associated STAs [1]:
  STAs are identified by a range of AIDs, starting from value of ‘Starting_AID’ field
  Scheduled STAs select a tone set according to STA’s RU_TONE_SET_INDEX ([1] table 27-32), and modulate tones of the tone set according to the FEEDBACK_STATUS (0/1) to emit.
Later, based on received NDP feedbacks, AP may solicit (e.g. via Basic TF for UL MU) some responding STAs
Illustration:
e.g. Feedback is 0
e.g. Feedback is 1

## Slide 13: NFRP TF format (802.11ax)
340

## Slide 14: RA-NFRP Advantages
Fully compliant with legacy 802.11ax format :
  Keep 11ax design format
    ‘Starting AID’ field takes value 0 (optionally 2047…), any predefined AID value outside the range of AID assigned by AP to associated stations
Very efficient random-access mechanism
  random access is moved to the short time NDP Feedback report procedure
  AP schedules only used RU Tone Set:
    no empty data RUs are met in the subsequent UL MU operation
    Possibly still collisions on UL data RU, but half of the collisions compared to UORA(case C of previous slide)
Tips:
  AP later determines the STA AID (at final stage upon receiving HE TB data PPDU), but this is not an issue.

## Slide 15: RA-NFRP TF format
B0 B5 | B6 | B7 | B8
Reserved | … | EHT | HE
Bits: 6 | 1 | 1 | 1
TF Techno bitmap
Value | Description
0 | Resource request
1 | Universal request
2-15 | Reserved
  Keeping conventional Feedback Type (0) or this new value (1) is TBD
This field tells
the inquired technology.

## Slide 16: Reference
[1]. Draft P802.11ax_D8.0
[2].