## Slide 1: Discussion of Frequency and Time Domain Attack
Date: 2020-12-08
Authors:

## Slide 2: PHY Security
Attacker tries to modify the measured range
  Make STA appear closer to AP to fake proximity detection
  Spoof time-stamps t2 or t4 to achieve that
Focus on physical layer attack
  Assume that MAC level is authenticated/encrypted
  Includes time-stamps t1/t4 feedback to initiator

## Slide 3: Integrity Attack Scenario
First line security
  Use secure LTF (sequence unknown to attacker)
  Replace Cyclic Prefix (CP) with zero-padded Guard Interval (to reduce structure)
Attack types
  Frequency Domain/ Computational attack: attacker observes fraction of symbol and predicts the rest to attack the later part
  Time Domain/MMSE Attack: attacker continuously observes and attacks using low pass nature of baseband signal

## Slide 4: Frequency Domain/Computational Attack
Steps
  Attacker will listen to first half portion of LTF
  Then try to estimate the full time-domain LTF waveform (typically by estimating frequency QAM symbols)
  Change measured t2 or t4 by transmitting the last (estimated) quarter of time-domain LTF waveform with timing advance
Advantages:
  High received SNR (listen only)
  Processing delay of 100 ns okay
Disadvantages
  Attack correlation limited by attack duration
  Receiver will notice poor SINR if boost power
First half
Last quarter
Waveform for channel measurement
Waveform transmitted by attacker
Timing advance
6.4 µs

## Slide 5: Time Domain/MMSE Attack
Steps
  Attacker will try to predict the waveform sample-by-sample
  Use finite bandwidth of signal and pulse shape/sidelobes
  Subtract out predicted symbols
  Start tx attack, while rx more data
Advantages
  Can attack large part of symbol
  Does not depend on finite constellation
Disadvantages
  Needs full duplex, limits receive SNR
  Needs to account for inter-symbol-interference
  Can only change RTT by prediction time (less proc. Delay)
Measure here
Attack here
Maximum RTT
effect

## Slide 6: Example: Computational Attack
Setup
  40 MHz, overlap-add receiver
  LTF with random QPSK symbols
  Observation period 50%
Observations
  First half of time domain, contains information about all symbols
  Intercarrier-interference (ICI) between neighboring symbols

## Slide 7: Frequency Domain/Computational Attack
Attack challenge
Partial observation of OFDM symbol leads to ICI
Without removing ICI, SINR is around 0 dB
Attacker can apply Viterbi or Sphere decoder
Counters
Move to high order constellation, e.g., 64 QAM
Use “poor” constellation to increase decoding errors
Remove structure in frequency domain, e.g., random Gaussian modulation or DFT precoded modulation

## Slide 8: Modulation examples
64 QAM – equal minimum distance
64 QAM + 4PSK

## Slide 9: Performance Results
Simulate different modulation
One repetition
18 dB SNR
MMSE-frequency channel estimation
MUSIC based and FFT based

## Slide 10: Window Design – Rectangle
HE20 2x Subcarriers
No Window (rectangular, β=0)
Time domain
Equivalent “Pulse shaper”
First sidelobe at 0.2
Floor at 0.01

## Slide 11: Window Design – Raised Cosine
HE20 2x Subcarriers
Raised cosine (β=0.3)
Time domain
Equivalent “Pulse shaper”
First sidelobe at 0.2
Floor at 0.01

## Slide 12: Window Design – Dual Raised Cosine
HE20 2x Subcarriers
Dual raised cosine (outside β=0.3, inside β=0.1)
Time domain
Equivalent “Pulse shaper”
First sidelobe at 0.27
No more floor

## Slide 13: Window Design – Flattop
HE20 2x Subcarriers
Flattop window (truncated at 0.5)
Time domain
Equivalent “Pulse shaper”
First sidelobe at 0.15
Floor at 0.01

## Slide 14: Window Design – Combined?
HE20 2x Subcarriers
Flattop window + DC (β=0.1)
Time domain
Equivalent “Pulse shaper”
First sidelobe at 0.2
Floor lowered

## Slide 15: Window Design – Trimmed Raised Cosine
HE20 2x Subcarriers
Dual raised cosine (β=0.5, β=0.1), cut at 0.5
Time domain
Equivalent “Pulse shaper”
First sidelobe at 0.15
Floor at 0.01

## Slide 16: Conclusion
Presented Discussion on Frequency and Time Domain Attack
Frequency Domain Attack can be Averted
  Use higher order constellation
  Use “poor” constellation to increase decoding errors
  Use random Gaussian modulation or DFT precoded modulation
Time Domain Attack needs further study
  Well known trade-offs in window/pulse design
    Main pulse width
    First sidelobes
    Exponential decay
  Effect on performance?