## Slide 1: Clarification of 80 MHz operation in wider-BW OFDMA
Date: 01/04/2021
Authors:

## Slide 2: Abstract
11be 80 MHz operating STAs are expected to be able to participate in OFDMA transmissions with bandwidth > 80 MHz
Some requirements for 80 MHz operating STAs in wider BW OFDMA are ambiguous
Processing of preamble in non-primary 80 MHz may be different from processing in primary 80 MHz
  Is this intentional/desirable?

## Slide 3: 80 MHz operating STA in 11be – status
80 MHz operating STAs are required to support participation in 160 MHz and 320 MHz OFDMA
  80 MHz could be primary or non-primary 80 MHz
Support for operation in non-primary 80 MHz is expected
  Full extent TBD
RU allocation to 80 MHz operating STAs could be outside the primary 80 MHz
STA is not required to process more than one 80 MHz segment for preamble decoding

## Slide 4: Supporting agreements
From SFD:
  802.11be supports that 80 MHz and 160 MHz operating STA shall be able to participate in a higher BW DL and UL OFDMA transmission.
    STA shall be able to decode the preamble and its assigned RU (some restrictions TBD).
    No capability bit as in 802.11ax.
    [Motion 115, #SP75, [1]]
  A STA only needs to process up to one 80 MHz segment of the pre-EHT preamble (up-to and including EHT-SIG) to get all the assignment information for itself.
    No 80 MHz segment change is needed while processing L-SIG, U-SIG and EHT-SIG.
    [Motion 111, #SP0611, [2]]

## Slide 5: Supporting text in 11be D0.2

## Slide 6: Issue 1: operation on non-secondary 80 MHz
Is support for operation in non-secondary 80 MHz mandatory?
  Current agreements are somewhat ambiguous:
    Participation in wider BW is mandatory
    No clear statement on operation outside of primary 80
    “Some restrictions TBD”
What, if any, MAC agreements are needed?

## Slide 7: Issue 2: preamble processing in non-primary 80 MHz
For an 80 MHz operating STA in a secondary 80 MHz, there is no guaranteed 20 MHz channel to decode U-SIG and learn about possible puncturing in the 80 MHz channel
  By contrast, in primary 80 MHz, the primary 20 MHz is always present
  Could mean different processing in primary 80 MHz vs. secondary 80 MHz
    Especially with puncturing, this adds processing complexity
  STA is not expected to process more than its 80 MHz channel

## Slide 8: Possible scenarios for non-primary 80 preamble processing
How does the 80 MHz operating STA deal with puncturing in its (non-primary) 80 MHz channel?
  Blindly determines a 20 MHz channel that is not punctured
  Disallow puncturing in non-primary 80 MHz of wider band OFDMA transmission if it includes 80 MHz-operating STAs parked there
  Indicate “guaranteed” 20 MHz channel in non-primary 80 MHz as part of e.g. SST setup
    Equivalent of a primary 20 MHz in the primary 80 MHz

## Slide 9: 160 MHz operating STAs
Similar discussion and questions need to be resolved for 160 MHz operating STAs

## Slide 10: Strawpoll
With regards to puncturing, which approach do you prefer for 80 MHz STAs operating in a non-primary 80 MHz channel?
  Option 1: STA autonomously finds a 20 MHz channel that is not punctured, without explicit information
  Option 2: Disallow puncturing in non-primary 80 MHz of wider band OFDMA transmission that includes 80 MHz-operating STAs in the non-primary 80 MHz
  Option 3: Provide a “guaranteed non-punctured” 20 MHz channel for 80 MHz-operating STAs in the non-primary 80 MHz
NOTE: SP for information only, not for SFD

## Slide 11: References
[1] Ron Porat (Broadcom), “Mandatory larger BW support,” 20/0796r1, June 2020.
[2] Sameer Vermani (Qualcomm), “U-SIG structure and preamble processing,” 20/0380r0, March 2020.