## Slide 1: Definitions and scenarios of the WLAN sensing
Date: 2021-01-12
Authors:
Name | Affiliation | Address | Phone | Email
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | Ray.du@Huawei.com
Meihong Zhang |  |  |  | 
Yingxiang Sun |  |  |  | 
Chenchen Liu |  |  |  | 
Danny Tan Kai Pin |  |  |  | 

## Slide 2: Outline
Abstract
Definitions of WLAN sensing
  Roles of WLAN sensing
  Related terms in WLAN sensing
  Sensing session
  Sensing phases
  Sensing types
Scenarios of WLAN sensing
Summary
References
Rui Du, et al. (Huawei)

## Slide 3: Abstract
Rui Du, et al. (Huawei)
WLAN sensing definitions and scenarios have been discussed in previous contributions[1-5].
In this contribution, the definition of sensing roles, related terms, sensing session and sensing types are shown and discussed. Different with previous contributions, some new terms for WLAN sensing have been proposed and discussed.
Based on the definition we discussed, different WLAN sensing scenarios are introduced.

## Slide 4: Definition of roles WLAN sensing
Rui Du, et al. (Huawei)
Roles in the WLAN sensing
Sensing initiator
Device who initiates the sensing session and wants the sensing results. It is not mandatory for the sensing initiator to participate in the sensing measurement or processing.
If sensing initiator also is sensing transmitter or receiver, it is a non-standalone initiator.
If sensing initiator is neither sensing transmitter nor receiver, it is a standalone initiator.
Sensing transmitter
Device who transmits sensing illumination signal to illuminate the area of interest.
Sensing receiver
Device who receives echo signal and measure the area of interest.
Sensing processor
Device who processes the sensing measurements and gets sensing result.
Sensing processor could be the same device with sensing initiator, which means sensing measurements are processed at sensing initiator.
Sensing processor also could be different device with sensing initiator(could be sensing transmitter and/or receiver), which means sensing measurements are processed and the sensing result is feedback to sensing initiator.
During the sensing session, there could be more than one sensing processor.
Note: the roles discussed here are functions rather than fixed roles of stations.

## Slide 5: Definition of related terms in WLAN sensing
Rui Du, et al. (Huawei)
Signals in the WLAN sensing
Illumination signal
The illumination signal is transmitted by a sensing transmitter to illuminate the area of interest.
The illumination signal could be non-dedicated illumination signal in the environment(un-coordinated or passive mode).
Echo signal
The echo signal is the signal received at the sensing receiver which contains the information of the area of interest.
Results in the WLAN sensing
Sensing measurement
The sensing measurement is the measurement of the area of interest（e.g. raw CSI, received radar signal）.
Sensing result
The sensing result is the result after signal processing at the sensing processor(e.g. compressed CSI, range-Doppler map, range-time map).

## Slide 6: Definition of sensing session
Sensing session
Sensing session is a process includes three phases, i.e. sensing negotiation, sensing measurement and sensing feedback.
Sensing session is initiated by a sensing initiator. The station who wants the sensing result is the sensing initiator and will initiate the sensing session.
During the sensing session, some of the sensing roles discussed in slide 4 would participate in the session.
Rui Du, et al. (Huawei)

## Slide 7: Definition of sensing session(Cont’d)
Three phases are defined as follows.
Sensing negotiation
During the negotiation phase, initiator negotiates with the station who will participate in the sensing session and identifies the transmitter, receiver and processer.
Sensing measurement
During the measurement phase, sensing transmitter transmits the illumination signal to illuminate the area of interest, sensing receiver receives the echo signal to measure the area of interest.
Sensing feedback
During the feedback phase, two kinds of information could be feedback to the initiator.
If the sensing initiator also is the sensing processor, sensing measurement(s) will be feedback to the initiator and processed to get the sensing result.
If the sensing initiator is not the sensing processor, sensing measurement(s) will be sent to the sensing processor and the sensing result will be feedback to sensing initiator.
Rui Du, et al. (Huawei)

## Slide 8: Definitions of sensing types
The transmitter and receiver do not need to be synchronized.
Coordinated
Sensing transmitter(s) will be involved in the sensing session and would transmit illumination signal to illuminate the area of interest. The sensing receiver receives the echo signal to measure the area of interest.
Un-coordinated
There is no dedicated sensing transmitter involved in the sensing session and the sensing receiver measures the area of interest by receiving the illumination signal in the environment.
Rui Du, et al. (Huawei)
CSI based sensing
The transmitter and receiver are usually synchronized (usually ask for much higher synchronization performance than wireless communication, e.g. STF ).
Active radar (coordinated)
Sensing transmitter(s) will be involved in the sensing session and would transmit illumination signal to illuminate the area of interest. The sensing receiver receives the echo signal to measure the area. There could be different geometries for active radar, e.g.
Monostatic radar
Bistatic radar
Multistatic radar
Passive radar (un-coordinated)
There is no dedicated sensing transmitter involved in the sensing session and the sensing receiver measures the area of interest by receiving the illumination signal in the environment. Although the transmitter and receiver are not synchronized in the passive radar, the reference signal channel and echo signal channel at the receiver are synchronized.
Radar based sensing

## Slide 9: Scenarios of WLAN sensing
Rui Du, et al. (Huawei)
January 2021
The scenarios of WLAN sensing are quite complicated and we classify them into different categories.
Each individual scenario is further discussed in the following slides.

## Slide 10: Scenarios of WLAN sensing 1-1 Coordinated CSI based sensing(one transmitter and one receiver)
Rui Du, et al. (Huawei)
STA1 is the sensing initiator, sensing receiver and sensing processor(non-standalone initiator).
STA2 is the sensing transmitter.
STA1 initiates the sensing session, STA2 transmits the illumination signal and STA1 receives the echo signal to measure the area of interest.
Sensing measurement is processed at STA1 to get the sensing result(left figure).
If STA1 is standalone initiator, sensing measurement could be sent to STA1(STA1 also is the processor, middle figure), or the sensing result could be sent to STA1(STA1 has limited computation ability and STA2 is the processor, right figure).
STA1 is the sensing initiator and sensing transmitter(non-standalone initiator).
STA2 is the sensing receiver.
STA1 initiates the sensing session, transmits the illumination signal and STA2 receives the echo signal to measure the area of interest.
Sensing measurement is feedback to and processed at STA1 to get the sensing result(left figure).
If STA1 has limited computation ability, sensing measurement is processed at STA2 and the sensing result is feedback to STA1(right figure).
Also could be extended to standalone sensing initiator.

## Slide 11: Scenarios of WLAN sensing 1-2 Coordinated CSI based sensing(multi transmitter or multi receiver, participators are transmitters or receivers)
Rui Du, et al. (Huawei)
STA1 is the sensing initiator, sensing receiver and sensing processor(non-standalone initiator).
STA2 and STA3 are the sensing transmitters.
STA1 initiates the sensing session, STA2/STA3 transmit the illumination signal and STA1 receives the echo signal to measure the area of interest.
Sensing measurements are further processed at STA1.
If STA1 has limited computation ability, sensing measurements could be sent somewhere for further processing.
If STA1 is standalone initiator, sensing measurements could be sent to STA1(STA1 also is the processor, middle figure), or the sensing result could be sent to STA1(STA1 has limited computation ability and STA2 is the processor, right figure).
STA1 is the sensing initiator and sensing transmitter.
STA2 and STA3 are the sensing receivers.
STA1 initiates the sensing session, STA1 transmits the illumination signal and STA2/STA3 receive the echo signal to measure the area of interest.
Sensing measurements are feedback to STA1 for further processing(left figure, STA1 is the sensing processor).
If STA1 has limited computation ability, sensing measurements could be sent somewhere(e.g. STA2, STA2 is the sensing processor) for further processing and sensing result could be feedback to STA1 (right figure).
Also could be extended to standalone sensing initiator.

## Slide 12: Scenarios of WLAN sensing 1-3 Coordinated CSI based sensing(multi transmitter or multi receiver, participators are transmitters and receivers)
Rui Du, et al. (Huawei)
STA1 is the sensing initiator, sensing receiver and sensing processor(non-standalone initiator).
STA2 is the sensing transmitter.
STA3 is the sensing receiver.
STA1 initiates the sensing session, STA2 transmits the illumination signal and STA1/STA3 receive the echo signal to measure the area of interest.
Sensing measurements of STA2 to STA3 are feedback to STA1 and sensing measurements are processed at STA1(left figure).
If STA1 has limited computation ability, the measurements could be sent to somewhere(e.g. STA2) for further processing and the sensing result will be feedback to STA1(middle figure).
If STA1 has limited computation ability, the measurements could be sent to somewhere(e.g. STA3) for further processing and the sensing result will be feedback to STA1(right figure).
Also could be extended to standalone sensing initiator.

## Slide 13: Scenarios of WLAN sensing 2 Un-coordinated CSI based sensing
Rui Du, et al. (Huawei)
STA1 and STA2 are communicating.
STA3 is the sensing initiator, sensing receiver and sensing processor.
In un-coordinated CSI based sensing, STA3 receives the communication signal passively to measure the area of interest.
Sensing measurement is processed at STA3 to get the sensing result.
If STA3 is standalone initiator, the sensing measurement could be sent to STA3(STA3 also is the processor, middle figure), or the sensing result could be sent to STA3(STA3 has limited computation ability and STA4 is the processor, right figure).
STA1 and STA2 are communicating.
STA3 is the sensing initiator, sensing receiver and sensing processor.
STA4 is the sensing receiver.
In un-coordinated CSI based sensing, STA3 and STA4 receive the communication signal passively to measure the area of interest.
The measurements are processed at STA3 to get the sensing result.
Similarly, if the initiator has limited computation ability, the measurements could be sent to somewhere else(e.g. STA4) for further processing and sensing result will be feedback to STA3.
Also could be extended to a standalone sensing initiator.

## Slide 14: Scenarios of WLAN sensing 3-1 Active radar sensing(one monostatic radar)
Rui Du, et al. (Huawei)
STA1 is the sensing initiator, sensing transmitter, sensing receiver and sensing processer(non-standalone initiator).
STA1 transmits the illumination signal and receives the echo signal to measure the area of interest. The measurement is processed at STA1 to get the sensing result.
STA1 is the sensing initiator and sensing processor(standalone initiator).
STA2 is the sensing transmitter and sensing receiver.
STA2 transmits the sensing illumination signal and receives the sensing echo signal to measure the area of interest.
Sensing measurement is sent to STA1(initiator) for signal processing to get the sensing result(left figure).
If STA1 has limited computation ability, sensing measurement is processed at STA2 and the sensing result is feedback to STA1(standalone initiator, right figure).

## Slide 15: Scenarios of WLAN sensing 3-2 Active radar sensing(multi monostatic radars)
Rui Du, et al. (Huawei)
STA1 is the sensing initiator, sensing transmitter, sensing receiver and sensing processor(non-standalone initiator).
STA2 is the sensing transmitter and sensing receiver.
STA1 and STA2 transmit the sensing illumination signal and receive the sensing echo signal to measure the area of interest.
The sensing measurements are sent to STA1(initiator) for further processing to get the sensing results.
If STA1 has limited computation ability, sensing measurements could be sent somewhere for further processing and the sensing result will be feedback to STA1.
STA1 is the sensing initiator(standalone initiator).
STA2 is the sensing transmitter and sensing receiver.
STA3 is the sensing transmitter and sensing receiver.
STA2 and STA3 transmit the sensing illumination signal and receive the sensing echo signal to measure the area of interest.
The sensing measurements will be sent to STA1 for further processing to get the sensing result(left figure).
If STA1 has limited computation ability, sensing measurements are processed at STA2 for further processing and the sensing result will be feedback to STA1(standalone initiator, right figure).

## Slide 16: Scenarios of WLAN sensing 3-3 Bistatic/multistatic radar sensing
Rui Du, et al. (Huawei)
The secnarios of bistatic radar sensing are similar with the coordinated CSI based sensing shown in slide 9.
Both non-standalone initiator and standalone initiator could be considered.
The scenarios of multistatic radar sensing are similar with the coordinated CSI based sensing shown in slide 10 and 11.
Both non-standalone initiator and standalone initiator could be considered.

## Slide 17: Scenarios of WLAN sensing 4 Passive radar sensing
Rui Du, et al. (Huawei)
STA1 and STA2 are communicating.
STA3 is the sensing initiator, sensing receiver and sensing processor.
In passive radar sensing, STA3 receives the communication signal passively to measure the area of interest.
Sensing measurement is processed at STA3 to get the sensing result.
If STA3 is standalone initiator, the sensing measurement could be sent to STA3(STA3 also is the processor, middle figure), or the sensing result could be sent to STA3(STA3 has limited computation ability and STA4 is the processor, right figure).
STA1 and STA2 are communicating.
STA3 is the sensing initiator, sensing receiver and sensing processor.
STA4 is the sensing receiver.
In passive radar sensing, STA3 and STA4 receive the communication signal passively to measure the area of interest.
The measurements are processed at STA3 to get the sensing result.
Similarly, if the initiator has limited computation ability, the measurements could be sent to somewhere else(e.g. STA4) for further processing and sensing result will be feedback to STA3.
Also could be extended to a standalone sensing initiator.

## Slide 18: Scenarios of WLAN sensing
CSI based sensing
Coordinated CSI based sensing (1)
  One transmitter and one receiver (1-1)
  Multi transmitters or multi receivers, participators are transmitters or receivers (1-2)
  Multi transmitters or multi receivers, participators are transmitters and receivers (1-3)
Un-coordinated CSI based sensing (2)
Radar based sensing
Active radar sensing (3)
  One monostatic radar (3-1)
  Multi monostatic radars (3-2)
  Bistatic/multistatic radar (3-3)
Passive radar sensing (4)
Rui Du, et al. (Huawei)

## Slide 19: Summary
Rui Du, et al. (Huawei)
In this contribution, the definition of sensing roles, related terms, sensing session and sensing types are shown and discussed.
Based on the discussion, different sensing scenarios, including coordinated CSI based sensing, un-coordinated CSI based sensing, active radar sensing and passive radar sensing have been presented and discussed.

## Slide 20: References
Rui Du, et al. (Huawei)
[1] 11-20-1849-01-00bf-wi-fi-sensing-definitions.pptx
[2] 11-20-1850-00-00bf-overview-of-wi-fi-sensing-scenarios.pptx
[3] 11-20-1805-00-00bf-discussion-on-wlan-sensing-roles.pptx
[4] 11-20-1804-00-00bf-discussion-on-wlan-sensing-procedure.pptx
[5] 11-20-1960-00-00bf-analysis-of-the-functionality-of-sensing.pptx