## Slide 1: Discussion on Special User Info field of Trigger Frame
Date: 2021-01-11
Authors:
Name | Affiliation | Address | Phone | Email
Lei Huang | OPPO |  |  | huang.lei1@oppo.com
Chaoming Luo |  |  |  | 
Pei Zhou |  |  |  | 
Liuming Lu |  |  |  | 
Aiguo Yan | zeku |  |  | 

## Slide 2: Special User Info Field
The Special User Info field has been introduced into enhanced Trigger frame [1].
The Special User Info field has two main usages:
    It carries the non-derived subfields of the U-SIG in the EHT TB PPDU to be solicited:
      PHY Version ID (3 bits)
      PPDU Bandwidth Extension (2 bits)
      Spatial Reuse 1 (4 bits)
      Spatial Reuse 2 (4 bits)
      U-SIG Reserved (12 bits)
    Its presence in a Trigger frame indicates the format of user info fields addressed to EHT STAs in R1.
      If the Special User Info field is not present in the Trigger frame, then the User Info field is the HE format
      In R1, if the Special User Info field is present in the Trigger frame, the User Info field is the EHT Format

## Slide 3: Discussion
For MU-RTS Trigger frame, since CTS frames to be solicited are transmitted in non-HT PPDU or non-HT DUP PPDU, U-SIG subfields except the PPDU Bandwidth Extension subfield carried in the Special User Info field shall be reserved.
    1-bit HE/EHT indication suggested in [2] can be used to indicate the format of user info fields addressed to EHT STAs in R1.
It seems that the Special User Info field is no longer required for the MU-RTS Trigger frame if 2-bit PPDU Bandwidth Extension subfield in the Special User Info field is moved to the common info field.
      Note: PPDU Bandwidth Extension subfield actually is not a non-derived U-SIG subfield since the BW subfield in U-SIG field needs to be derived from the UL BW subfield and PPDU Bandwidth Extension subfield in the Trigger frame.

## Slide 4: Proposal
  In order to minimize overhead of enhanced MU-RTS Trigger frame, we propose
    The 2-bit PPDU Bandwidth Extension subfield in the Special User Info field is moved to the common info field (e.g. using 2 bits of the UL HE-SIG-A2 Reserved subfield).

## Slide 5: SP 1
Do you agree the 2-bit PPDU Bandwidth Extension subfield in the Special User Info field of Trigger frame is moved to the common info field which uses 2 bits of the UL HE-SIG-A2 Reserved subfield?

## Slide 6: Reference
11-20-1935-07-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document-part-2
11-20-1808-04-00be-backward-compatible-EHT-trigger-frame-follow-up