## Slide 1: Disambiguate Trigger Frame Special User Info Field
Date: 2021-02-10
Authors:
Name | Affiliations | Address | Phone | email
Steve Shellhammer | Qualcomm |  |  | shellhammer@ieee.org
Bin Tian |  |  |  | btian@qti.qualcomm.com
Yanjun Sun |  |  |  | yanjuns@qti.qualcomm.com
Alfred Asterjadhi |  |  |  | aasterja@qti.qualcomm.com

## Slide 2: Issue
The issue is that it is possible that an EHT STA might be associated with an HE AP that assigns AID12 value 2007 to one of its STAs. And the AP locates this User Info field (2007) first in the Trigger frame
  This could lead the EHT STA to incorrectly think that this Trigger frame is soliciting an EHT TB PPDU and as such the EHT STA might generate an EHT TB PPDU in response
We need a method to disambiguate between the following two cases:
  An HE AP sending a Trigger Frame with the first User Info Field having an AID12 value of 2007
  An EHT AP sending a Trigger Frame with the Special User Info Field
Here we will propose an explicit method to disambiguate between these two cases
  The current design is based on implicit signaling (EHT STA acts as an HE STA when associated to an HE AP)

## Slide 3: Implicit Signaling Method
If the EHT STA receives a Trigger Frame and the first User Info Field after the Common Info Field has an AID12 value of 2007, then the EHT STA checks whether it is associated with an HE or an EHT AP. It then can decide as follows:
  If it is an HE AP The first User Info Field is for a STA with AID12 value of 2007
  If it is an EHT AP The first User Info Field is the Special User Info Field
This requires the EHT STA to check whether it is associated with an HE or an EHT AP
  This information is not directly provided in the Trigger Frame and requires the EHT STA to check the context of its association, which may be handled in a different part of the implementation

## Slide 4: Explicit Signaling Method
Set B39 to 1 in the Special User Info Field
  Recall that in 802.11ax B39 (Reserved Bit) is set to 0
    Exception is NFRP Trigger variant which uses B39 as a multiplexing flag
      However, this variant has 16 reserved bits which can be used
If an EHT STA receives a Trigger Frame and the First User Info Field after the Common Info Field has an AID12 value of 2007 the EHT STA checks B39 of that first User Info Field
  If B39 == 0 The first User Info Field is for a STA with AID12 value of 2007
  If B39 == 1 The first User Info Field is the Special User Info Field
Note we currently have three unused bits in the Special User Info Field
This does not require checking whether the STA is associated with an HE AP or an EHT AP

## Slide 5: Straw Poll
Do you support setting B39 in the Special User Info Field to 1?
  Note: This is to enable a receiving EHT STA to easily disambiguate between the Special User Info Field and the case where an HE AP sends a Trigger Frame with the first User Info Field addressed to a STA with an AID12 value of 2007?