## Slide 1: Dicussion on HE or EHT variant differentiation of a trigger frame
Date: 2021-03-03
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | ming.gan@huawei.com
Mengshi Hu | Huawei |  |  | humengshi@Huawei.com

## Slide 2: Background
  The following motions or SP have passed regarding trigger frame:
  In R1, an 1-bit HE/EHT indication in the common part of the Trigger frame is used to indicate to the EHT STA whether to transmit an HE or EHT TB PPDU within the primary 160 MHz.
  Use B54 (the first bit) of UL HE-SIG-A2 Reserved field to carry this HE/EHT indication.
  NOTE – The EHT STA shall not transmit an HE TB PPDU on the secondary 160 MHz.
  [Motion 150, #SP384, [92] and [316]][#M19]
  If the Special User Info field is not present in the Trigger frame, then the User Info field is the HE format and the EHT STA transmits an HE TB PPDU.
  In R1, if the Special User Info field is present in the Trigger frame, the User Info field is the EHT Format and the EHT STA transmits an EHT TB PPDU.
  [Motion 150, #SP369, [92] and [322]][#M21]
  B39 in a User Info field addressed to an EHT STA within a Trigger frame is the Primary/Secondary 160 (PS160) subfield.
  • NOTE – The PS160 subfield, along with B7-B0 of the RU Allocation subfield, specify the RU/MRU.
  [Motion 150, #SP380, [92] and [324][#M25]
  Do you support using B55 of the Common Info Field to indicate the presence of the Spacial User Info Field in the Trigger Frame?
  • B55 is set to 1 to indicate that there is no Special User Info field in the Trigger frame.
  • B55 is set to 0 to indicate that the Special User Info field is present in the Trigger frame.
  Straw poll #393 [#SP393]

## Slide 3: HE or EHT differentiation discussion
A-PPDU is not supported in R1. Hence, in the PDT (21/0259r3), it is said
  If the BaselineMACFeaturesOnly capability is 1 then an EHT AP shall not transmit a Trigger frame that solicits both an HE TB PPDU and an EHT TB PPDU.(#M2 )
In this case, there is some redundancy or dependency of several bits from the AP side:
  B54 in common field: HE/EHT P160
  B55 in common field: presence of special user field
There are some comments to state the dependency of the two bits for R1, which is reasonable from the AP side..
At the STA side, as there are some dependency at the Tx side, several methods have been mentioned to decide HE or EHT variant, or we can say to decide HE or EHT TB PPDU.

## Slide 4: HE or EHT – Method 1
Several methods include:
  Method 1: rely on B55 in common field: presence of special User field
  Method 2: rely ONLY on B54 in common field: HE/EHT P160
  Method 3: rely on BOTH B54 in common field and B39 in User field (PS160 for EHT variant and reserved for HE variant)
We will talk about each method and show why Method 3 should be applied.
Method 1: B55=0, special User field is present, then User field is EHT variant; B55=1, special User field is not present, then User field is HE variant.
Issue of method 1: later in R2, a R2 AP sends a trigger frame which solicits both HE TB PPDU and EHT TB PPDU, in this case, the AP will set B55=0. In this case, a R1 EHT STA (which is also an HE STA) will think all User fields are EHT variant, and hence this EHT STA cannot be solicited to transmit HE TB PPDU within A-PPDU, even worse than an old HE STA, which can participate in A-PPDU.

## Slide 5: HE or EHT – Method 2
Method 2: B54=0, EHT PPDU in P160, then User field is EHT variant; B55=1, HE PPDU in P160, then User field is HE variant.
Issue of method 2: although in R1, we restrict AP to send trigger to solicit A-PPDU. Whilst we don’t want to exclude the possiblity where a R1 STA could later transmit EHT PPDU within A-PPDU, solicited by a R2 AP in R2 stage. The transmission could be transparent to a R1 STA.
For example, later in R2, the UL BW is set to 3 (160MHz), UL BW Extension is set to 2 (320MHz-1), then a R2 AP could solicit HE PPDU in P160 and EHT PPDU in S160 with B54=1 indicating HE TB PPDU in P160, and B55=0, the special User field is present.
In this case, a R1 EHT STA will think all User fields are HE variant, and hence this EHT STA cannot be solicited to transmit EHT TB PPDU.

## Slide 6: HE or EHT – Method 3
Method 3: rely on both B54 in common field and B39 in User field (PS160 for EHT variant and reserved for HE variant)
  B54=1, HE PPDU in P160, then a User field in HE variant if B39 is 0 (P160 or reserved)
  B54=1, HE PPDU in P160, then a User field is EHT variant if B39 is 1 (S160, valid only for 320MHz case)
  B54=0, EHT PPDU in P160, then a User field is EHT variant regardless of B39.
Rewriting method 3 in a simple way:
  B54 of common field = 1, B39 of a User field = 0, then HE variant;
  Otherwise, EHT variant.
Same example as before: later in R2, the UL BW is set to 3 (160MHz), UL BW Extension is set to 2 (320MHz-1), then a R2 AP could solicit HE PPDU in P160 and EHT PPDU in S160 with B54=1 indicating HE TB PPDU in P160, and B55=0, the special User field is present.
In this case, a R1 EHT STA can be solicited to transmit either HE TB or EHT TB PPDU depending on AP’s schedule.

## Slide 7: HE or EHT Method 3 (cont’d)
Even later, we find some potential interoperability issue in R2, we can still disallow a R2 AP to solicit EHT TB PPDU or HE TB PPDU from a R1 EHT STA by restriciting the AP’s behavior. But we should not prevent this from happening in R1 stage by wrongly describe the STA’s behavior regarding HE or EHT differentiation.
In this proposal, no additional bits are proposed, method 3 only relies on the existing bits in the trigger frame.

## Slide 8: Straw Poll #1
  Do you agree the following description regarding HE or EHT variant User info field differentation?
  B54 of common info field = 1, B39 of a User info field = 0, then HE variant;
  Otherwise, EHT variant.
  Note:
    B54 of common info field is HE/EHT P160
    B39 in User info field is PS160 for EHT variant and reserved for HE variant
  Y
  N
  A

## Slide 9
[1] https://mentor.ieee.org/802.11/dcn/20/11-20-1935-19-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document-part-2.docx
[2] https://mentor.ieee.org/802.11/dcn/21/11-21-0259-03-00be-pdt-trigger-frame-for-eht.docx
References