## Slide 1: MLO: Broadcast TWT for MLDs
Date: 2021-03-05
Authors:

## Slide 2: Abstract
In this contribution, we propose the facilitation of broadcast TWT operation for multi-link devices.

## Slide 3: Background
Broadcast TWT operation enables an AP to set up a shared TWT session for a group of STAs [1], [2]
  Allows an AP to manage activity in the BSS
  Minimize contention between STAs, minimize STAs’ awake time
For MLDs, individual TWT operation could be set up on a setup link for more than one setup links [Motion 115, #SP60].
In this contribution, we address the broadcast TWT operation for multi-link devices (MLDs)

## Slide 4: Motivation
Broadcast TWT operation for MLD can reduce the signaling overhead for TWT setup for multiple links by exchanging the TWT signaling information over a single link.
In addition, multiple MLDs can also become members of the same broadcast TWT schedule.

## Slide 5: Broadcast TWT for MLDs (1/3)
An MLD in a BSS may support broadcast TWT operation
  TWT service period (SP) for any MLD supporting TWT operation can be either trigger-based or non-trigger based
  A non-AP MLD may provide its broadcast TWT operation capabilities during ML setup
When broadcast TWT is supported by both AP MLD and non-AP MLD, an STA affiliated with the non-AP MLD may receive the Beacon frame containing the broadcast TWT element from an AP affiliated with an AP MLD on a setup link.
  The STA affiliated with the non-AP MLD on the setup link wakes up to receive the beacon frame and determines the starting time of the broadcast TWT SP.
An STA affiliated with a non-AP MLD may negotiate broadcast TWT agreements with an AP affiliated with an AP MLD on one setup link for other setup links between the AP MLD and non-AP MLD.

## Slide 6: Broadcast TWT for MLDs (2/3)
In this illustrative example, three links are setup between the AP MLD and non-AP MLD– link between AP1 and STA1, link between AP2 and STA2, and link between AP3 and STA3. Both AP MLD and non-AP MLD support broadcast TWT operation. Broadcast TWT negotiation occurs on the setup link between AP1 and STA1. After successful negotiation, broadcast TWT agreement is applied to the all three setup links.
AP1
AP2
AP3
AP1
AP2
AP3
STA1
STA2
STA3
STA1
STA2
STA3
  Broadcast TWT negotiation
  Broadcast TWT
  agreement
  AP MLD
  Non-AP MLD
  Non-AP MLD
  AP MLD

## Slide 7: Broadcast TWT for MLDs (3/3)
In this illustrative example, three links are setup between the AP MLD and non-AP MLD-A. Also, three links are setup between the AP MLD and non-AP MLD-B. Both AP MLD and non-AP MLDs support broadcast TWT operation. A broadcast TWT negotiation takes place between AP1 of AP MLD and STA1 of non-AP MLD-A. Similarly, another TWT negotiation takes place between AP1 of AP MLD and STA1 of non-AP MLD-B. After successful negotiation, same broadcast TWT agreement is established between AP1 of AP MLD and STA1 of non-AP MLD-A, AP1 of AP MLD and STA1 of non-AP MLD-B, and AP3 of AP MLD and STA3 of non-AP MLD-B.
AP1
AP2
AP3
STA1
STA2
STA3
  Broadcast TWT negotiation
  AP MLD
  non-AP MLD-A
STA1
STA2
STA3
  non-AP MLD-B
AP1
AP2
AP3
STA1
STA2
STA3
  AP MLD
STA1
STA2
STA3
  non-AP MLD-B
  Broadcast TWT
  agreement
  non-AP MLD-A

## Slide 8: Summary
In this contribution, we propose the facilitation of broadcast TWT operation for MLDs
  For any MLD, it is optional to support broadcast TWT operation
  A non-AP MLD may provide its broadcast TWT operation capabilities during ML setup
Between an AP MLD and a non-AP MLD supporting broadcast TWT operation , broadcast TWT negotiation can take place over any setup link for more than one setup links between the AP MLD and non-AP MLD
  - Broadcast TWT agreement on one setup link may be applied to other setup links between the AP MLD and non-AP MLD as well.

## Slide 9: References
[1] IEEE P802.11ax/D8.0 – 26.8.3 (Broadcast TWT operation)
[2] IEEE P802.11ax/D8.0 – 10.47 (Target Wake Time)

## Slide 10: SP 1
Do you agree that in R1:
  An MLD may support broadcast TWT operation
    Broadcast TWT negotiation can take place on any setup link between an STA affiliated with a non-AP MLD and an AP affiliated with an AP MLD that support broadcast TWT operation. The negotiation can be for more than one setup links.
    Broadcast TWT agreement on one setup link between an STA affiliated with a non-AP MLD and an AP affiliated with an AP MLD may be applied to more than one setup links between the AP MLD and non-AP MLD