## Slide 1: Preferred Link Pair
Date: 2021-03-05
Authors:
Name | Affiliations | Address | Phone | email
Wook Bong Lee | Samsung |  |  | wookbong.lee@Samsung.com
Steve Jones | Samsung |  |  | 
Srinivas Kandala | Samsung |  |  | 

## Slide 2: Introduction
In this contribution, we propose a preferred link pair to enable better STR operation

## Slide 3: How much isolation do we need? (1/2)
Transmitter Noise
  We assume that the transmit and receive channels will be spaced apart such that the OOB modulation noise from the transmit is below the thermal noise of the transmit chain at full power. Let us take this to be 5x channels offset.
  At this point, a well-designed 802.11 transmit chain should generate less than -55dBm/MHz of noise at max transmit power, which is +59dB above thermal noise at room temp.
Receiver Noise Floor
  802.11 minimum receiver sensitivity requirements can be met with a receiver NF of 15dB using modern modem technology.
  A receiver NF of 15dB equates to -99dBm/MHz noise floor at room temp.
  Most implementations have an equivalent receiver NF of around 3dB to 5dB.

## Slide 4: How much isolation do we need? (2/2)
Isolation Estimate
  We need to leave some margin for receiver blocking effects from the transmit signal (see next bullet).
  If we divide up desensitization from receiver blocking and transmit noise equally, then the maximum allowable noise at the receiver input will be (-99dBm) – (3dB) = -102dBm/MHz, which gives an equivalent receiver NF of 12dB.
  So the isolation needed is (-55dBm/MHz) – (-102dBm/MHz) = 47dB.
Receiver Blocking
  The desensitization in the receiver sensitivity in the presence of the -31dBm blocker, must equate to an receiver NF of <12dB. For a typical implementation of receiver NF in the range 3-5dB, this gives 7-9dB of allowable desensitization due to receiver blocking.
Effect of isolation
  Taking receiver NF < 12dB for transmit noise and receiver NF from transmit signal to <12dB, gives a total of <15dB, which should allow the modem to demodulate at the minimum receiver sensitivity levels specified in 802.11.

## Slide 5: Self Interference Rejection Techniques
There are lots of self-interference rejection schemes were developed and studied under the full-duplex system
Three categories [1]
  Wireless-propagation domain techniques
    More 30 dB isolation with on-air antenna isolation is possible, but this will reduce the number of spatial streams per link.
  Digital-domain techniques
    Bit width of ADC should be increased
  Analog-circuit-domain techniques, e.g. circulator
    Circulator can be a bit bulky for mobile phone

## Slide 6: Preferred Option (1/2)
Define four bands
  We can consider filter banks with four bands, i.e. 5L (lower 5 GHz band), 5U (upper 5 GHz band), 6L (lower 6 GHz band), and 6U (upper 6 GHz band).
Disallowing multilink channel selection in adjacent bands
  To achieve the level of isolation required with a practical filter/duplex implementation, we will need to forbid the use of adjacent bands.
  An additional benefit of this is that the passbands of each sub-band filter can be made to overlap slightly with the adjacent bands, which ensures that we don’t lose performance on any of the channels that occur at the top and bottom of the sub-bands.
  Although the submission has focused on STR, as this is the most demanding case, the isolation levels estimated here will be sufficient for STT operation as well.
  For this mode, it is important to consider isolation for reducing inter and cross-modulation effects from the two transmit paths, which can degrade spectral mask and EVM.

## Slide 7: Preferred Option (2/2)
Allowed band pairs are 5L + 6L, 5L + 6U, and 5U + 6U
One example implementation choice for 5L + 6L
  For each antenna, two transmit and two receive chains are connected to filters for 5L and 6L.
  High band and low band can be combined onto the antenna via a high-pass/low-pass diplexer.
  Other arrangements of filters/diplexers and switches can be used which does not fundamentally change the combinations of channels/bands that can be supported concurrently.

## Slide 8: Proposal
Define preferred link pair
  One link using a channel in 5L and the other using a channel in 6L
  One link using a channel in 5L and the other using a channel in 6U
  One link using a channel in 5U and the other using a channel in 6U
  One link using a channel in 2.4 GHz and the other using a channel in one of 5L, 5U, 6L, and 6U
  Where
    5L: U-NII-1 and U-NII-2A (from 5170 MHz to 5330 MHz)
    5U: U-NII-2C, U-NII-3 and U-NII-4 (from 5470 MHz to 5895 MHz)
    6L: U-NII-5 (5945 MHz to 6425 MHz)
    6U: U-NII-6 to U-NII-8 (6425 MHz to 7125 MHz)

## Slide 9: SP #1
Do you support to define preferred link pair as follows?
  Preferred link pair
    One link using a channel in 5L and the other using a channel in 6L
    One link using a channel in 5L and the other using a channel in 6U
    One link using a channel in 5U and the other using a channel in 6U
    One link using a channel in 2.4 GHz and the other using a channel in one of 5L, 5U, 6L, and 6U
    Where
      5L: U-NII-1 and U-NII-2A (from 5170 MHz to 5330 MHz)
      5U: U-NII-2C, U-NII-3 and U-NII-4 (from 5470 MHz to 5895 MHz)
      6L: U-NII-5 (5945 MHz to 6425 MHz)
      6U: U-NII-6 to U-NII-8 (6425 MHz to 7125 MHz)
  Y/N/A

## Slide 10: Reference
[1] A. Sabharwal et al., “In-Band Full-Duplex Wireless: Challenges
and Opportunities,” IEEE Journal On Selected Areas In Communications, vol. 32, no. 9, Sept. 2014