## Slide 1: RA-RU Indication in Trigger frame
Authors:
Date: 2021-03-10

## Slide 2: Introduction
According to the SFD, 11be has agreed the followings [1]:
  An AP may allocate an RA-RU to solicit a response in an EHT TB PPDU.
  In a Trigger frame that solicits an EHT TB PPDU, a Special User Info field is placed immediately after the Common Info field and …
If a Trigger frame soliciting EHT TB PPDUs indicates RA-RUs as defined in 11ax with the Special User Info, HE STAs can also respond on the RA-RUs with an HE TB PPDU [2].
This contribution discusses possible solutions to solicit EHT TB PPDUs on RA-RUs.

## Slide 3: Problem
In 11ax, an RA-RU is indicated by the User Info field with its AID12 subfield set to 0 or 2045.
Even when the Special User Info is included to solicit EHT TB PPDUs, HE STAs may respond to the User Info field with AID12 set to 0 or 2045 with an HE TB PPDU.
Following slides show potential solutions for this problem.
  Method 1 indicates an RU-RU with a new AID12 value.
  Method 2 includes the AID12 subfield set to 4095 before the RA-RU indication.
MAC header | Common Info | Special User Info (AID12: 2007) | User Info 1 | User Info 2 (AID12: 0) | Padding | FCS
HE STAs may respond on RA-RU indicated by User Info 2 using HE TB PPDU.

## Slide 4: Proposed solutions (1)
Method 1: To define a new AID12 subfield value (e.g., 2047) indicating RA-RUs to solicit an EHT TB PPDU
  HE STAs cannot recognize the new value as a value indicating RA-RUs.
  The Trigger frame soliciting EHT TB PPDUs should not include User Info fields with AID12 of 0 or 2045 in R1.
    The Trigger frame soliciting HE TB PPDUs only should not include User Info fields with AID12 set to the new value.
  An EHT STA can maintain a single OBO counter and decrease it for RA-RUs indicated by AID12 of 0, 2045 and the new value.
MAC header | Common Info | Special User Info (AID12: 2007) | User Info 1 | User Info 2 (AID12: New value indicating RA-RU) | Padding | FCS

## Slide 5: Proposed solutions (2)
Method 2: To include the User Info field with its AID12 subfield set to 4095 before the User Info field indicating RA-RUs to solicit EHT TB PPDUs
  AID12 of 4095 is the value indicating the start of the Padding field.
    HE STAs cannot continue to parse User Info fields after the User Info field with AID12 of 4095.
  In R1, the Trigger frame soliciting EHT TB PPDUs should not include the User Info field indicating RA-RUs before the User Info field with AID12 of 4095.
  The length of the User Info field with AID12 of 4095 is the same with other User Info fields included in the same Trigger frame.
  AID12 of 4095 can still be used for the Padding field.
    AID12 of 4095 for spoofing can be indicated by the other subfield in the same User Info field.
MAC header | Common Info | Special User Info (AID12: 2007) | User Info 1 | User Info 2 (AID12: 4095) | User Info 3 (AID12: 0) | Padding | FCS

## Slide 6: Comparison of two methods
Method 1 does not require the additional User Info field as in Method 2.
  The Trigger frame may be shorter when using Method 1.
In Method 2, a non-AP STA does not need to check the additional AID12 value.
  In Method 1, a non-AP STA needs to check three AID12 values (its own AID, 0, and new value).
  In Method 2, a non-AP STA needs to check two AID12 values (its own AID, and 0).
  HE STAs will not parse the remaining User Info fields after AID12 of 4095.
MAC header | Common Info | Special User Info (AID12: 2007) | User Info 1 | User Info 2 (AID12: New value indicating RA-RU) | Padding | FCS
MAC header | Common Info | Special User Info (AID12: 2007) | User Info 1 | User Info 2 (AID12: 4095) | User Info 3 (AID12: 0) | Padding | FCS
* Method 1: New AID12 value
* Method 2: AID12 of 4095

## Slide 7: Conclusion
This contribution proposed signaling methods to indicate RA-RUs when soliciting an EHT TB PPDU.
Method 2 may be more preferable considering the non-AP side operation.

## Slide 8: References
[1] 11-19/1262r23 Specification Framework for TGbe
[2] 11-20/1192r1 TB PPDU Format Signaling in Trigger Frame

## Slide 9: Straw poll 1
Which option do you prefer between method 1 and method 2 to solicit EHT TB PPDUs using UORA?
  Method 1: To define a new AID12 value indicating RA-RUs
  Method 2: To include the User Info field with AID12 subfield of 4095 before the User Info field indicating RA-RUs

## Slide 10: Straw poll 2-1
Do you agree that RA-RUs soliciting EHT TB PPDUs are indicated by the AID12 subfield set to TBD value which is not 0 or 2045?
  Y/N/A

## Slide 11: Straw poll 2-2
Do you agree that the Trigger frame can include the User Info field with its AID12 subfield set to 4095 before the User Info field indicating RA-RUs to be responded with an EHT TB PPDU?
  Y/N/A