## Slide 1: Sensing session and reuse of .11az
Date: 2021-03-22
Authors:

## Slide 2: Abstract
Sensing session establishment, Sensing measurement and Sensing reporting using existing MAC/PHY features of 802.11az, 802.11ad, and 802.11ay amendments

## Slide 3: Preliminary investigation
WLAN sensing measurement collects channel state information from 802.11 compatible PPDUs
WLAN sensing is unidirectional, and the measurement is performed by the Sensing Receiver
While in the coordinated measurement, the sensing measurement participants may be in the roles of sensing initiator, responder, transmitter, and receiver
One initiator may coordinate multiple responders
TB and non-TB approaches may be applicable for the WLAN sensing

## Slide 4: TB sensing and non-TB sensing
Non-AP as an Initiator in the non-TB sensing same as in .11az.
AP as an Initiator in the TB sensing – mirroring of the .11az

## Slide 5: Session
Keep the Sensing session 1:1 apart of the sensing measurement, same as in FTM
Use Association/Authentication and Pre-association security negotiation (PASN) as in the 11.az
Why?
  Reuse existing solution
  Easy add/terminate transmitters/receivers
  Allows parallel sensing measurements among the same devices

## Slide 6: ID
In the TB sensing identification can be kept as in TB FTM (AP STA is defined as Initiator). In the TB sensing, one Initiator maintains sessions with multiple responders. The sessions are coordinated within one BSS.
A session is defined by
  The initiator’s identifier: the BSSID, which determines with whom the respondents are authenticated/associated
  The responder AID/RSID
A measurement can involve STAs belonging to different sessions:
  Dialog token identifies a sensing measurement
  Different measurements may involve different subset of STAs
In the non-TB sensing, the Initiator (non-AP) may switch between multiple Responders (APs) that may reside in different bands

## Slide 7: Negotiation for Sensing measurement exchange
Use the Initial FTM Request and the FTM (public frames) handshake for the Negotiation
Follow the negotiation as defined in .11az
Append WLAN Sensing specific information to the negotiation:
  Set the Transmitter and Receiver roles among Responders

## Slide 8: Comment to the motion 16
Motion 16: More than one sensing responder may participate in the measurement phase and reporting phase of a sensing session
  the meaning of the session contradicts the meaning of the FTM session
The contradiction may be resolved by following the FTM definition
  A session is defined by
    The initiator’s identifier: the BSSID, which determines with whom the respondents are authenticated/associated
    The responder AID/RSID