## Slide 1: NLTF for UL TB PPDU
Date: 2021-03-23
Authors:

## Slide 2: Extra LTF for EHT PPDU
The group agreed on the following motion for the extra LTF:
  “If extra LTF is applied to non-OFDMA transmission, the number of EHT-LTF should be chosen from the set [2 4 8], and up to 2 times of the initial NLTF for all Nss.”
  [Motion 137, #SP262]
The motion is discussed mostly in the context of MU PPDU to limit to the useful modes for Rx to support.

## Slide 3: UL TB PPDU
Non-AP STA already mandatory support transmission of up to 8 EHT-LTFs in TB PPDU with non-OFDMA
AP can trigger up to 8 LTFs in non-OFDMA TB PPDU regardless of total Nss.
  Non-AP STA is not aware of total Nss, unless it checks all User Infos in the TF.
  Transparent to non-AP STA, just spec change.
Propose to allow AP to trigger extra LTF in UL non-OFDMA transmissions.
  Channel estimation SNR gain for UL TB Rx.
  Support A-PPDU EHT-LTF and HE-LTF alignment in R2.

## Slide 4: NLTF for EHT TB PPDU
Change to the PDT text in 11-21/0114r4:
  In an EHT TB PPDU, NEHT-LTF is indicated in the Trigger frame that triggers the transmission of the PPDU. In a non-OFDMA EHT TB PPDU, NEHT_LTF may be greater than or equal to the initial number of EHT-LTF symbols, which is a function of the total number of spatial streams, NSS,total, as shown in Table 36-xx (Initial Number of EHT-LTFs required for different numbers of spatial streams). ”

## Slide 5: SP1
Do you agree that EHT allows AP to trigger UL TB PPDU in non-OFDMA mode with Number of EHT-LTF to be larger than total Nss?