## Slide 1: 802.11ax Features and Applicability to 5G and Wi-Fi Convergence
Date: 2021-04-9
Authors:

## Slide 2: Revisions
R0 : Initial draft to stimulate the discussion at the AANI SC

## Slide 3: Background
The Wireless Broadband Alliance has forwarded a liaison statement [1] to the 802.11 WG including a white paper entitiled “5G and Wi-Fi RAN Convergence”.
The liaison letter includes two specific requests:
  Need for further study within IEEE 802.11 on how fine grain QoS for 5G flows can be provided in 802.11ax and 802.11be leveraging new MAC/PHY capabilities of these standards.
  Challenges related to enabling QoS differentiation for 5G flows over WLAN access, especially if the QoS mapping is not addressed by WLAN vendor - one way to address this includes defining 5QIs to DSCP values to 802.11 User Priority mapping, considerations for supporting the device centric and network centric approaches for WLAN QoS differentiation for 5G flows based on IPsec child SAs, defining 5G QoS parameters to 802.11 User Priority and TSPEC parameters mapping and extending TCLAS element to support IPsec SA traffic.

## Slide 4: Abstract
This submission is concerned with 802.11ax features and how these may be related to WBA requirements.

## Slide 5: 802.11ax Features - I
Item | Description | Remark | Applicability to WBA Requirements
Channel Bandwidth | 20, 40, 80, 160, and 80+80 MHz | Same as in 802.11ac | 
Band of Operation | 2.4 GHz. 5 GHz, and 6 GHz | First 802.11 amendment to specify the operation in the 6 GHz band | May be easier to find vacant wider channels (e.g., 160 MHz) available for improved performance.
Waveform and Resource Units | OFDMA (UL and DL) | First 802.11 amendment to specify OFDMA transmission format | The AP may schedule flows more often than others to achieve certain performance goal (e.g. GBR). However the scheduler is implementation dependent
 | RUs = 26, 52, 106. 242, 484, 996, 2x996 subcarriers |  | 

## Slide 6: 802.11ax Features - II
Item | Description | Remark | Applicability to WBA Requirements
MU MIMO | UL and DL MU MIMO. MU MIMO allows for up to 8 users per RU. | 802.11ac supports DL MU MIMO only. | 
Trigger Frame (several Types) | Basic Trigger Frame | Triggers UL transmissions. Indicates participating STAs and RU allocation. | Scheduler is implementation dependent
 | Beam Forming Report Poll (BFRP) |  | 
 | MU-BAR |  | 
 | Buffer Status Report Poll (BSRP) | A non-AP STA delivers buffer status reports (BSRs) to assist its AP in allocating UL MU resources | Can be used as an input to the scheduler.

## Slide 7: 802.11ax Features - III
Item | Description | Remark | Applicability to WBA Requirements
Trigger Frame (several Types) | GCR MU-BAR |  | 
 | Bandwidth Query Report Poll (BQRP) | A non-AP STA may send bandwidth query reports (BQRs) to assist its AP in allocating DL MU and UL MU resources | 
 | NDP Feedback Report Poll (NFRP) |  | 
 | MU-RTS |  | 

## Slide 8: 802.11ax Features - VI
Item | Description | Remark | Applicability to WBA Requirements
Target Wake Up Time (TWT) | Individual TWT | TWT is mainly a power save mechanism | STAs may set individual TWT SP or follow the broadcast TWT schedule as advertised by the scheduling AP
 | Broadcast TWT |  | 
Spatial Reuse | OBSS PD-based spatial reuse operation | Simulation results show a throughput gain of about 20% [6] | 
 | PSR-based spatial reuse operation | ?? | 
User Experience | 4x improvement in user throughput compared to 802.11n and 802.11ac | The 4x improvement is not universal and is dependent on the traffic scenarios – see [2-5] | Gain in user throughput is dependent on scenario
MCS 10 and MCS 11 (1024 QAM) | Higher MCS values | Compared to 256 QAM in 802.11ac | 

## Slide 9: Conclusion
802.11ax has not developed any mechanisms specific to improving the QoS
  No new priority access scheme or code points
802.11ax introduced a new set of mechanisms (OFDMA, MU MIMO, etc) that may improve performance measures. The improvement is related to specific implementation and traffic scenario, which do not cover the scenarios of the WBA liaison [1].

## Slide 10: References
[1] https://mentor.ieee.org/802.11/dcn/21/11-21-0170-00-0000-2021-jan-liaison-from-wba-re-convergence.docx
[2] https://mentor.ieee.org/802.11/dcn/17/11-17-1360-00-00ax-multiple-bss-simulations-for-par-verification-follow-up.pptx
[3] https://mentor.ieee.org/802.11/dcn/17/11-17-0090-01-00ax-11ax-par-verification-using-ul-mu-mimo.pptx
[4] https://mentor.ieee.org/802.11/dcn/16/11-16-1363-01-00ax-11ax-par-verification-through-ofdma.ppt
[5] https://mentor.ieee.org/802.11/dcn/16/11-16-1198-03-00ax-preliminary-11ax-par-verification.pptx
[6] https://mentor.ieee.org/802.11/dcn/15/11-15-1109-01-00ax-obss-nav-and-pd-threshold-rule-for-spatial-reuse.pptx