## Slide 1: TGbi Proposed Issues
Date: 2021-10-14
Authors:

## Slide 2: Revision History
Revision | Date | Description
0 | 2021-04-09 | Initial version with the issue about password identifier
1 | 2021-05-10 | Added abstract, privacy issue Template and privacy use case template
2 | 2021-06-01 | Added revision history and the use case agreed in 11-21-0899r0
3 | 2021-08-12 | Added the issue agreed in 11-21-1225r0
4 | 2021-10-14 | Added the issues and use case agreed in 11-21-1551r0

## Slide 3: Abstract
This document contains a summary of all TGbi proposed issues and use cases.

## Slide 4: TGbi Privacy Issue Template (replace with title)
Problem or issue
  Text describing problem or issue including scope of exposure (all users/some users/users of a specific 802.11 features), extent of exposure (user data directly exposed, user data inferable, other?), potential spec area affected.
Status of problem or issue
  Text indicating when issue was presented and any agreements on the issue.
Document references
  Text listing submission document number(s), also any other relevant documentation such as IETF draft or technical paper.

## Slide 5: 1) Protecting Password Identifiers
Issue
Password identifiers are used to look up passwords
Password identifiers are passed in the clear (PII)
Need to provide privacy to password identifiers
Status of issue
No objection to this issue from TGbi (April 8th meeting)
Document references
11-21-0488r0 and 11-21-0541r0

## Slide 6: 2) Avoid Element Fingerprint
Issue
Elements carried in an unprotected management frame are sent in clear to provide capabilities, operation parameters, or vendor specific indication, etc.
A large number of elements carried in an unprotected management frame may provide sufficient entropy as a fingerprint of a device/user
Need to provide privacy and avoid element fingerprint
Status of issue
Issue presented at IEEE 802.11bi session on 05/14/2021
Document references
Why MAC Address Randomization is not Enough: An Analysis of Wi-Fi Network Discovery Mechanisms
11-21-0839r0, 11-19-0489r0, 11-20-940r0, 11-20-746r1

## Slide 7: 3) STA MAC address persistence within an ESS
Problem/Issue
Current STA MAC address usage presents challenges to providing privacy.
  MAC address used for TA/RA does not change
  MAC address used for DA/SA does not change
Additional challenges
  DS requires an identifier for correlating associations from a single STA
    Currently using the MAC Address, and we want to change MAC address to improve privacy
  MAC address for DA/SA is used in upper layers. Changing these within association impacts upper layers
  MAC address for TA/RA is used for received packet filtering at the AP.
Status
Issue presented at IEEE 802.11bi session on 09/17/2021
Reference
11-21/1328r1

## Slide 8: 4) Tracking SA and DA OTA
Problem/Issue
SA and DA are currently sent in the clear OTA.
This reveals MAC addresses of other Devices used in the DS, which allows
  Identifying OUI of Wired Devices, and further profiling using traffic analysis
  Tracking STAs performing STA-to-STA communication, even if other tracking mitigations are applied
Status
Issue presented at IEEE 802.11bi session on 09/17/2021
Reference
11-21/1464r0

## Slide 9: TGbi Privacy Use Case Template (replace with title)
Use case
  Text describing use case including scope of use case (all users/some users/users of a specific 802.11 features), extent of use case (user data directly exposed, user data inferable, other?), potential spec area affected.
Status of Use Case
  Text indicating when use case was presented and any agreements on the use case.
Document references
  Text listing submission document number(s), also any other relevant documentation such as IETF draft or technical paper.

## Slide 10: 1) Smart Home Environment
Use case
  The Smart Home scenario is composed of different kind of devices, mainly of static nature, which do not generally change of AP.
  Possible privacy risks occur due to the static nature of the smart home appliances and possible correlation by inspection.
  Correlation between the data generated by devices at home, physically observable events and identity of the devices (e.g., MAC address) is possible, potentially leaking private data about the users’ behavior.
Status of Use Case
  Use case presented at IEEE 802.11bi session on 05/14/2021, agreed to move forward the use case based on this template
Document references
  11-21-0841r0 and 11-21-0878r0

## Slide 11: 2) Remote Stalking in public spaces
Use case
  The continuous use of a MAC address within a public network enables an attacker to detect the presence of a user in the public space and remotely follow him.
  When a user arrives at a public space, correlation between his presence and the MAC address used by his devices to join the public network is possible.
  While the user keeps associated using the same MAC address, it will be possible to identify when the user is associated to the network of the public space (presence), and his movements can be followed.
Status of Use Case
  Use case presented at IEEE 802.11bi session on the 07/15/2021, agreed to move forward the use case based on this template
Document references
  11-21-0993r0