## Slide 1: Further Improve Latency Performance in 11be
Date: 2021-04-13
Authors:
Name | Affiliation | Address | Phone | Email
Boyce Bo Yang | Huawei | Nanjing, China |  | yangbo59@huawei.com
Jason Yuchen Guo | Huawei | Shenzhen, China |  | guoyuchen@huawei.com
Ross Jian Yu | Huawei | Shenzhen, China |  | ross.yujian@huawei.com
Boyce, Huawei

## Slide 2: E2E Delays in heterogeneous networks
A typical data path nowadays consists of three hops, wireless LAN, wired network, and then wireless LAN.
E2E delay is a combination of transmission delays of wireless and wired networks.
    For wired networks, many efforts have been made over last several years, such as TSN, DetNet etc.
    For wireless LANs, 802.11be also aims at providing better delay performance for latency sensitive traffic.
This proposal is to provide some mechanism to further improve latency performance in 11be
Boyce, Huawei
Slide 2
Source
Destination
WLAN - 1
Wired Networks
(Ethernet and IP)
WLAN - 2

## Slide 3: Analysis on access delays when using EDCA
The figure above shows where the latency tail comes from in WLAN.
    Waiting for the transmission of other ongoing PPDUs of the device itself.
    Backoff and frequently being interrupted by transmissions of other STAs
    Collisions and backoff with a larger window
Boyce, Huawei
Slide 3
DIFS+
36us
STA a
STA b
STA c
STA d
5 ms
DIFS+27us
5 ms
DIFS+27us
Backoff: 10
Backoff: 20
Latency-sensitive traffic arrives

## Slide 4: Improved TXOP Sharing (1)
Boyce, Huawei
Slide 4
Latency-sensitive traffic usually has higher priority than non-latency-sensitive traffic. While it is still possible that the backoff counter of latency sensitive traffic is larger at some time.
    The backoff counter of non-latency-sensitive traffic may start to count down earlier
    The backoff counter of non-latency-sensitive traffic happens to choose a small value
Latency sensitive traffic has to wait until the device has obtained the second or even the third TXOP.
    Pre-EHT STAs are not allowed to include MPDUs from other ACs in the TXOP if the TIDs from primary AC are not empty. (Note: The AC that gains an TXOP is referred to as the primary AC.)
Non-LS MPDUs
4
3
2
1
2
1
3
2
1
1
2
1
1
LS MPDU
TXOP 1
TXOP 2
Latency-sensitive
AC
Non-Latency-sensitive
AC
PHY HDR
PHY HDR

## Slide 5: Improved TXOP Sharing (2)
Boyce, Huawei
Slide 5
A minor amendment can improve the delay performance of latency sensitive traffic:
Latency sensitive traffic belonging to any AC that has a higher priority with respect to the primary AC is allowed to be included in the A-MPDU or multiple frame transmission within the TXOP.
Non-LS
MPDUs
4
3
2
1
2
1
3
2
1
1
LS
MPDU
TXOP 1
Latency-sensitive traffic in an A-MPDU as a secondary AC
Latency-sensitive
AC
Non-Latency-sensitive
AC
PHY HDR
Latency-sensitive traffic in multiple frame transmission in other AC’s TXOP
Non-LS MPDU
4
3
2
1
2
1
3
2
1
1
LS MPDU
TXOP 1
Latency-sensitive
AC
Non-Latency-sensitive
AC
PHY HDR
PHY HDR
Notes: So the MPDUs of low latency traffic can be included in the A-MPDU even though there are some MPDUs in primary AC that can be aggregated in the A-MPDU

## Slide 6: Pre-emptible PPDU aggregation
Boyce, Huawei
Slide 6
The device may have a TXOP and is transmitting non-latency-sensitive traffic when latency-sensitive traffic arrives. In that case, latency sensitive traffic has to wait until the TXOP ends and contends the channel again.
Non-LS payload
HDR
TXOP 1
TXOP 2
Delay
LS traffic arrives
LS payload
HDR
To reduce delay of latency-sensitive traffic, we can introduce a pre-emptible PPDU so that latency sensitive traffic can be sent in current TXOP
    The transmitter can end the ongoing PPDU after the nearest segment with a PPDU end marker, and then send latency-sensitive traffic within the TXOP.
    The PPDU end marker could be a rotation of L-LTF or some other predefined sequences.
Notes: One simple example is that they are encoded and processed in PHY as 4 short PPDUs with same parameters. And then concatenated together omitting the PHY headers of the last 3 PPDUs.
Note that It only applies to STAs that has latency sensitive traffic.

## Slide 7: Pre-emptible PPDU aggregation- Example 1
Boyce, Huawei
Slide 7
LS payload
HDR
HDR
Payload
Payload
Payload
Payload
HDR
PPDU Payload
PPDU Payload
PPDU Payload
PPDU Payload
SIFS
SIFS
HDR
PPDU end marker
    To this end, PHY layer needs to encode a 4ms PPDU payload into 4 PPDU payloads, each of which is 1ms, when latency sensitive traffic does not arrive.
    When latency sensitive traffic arrives during the transmission of non-latency-sensitive traffic, PHY layer can end at the nearest boundary with a PPDU end marker.
    The receiver would deliver the segments that have been received to upper layer.
For a long non-latency-sensitive PPDU as long as 4ms, the transmitter can choose to interrupt the transmission and reassign the TXOP to latency sensitive traffic
Notes: Pros:
Latency sensitive traffic can be send within the current TXOP as early as possible
Data bits that has already been send can be received and delivered to up layer by the receiver.
Conts:
A bit complex for the PHY. Need to encode 4 short PPDUs instead of 1 long PPDU.
The good news is that
It only applies to STAs that has latency sensitive traffic(for example the STA that has setup a rTWT with AP). The STA don’t have to do this all the time.

## Slide 8: Pre-emptible PPDU aggregation- Example 2
Slide 8
    When there is no latency sensitive traffic arrives, PHY layer encodes a PPDU as usual and wait for ACK
    When latency sensitive traffic arrives during the transmission of non-latency-sensitive traffic, PHY layer can insert a PPDU sequence end marker at the end of the PPDU. So the following frame exchange is interrupted and the transmitter can send latency sensitive traffic instead.
    The receiver would not send a BA and expect to receive a latency sensitive PPDU after SIFS when a PPDU sequence end marker is detected at the end of a PPDU.
The transmitter can also choose to finish the ongoing transmission and send the latency sensitive traffic subsequently
HDR
Payload
HDR
BA
LS payload
HDR
HDR
PPDU Payload
SIFS
PPDU sequence end marker
HDR
M-TID BA
Boyce, Huawei
Notes: Pros：
Latency sensitive traffic can be send within the current TXOP.
Less changes are made to phy. Phy don’t have to separate a long PPDU into many short PPDUs.
Conts：
Latency sensitive traffic may have to wait for a long time if the ongoing PPDU is very long, say 4ms.
STAs that don’t support latency sensitive feature are not afftected

## Slide 9: Pre-emptible PPDU aggregation- Example 3
Slide 9
    When there is no latency sensitive traffic arrives, PHY layer encodes a PPDU as usual and wait for ACK
    When latency sensitive traffic arrives, PHY layer can interrupt the ongoing transmission with a PPDU end marker and send latency sensitive traffic after SIFS.
    The receiver may discard part or all of the received bits depending on whether a complete MPDU has been received.
The transmitter can also choose to interrupt the ongoing transmission directly
HDR
Payload
HDR
BA
LS payload
HDR
HDR
Payload
SIFS
PPDU end marker
Boyce, Huawei
Notes: Pros:
Less changes are made to phy.
Latency sensitive traffic can be send earlier.
Conts:
Part or all bits that have been send may be discarded
The receiver would expect receiving a latency sensitive PPDU after SIFS when a PPDU sequence end marker is detected.

## Slide 10: Transmitter block diagram of PHY
Slide 10
Transmitter block diagram for EHT PPDU Data field
Control Switch
Analog and RF
PPDU End Marker
Control signal
Data bits of EHT PPDU 1
Data bits of EHT PPDU 2
Transmitter block diagrams for Pre-EHT PPDU Data field
Transmitter block diagram for L-SIG, RL-SIG,U-SIG, HE-SIG-A fields
bits of PHY Header
HDR
Payload
Payload
Payload
Payload
Generate 1 PHY Header and then 4 Data fields
LS payload
HDR
HDR
Payload
Payload
HDR
Switch to generate PPDU End Marker at the end of the first PPDU Data field
Generating PPDUs shown in previous examples
LS payload
HDR
HDR
Payload
Switch to generate PPDU End Marker at any time
Pre-FEC Padding, Scrambler, LDPC Encoder, Post FEC Padding, Stream Parser, Constellation mapper, LDPC Tone mapper, CSD, Spatial and Frequency mapping, IDFT, Insert GI, window
Boyce, Huawei

## Slide 11: Conclusion
We give some basic ideas on further improving latency and jitter performances in 11be.
Boyce, Huawei
Slide 11

## Slide 12: Reference
[1] 11-20-1670-02-00be-low-latency-resource-agreements
[2] 11-20-1897-03-00be-obss-edca-parameter-sets-for-rta
Boyce, Huawei
Slide 12

## Slide 13: BACKUP
Boyce, Huawei
Slide 13
Current rules for TXOP sharing in md5.0
Additional rules for TXOP sharing in ax8.0
If the TXOP limit of the primary AC is greater than 0, then the STA may aggregate QoS Data frames from one or more TIDs in the AMPDU under the following conditions:
Frames from ACs other than the primary AC shall not be included in the TXOP, with the following exceptions (TXOP sharing):