## Slide 1: Discussion on B55 of Common Info Field in EHT TF
Date: 2021-04-21
Authors:

## Slide 2: Recap
11be has agreed to use B55 of Common Info Field to indicate the presence of Special User Info Field in EHT TF variants
  B55 is set to 1 to indicate that there is no Special User Info field in the Trigger frame.
  B55 is set to 0 to indicate that the Special User Info field is present in the Trigger frame.
11be has agreed that the Special User Info Field shall be present in all EHT TF variants 11be in R1

## Slide 3: Discussion
Scenario 1 – non-AP EHT STA associated with AP EHT STA
  The non-AP EHT STA can tell the Special User Info Field from User Info Fields via AID=2007 because the Special User Info Field is always there in EHT TF.
Scenario 2 – non-AP HE STA associated with AP EHT STA
  The non AP HE STA will not use the Special User Info Field forever because AID 2007 will not be assigned to any non-AP STA.
Scenario 3 – non AP EHT STA associated with AP HE STA
  The non AP EHT STA will not take the User Info Fields with AID=2007 as the Special User Info Field even if AID 2007 is assigned because it knows the BSS is not an EHT BSS.

## Slide 4: Conclusion
In R1, the Special User Info Field shall be present in all EHT TF variants. So B55 of the Common Info Field, which indicates the presence of the Special User Info Field, is redundant. The B55 can be reserved.
  The additional step of processing the B55 can be saved in non-AP EHT STA.
  More reserved bits can be used for furture
For R2, we can have further discussion. Indication bit of the presence of the Special User Info Field in the Common Info Field can be added even if there are scenarios and requirements.

## Slide 5: Proposal
B55 of the Common Info Field in ETH TF is reserved in R1.
  Note - For R2, we can have further discussion on the indication of presence of the Special User Info Field in EHT TF.

## Slide 6: SP
Do you support to reserve B55 of the Common Info Field in ETH TF in R1?
  Note - For R2, we can have further discussion on the indication of presence of the Special User Info Field in EHT TF.

## Slide 7: Reference
[1] https://mentor.ieee.org/802.11/dcn/20/11-20-1935-26-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document-part-2.docx