## Slide 1: Narrowband Coexistence with Wi-Fi in 6 GHz
Author:
Name | Affiliation | Address | Phone | Email
Menzo Wentink | Qualcomm | Utrecht, The Netherlands |  | mwentink qti.qualcomm.com

## Slide 2: Introduction
Narrowband (NB) frequency hopping has been proposed in the 6 GHz band, per document BRAN(21)109e003r1 (EN 303 687 NB Inputs)
  this document proposes to use the NB channel access rules from the 2.4 GHz band in EN 300 328
  these rules include Detect and Avoid (DAA)
Document BRAN(21)109e003r1 (EN 303 687 NB Inputs) presents interference measurements between BT and Wi-Fi
This submission analyzes coexistence between BT and Wi-Fi, on the same test setup as used in BRAN(21)109e003r1

## Slide 3: Wi-Fi - BT Test Setup

## Slide 4: Simulation settings
Wi-Fi link
  80 MHz channel width, VHT (11ac), Nss = 1
  Maximum throughput about 410 Mbps (MCS9, 400 ns GI, 80 MHz, 433.3 Mbps)
  Receive bitrate based on receive SINR and MCS sensitivities for MCS0 – MCS9
BT link
  79 hops, 1 MHz hop width, 79 MHz hopping bandwidth
  625 μs dwell time, 600 μs Tx, 25 μs switch time, 96% duty cycle
  3 Mbps max bitrate based on EDR 8-DPSK
  BT is on the same channel as the Wi-Fi link (co-channel interference)
  DAA uses a 40 ms COT, when enabled
100 pps Wi-Fi link (BT replacement link)
  80 MHz channel width, VHT (11ac), Nss = 1
  3 Mbps throughput
  AC_VO access parameters

## Slide 5: Wi-Fi throughput as a function of the BT interference level (BT does not use DAA)
the Wi-Fi throughput degrades significantly with increasing BT interference
the residual Wi-Fi throughput is very low

## Slide 6: Wi-Fi throughput as a function of the BT interference level (BT uses DAA)
the residual Wi-Fi throughput is still very low, also when BT uses DAA
with DAA, the Wi-Fi throughput also degrades significantly

## Slide 7: Wi-Fi throughput as a function of the BT interference level (BT uses 1 in 5 hops, 20% DC)
the Wi-Fi thoughput degrades significantly, also when BT uses 1 out of every 5 hops (20% duty cycle)
the residual Wi-Fi throughput is very low

## Slide 8: Wi-Fi throughput as a function of the BT interference level (BT uses 20% of every hop)
the Wi-Fi thoughput degrades significantly, also when BT uses 20% of every hop
the residual Wi-Fi throughput is very low

## Slide 9: Wi-Fi latency as a function of the BT interference level (BT does not use DAA)
without DAA, the Wi-Fi peak latency becomes very high when BT interferes above -62 dBm
the latency peaks depend on the specific BT hopping schedule (assuming Wi-Fi can dynamically switch to 20 MHz channel width, otherwise the latency will be even higher)

## Slide 10: Wi-Fi latency as a function of the BT interference level (BT uses DAA)
with DAA, the Wi-Fi peak latency still becomes very high
the latency peaks depend on the specific BT hopping schedule (assuming Wi-Fi can dynamically switch to 20 MHz channel width, otherwise the latency will be even higher)

## Slide 11: Wi-Fi latency as a function of the BT interference level (BT uses 1 in 5 hops, 20% DC)
BT using 1 out of 5 hops (20% dutcy cycle) causes very high latency for Wi-Fi
the latency peaks depend on the specific BT hopping schedule (assuming Wi-Fi can dynamically switch to 20 MHz channel width, otherwise the latency will be even higher)

## Slide 12: Wi-Fi latency as a function of the BT interference level (BT uses 20% of every hop)
BT using 20% of every hop causes very high latency for Wi-Fi
the latency is very high in this case, because the idle time inside the hops cause Wi-Fi to transmit, after which the next hop destructively interferes with it
the latency peaks depend on the specific BT hopping schedule (assuming Wi-Fi can dynamically switch to 20 MHz channel width, otherwise the latency will be even higher)

## Slide 13: DAA number of active hops as a function of time (BT at a high interference level, uses DAA)
with DAA, the number of active hops oscillates, which is very strange
after 10 s, DAA still did not detect Wi-Fi on 12 hops
16 s
period
it takes 3 s before DAA first reacts to the Wi-Fi traffic
simulation at high interference level
time between DAA CCAs: 3.16 s
maximum unavailability time: 15.8 s
BT DAA COT: 40 ms

## Slide 14: Wi-Fi throughput as a function of time (BT at a high interference level, uses DAA)
the Wi-Fi throughput oscillates in counter-phase with the number of active hops
Red: BT throughput

## Slide 15: Wi-Fi latency as a function of time (BT at a high interference level, uses DAA)
Wi-Fi can still experience very high latency when DAA is used
Red: BT latency

## Slide 16: Comparison between BT sharing and Wi-Fi sharing (Impact on main Wi-Fi link throughput)
in this plot, Wi-Fi uses 4x4 sensitivity levels, causing the throughput degradation to set in at higher interference levels
for the red curve, the BT link was replaced with a 100 pps 3 Mbps Wi-Fi link

## Slide 17: Comparison between BT sharing and Wi-Fi sharing (Impact on main Wi-Fi link latency)
for the red curve, the BT link was replaced with a 100 pps 3 Mbps Wi-Fi link

## Slide 18: Conclusions
BT frequency hopping can cause major throughput and latency degradation at a Wi-Fi link
  also when BT uses a reduced duty cycle or Detect and Avoid (DAA)
  while Wi-Fi defers for BT, BT will not defer for Wi-Fi and step onto ongoing Wi-Fi transmissions, due to the absence of LBT
  these simulations do not consider the effect of out of band emissions, which may cause similar issues even when the BT link is not on the same channel as the Wi-Fi link
  these simulations also do not consider the effect of multiple BT links operating near a WiFi link, which will make things worse
DAA shows an oscillation of active hops
  DAA may not have been designed for coexistence with Wi-Fi

## Slide 19: Potential next steps / areas for further analysis
Continue analysis of coexistence characteristics of NB proposals
Evaluate impact of NB interference from adjacent / non-overlapping frequencies on Wi-Fi throughput and latency
Evaluate impact of multiple NB links interfering with a Wi-Fi link
Analyze potential impact of NB interference on high value 6 GHz use cases
Explore protocol designs for improved NB coexistence
Further study the impact of NB interference into a wideband Wi-Fi signal
Other?