## Slide 1: Channel Access for Latency Sensitive Traffic
Date: 2021-05-18
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | Sony Corporation |  |  | Liangxiao.Xin@sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud@sony.com
Li-Hsiang Sun |  |  |  | Li-Hsiang.Sun@sony.com

## Slide 2: Introduction
The group has agreed on using R-TWT and quiet interval to provide more predictable latency performance for latency sensitive traffic.
During a R-TWT SP, R-TWT member STAs should be prioritized to transmit latency sensitive traffic.
Other STAs may not enter quiet period during R-TWT weak protection
  It is optional for AP to schedule quiet interval during the first TU of the R-TWT SP
  Quiet element is not implemented if device does not operate on DFS channel (e.g., U-NII) [1]
  EHT STAs may ignore the quiet element
  Miss the latest update of the quiet interval (e.g., miss quiet element in beacon)
Other STAs can access channel during R-TWT SP and harm the latency performance of latency sensitive traffic.
In this presentation, we discuss the channel access during the R-TWT SP to protect channel resource for latency sensitive traffic.
  Other tools are needed to protect R-TWT SP besides quiet interval.

## Slide 3: Network under consideration
During the R-TWT SP, the STA can be classified as
  R-TWT scheduled STA (member or not member)  support R-TWT operation
  Non-R-TWT scheduled STA  R-TWT support disabled and legacy devices
We propose the methods to protect R-TWT SP from non-R-TWT scheduled STA
R-TWT scheduling AP
R-TWT member STA
(AR/VR)
R-TWT scheduled STA, not member
(Online/cloud gaming)
Non-R-TWT scheduled STA

## Slide 4: Proposed Solution 1
The R-TWT scheduling AP may decide not to send an CTS in response to an RTS sent by non-R-TWT scheduled STA during a R-TWT SP.
  This solution could also apply to the R-TWT scheduled STAs that are not members
Open discussion: if non-R-TWT scheduled STA sends an RTS before the start of a R-TWT SP but the NAV duration of RTS overlaps that R-TWT SP, should R-TWT scheduling AP send CTS?
However, pre-11ax STA makes its own decision of sending RTS or not.
R-TWT scheduling AP
Non-R-TWT scheduled STA
R-TWT SP
RTS
AP does not send CTS
R-TWT scheduling AP
Non-R-TWT scheduled STA
R-TWT SP
RTS
Should AP send CTS?
NAV (RTS)

## Slide 5: Proposed Solution 2
Giving R-TWT member STAs higher priority to access the channel during their R-TWT SP than other STAs
  The R-TWT scheduling AP and the member STAs contend the channel together during R-TWT SP.
  If a member STA obtain the TXOP first, let the R-TWT scheduling AP arrange the transmissions during TXOP
  The R-TWT scheduling AP collects the QoS requirement of the latency sensitive traffic of all the member STAs to allocate the channel resources to those STAs during TXOP.
Benefits:
  Increase the chance of winning the competition with non-R-TWT scheduled STAs, not only those associated with the R-TWT scheduling AP but also those associated with OBSS AP.
  Reduce the channel contention delay for all the latency sensitive traffic
  Finish latency sensitive traffic transmissions of multiple STAs during one TXOP
  Help meet the QoS requirement of the latency sensitive traffic

## Slide 6: Example
The R-TWT scheduling AP and member STAs contend the channel together during a R-TWT SP.
  the latency sensitive packets may arrive after the start time of R-TWT SP
When a member STA (e.g., STA2) obtains TXOP during a R-TWT SP, it sends a frame (e.g., CTS frame) to share its TXOP with AP.
  The RA in CTS frame is set to a special address to indicate the TXOP sharing and NAV setting.
  The RA in CTS frame sent by any member STAs (e.g., STA1 and STA2) is the same.
When AP receives the CTS frame or obtains the TXOP by itself, it takes over the TXOP and arranges the transmissions of all the member STAs.
R-TWT scheduling AP
Member STA1
Member STA2
CTS
AP arranges DL/UL/P2P transmissions during TXOP
R-TWT SP
STA2 obtains TXOP and shares it with AP

## Slide 7: Meet QoS requirements of latency sensitive traffic
When a member STA reports its buffer status during R-TWT SP, it only reports the buffer status of latency sensitive traffic.
  No need to update current BSRP and BSR exchange
When R-TWT scheduling AP arranges transmission during R-TWT SP, it could collect the traffic information of latency sensitive traffic and schedule the transmissions for all the member STAs.
  AP might need the following information from each member STA:
    Earliest expiration time of latency sensitive traffic
    Buffer size of latency sensitive traffic that will expire at the earliest expiration time
    Buffer size of all the latency sensitive traffic
    Other traffic information, e.g., TID, latency sensitive traffic ID
  This information can be reported by a regular or a new type BSR is TBD

## Slide 8: Conclusion
R-TWT SP needs to be protected from the non-R-TWT STAs
R-TWT scheduling AP can refuse to send CTS when receiving RTS from a non-R-TWT STA during R-TWT SP
During R-TWT SP, R-TWT scheduling AP and member STAs should have higher priority to access the channel than other STAs.
  R-TWT scheduling AP and member STAs contend the channel together.
  When a member STA obtains the TXOP, let the R-TWT scheduling AP arrange the transmissions during TXOP
  The R-TWT scheduling AP collects the QoS requirement of the latency sensitive traffic of all the member STAs to allocate the channel resources to the member STAs during the TXOP.

## Slide 9: Reference
[1] Könings, Bastian, et al. "Channel switch and quiet attack: New DoS attacks exploiting the 802.11 standard." 2009 IEEE 34th Conference on Local Computer Networks. IEEE, 2009.