## Slide 1: Channel Access for Latency Sensitive Traffic
Date: 2021-05-18
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | Sony Corporation |  |  | Liangxiao.Xin@sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud@sony.com
Li-Hsiang Sun |  |  |  | Li-Hsiang.Sun@sony.com

## Slide 2: Related Comments
CID | Commenter | Clause Number(C) | Comment | Proposed Change | Resolution
5880 | Liangxiao Xin | 35.6.4.1 | Not every legacy STA will respect quiet element. More mechainsms other than quiet element is needed to enhance the medium access protection during a restricted TWT service period | During a restricted TWT SP, the scheduling AP may not respond to a RTS whose TXOP overlapps with a R-TWT SP from a STA which is not a member of the restricted TWT. | Revised Agree with the commenter. Current RTS/CTS mechanism can be updated to protect channel access for latency sensitive traffic during the restricted TWT SP TGbe editor, please incorporate changes as shown in 11-21/00894r4 tagged 5880

## Slide 3: Introduction
The group has agreed on using R-TWT and quiet interval to provide more predictable latency performance for latency sensitive traffic.
During a R-TWT SP, R-TWT member STAs should be prioritized to transmit latency sensitive traffic.
Other STAs may not enter quiet during R-TWT SP  weak protection
  Quiet element is not implemented if device does not operate on DFS channel (e.g., U-NII) [1]
  Miss the latest update of the quiet interval (e.g., miss quiet element in beacon)
  It is optional for AP to schedule quiet interval during the first TU of the R-TWT SP
  EHT STAs may ignore the quiet element
Other STAs will access channel during R-TWT SP and harm the latency performance of latency sensitive traffic.
In this presentation, we discuss the channel access during the R-TWT SP to protect channel resource for latency sensitive traffic.
  Other tools are needed to protect R-TWT SP besides quiet interval.

## Slide 4: Network under consideration
During the R-TWT SP, the STA can be classified as
  R-TWT scheduled STA (member or not member)  support R-TWT operation
  Non-R-TWT scheduled STA
We propose the methods to protect R-TWT SP from non-R-TWT scheduled STA
R-TWT scheduling AP
R-TWT member STA
(AR/VR)
R-TWT scheduled STA, not member
(Online/cloud gaming)
Non-R-TWT scheduled STA

## Slide 5: Proposed Solution 1
The R-TWT scheduling AP does not send an CTS in response to an RTS sent by non-R-TWT scheduled STA during a R-TWT SP.
  This solution could also apply to the R-TWT scheduled STAs that are not members
Open discussion: if non-R-TWT scheduled STA sends an RTS before the start of a R-TWT SP but the NAV duration of RTS overlaps that R-TWT SP, should R-TWT scheduling AP send CTS?
However, pre-11ax STA makes its own decision of sending RTS or not.
R-TWT scheduling AP
Non-R-TWT scheduled STA
R-TWT SP
RTS
AP does not send CTS
R-TWT scheduling AP
Non-R-TWT scheduled STA
R-TWT SP
RTS
Should AP send CTS?
NAV (RTS)

## Slide 6: Proposed Solution 2
Giving R-TWT member STAs higher priority to access the channel during their R-TWT SP than other STAs
  The R-TWT scheduling AP and the member STAs contend the channel together during R-TWT SP.
  If a member STA obtain the TXOP first, let the R-TWT scheduling AP arrange the transmissions during TXOP
  The R-TWT scheduling AP collects the QoS requirement of the latency sensitive traffic of all the member STAs to allocate the channel resources to those STAs during TXOP.
Benefits:
  Increase the chance of winning the competition with non-R-TWT scheduled STAs, not only those associated with the R-TWT scheduling AP but also those associated with OBSS AP.
  Reduce the channel contention delay for all the latency sensitive traffic
  Finish latency sensitive traffic transmissions of multiple STAs during one TXOP
  Help meet the QoS requirement of the latency sensitive traffic

## Slide 7: Example
The R-TWT scheduling AP and member STAs contend the channel together during a R-TWT SP.
  the latency sensitive packets may arrive after the start time of R-TWT SP
When a member STA (e.g., STA2) obtains TXOP during a R-TWT SP, it sends a frame (e.g., CTS frame) to share its TXOP with AP.
  The RA in CTS frame is set to a special address to indicate the TXOP sharing and NAV setting.
  The RA in CTS frame sent by any member STAs (e.g., STA1 and STA2) is the same.
When AP receives the CTS frame or obtains the TXOP by itself, it takes over the TXOP and arranges the transmissions of all the member STAs.
R-TWT scheduling AP
Member STA1
Member STA2
CTS
AP arranges DL/UL/P2P transmissions during TXOP
R-TWT SP
STA2 obtains TXOP and shares it with AP

## Slide 8: Conclusion
R-TWT SP needs to be protected from the non-R-TWT STAs
R-TWT scheduling AP can refuse to send CTS when receiving RTS from a non-R-TWT STA during R-TWT SP
During R-TWT SP, R-TWT scheduling AP and member STAs should have higher priority to access the channel than other STAs.
  R-TWT scheduling AP and member STAs contend the channel together.
  When a member STA obtains the TXOP, let the R-TWT scheduling AP arrange the transmissions during TXOP

## Slide 9: SP1
Do you support that A R-TWT scheduling AP may not send a CTS in response to an RTS from a STA which is not a member of the R-TWT SP during a R-TWT SP?
  Note: this SP aims to trigger the below change in the spec for the resolution of CID 4121
10.3.2.9 CTS and DMG CTS procedure
  Change the below paragraph of this subclause:
  A VHT STA that is addressed by an RTS frame in a non-HT or non-HT duplicate PPDU that has a bandwidth signaling TA and that has the RXVECTOR parameter DYN_BANDWIDTH_IN_NON_HT equal to Static behaves as follows:
  —If the NAV indicates idle, the STA is not NSTR limited and CCA has been idle for all secondary channels (secondary 20 MHz channel, secondary 40 MHz channel, and secondary 80 MHz channel) in the channel width indicated by the RTS frame’s RXVECTOR parameter CH_BANDWIDTH_IN_NON_HT for a PIFS prior to the start of the RTS frame, then the STA shall respond with a CTS frame carried in a non-HT or non-HT duplicate PPDU after a SIFS. The CTS frame’s TXVECTOR parameters CH_BANDWIDTH and CH_BANDWIDTH_IN_NON_HT shall be set to the same value as the RTS frame’s RXVECTOR parameter CH_BANDWIDTH_IN_NON_HT.
  •If all of the conditions in the previous paragraph are met, except for the condition “the STA is not NSTR limited”, then the STA may respond with the CTS frame as described in that paragraph.
  (#5880)•If the R-TWT scheduling AP receives a RTS frame during a R-TWT SP and the RTS frame is from a STA which is not a member STA of that R-TWT SP, then the AP may not respond with the CTS frame as described in that paragraph.
  —Otherwise, the STA shall not respond with a CTS frame.

## Slide 10: SP2
Do you support that during a R-TWT SP, a member STA of the R-TWT SP can access the channel and share TXOP with the R-TWT scheduling AP?
  Note: this SP aims to trigger the below change in the spec for the resolution of CID 4121
  35.8.4 Channel access rules for r-TWT service periods
  35.8.4.1 TXOP rules for r-TWT SPs
  Add the below paragraph at the end of this subclause:
  (#5880) A non-AP EHT STA with dot11RestrictedTWTOptionImplemented set to true may contend the channel during a R-TWT SP if that non-AP EHT STA is a member STA of that R-TWT SP. When the non-AP EHT STA accesses the channel, it may send a CTS frame to the R-TWT scheduling AP to share its TXOP.

## Slide 11: Reference
[1] Könings, Bastian, et al. "Channel switch and quiet attack: New DoS attacks exploiting the 802.11 standard." 2009 IEEE 34th Conference on Local Computer Networks. IEEE, 2009.