## Slide 1: EBCS Architecture
Date: 2021-05-31
Authors:

## Slide 2: Abstract
This presentation describes EBCS architecture.

## Slide 3: EBCS
EBCS provides 2 types of services.
  EBCS DL:
    An EBCS AP distributes multicast contents to both associated and unassociated EBCS receivers with origin authenticity.
  EBCS UL:
    The EBCS UL Service procedure allows a non-AP STA to transmit an EBCS UL frame with the expectation that one or more EBCS APs in the neighborhood would relay the HLP payload carried in the frame to a destination specified in the frame.

## Slide 4: DL Use Case: Stadium Video Distribution
Stakeholders
  Stadium system operators
  Stadium audience, coaches and referees
  Broadcasters, e.g., Live TV
  Manufacturers of semiconductor, networking and mobile devices
Topology/Architecture
Expected benefits:
  Ability to broadcast simultaneous information to a large number of users
  Reuse existing technology while reducing cost and implementation complexity
Service scene
  An eBCS AP provides eBCS for videos to a large number of densely located STAs, which may be mobile devices.
  An eBCS AP provides multiple eBCSs for multiple video streams, e.g.:
    live video feed/Video Highlights Replay
    Videos from different angles of the game (e.g., in soccer)
    Videos of different sport activities that take place in parallel (e.g., athletics)
Required function
Providing enhanced Broadcast Services (eBCS) for videos to a large number of densely located STAs. These STAs may be associated, or unassociated with the AP or may be STAs that do not transmit.
Contents
Server
AP
STA
STA
STA
STA
Network
STA

## Slide 5: UL Use Case: Low Power Sensor UL Broadcast
Internet
Server
STA 1
STA 2
Stakeholders
  Users of IoT devices
  IoT System Operators
  Manufacturers of semiconductor, APs, IoT devices, networking and mobile devices
Topology/Architecture
Expected benefits:
  Ability to broadcast information destined to the end server
  Ability to reduce cost and implementation complexity
  Ability to enable low power sensor STA operations
Service scene
  An eBCS AP provides forwarding service for eBCS non-AP STAs that are not associated with itself to end-servers
  eBCS STAs have pre-configured keys to enable secure message delivery
  eBCS non-AP STAs are expected to generate low rate data: e.g., 100bps short burst once a day
  eBCS APs may enforce service policy
Required function
Pre-configured IoT devices automatically connect to the end server through eBCS APs with zero setup action required
Low power IoT devices in mobility report to their servers through eBCS APs without scanning and association
Internet
Server
AP 1
STA 1
@ t=T1
AP 2
STA 1
@ t=T2
Zero Setup Sensor
Sensor on the move
AP 1
AP 2

## Slide 6: Frame Types
EBCS DL
  EBCS Info frame (Public Action frame):
    Key, Content information…
  EBCS Data frame (Data frame, Class 1):
    Content
EBCS UL
  EBCS UL frame (Public Action frame):
    Content, Key…
Public Action frames does not affect data plain architecture.

## Slide 7: EBCS DL
AP
Receiver
Server
IPv4 Multicast
(RFC1112)
Dst MAC
01:00:5e:xx:xx:xx
IPv6 Multicast
(RFC2464)
33:33:xx:xx:xx:xx
If the combination of the source IP address, the destination IP address and the destination UDP port of the packet is in the dot11EBCSContentList,
the AP uses EBCS to forward the frames.
Otherwise, the AP uses GTKSA to forward the frames. (If associated STA exists)
RA
01:00:5e:xx:xx:xx
33:33:xx:xx:xx:xx

## Slide 8: DL Architecture Option 1
EBCS Proxy function
TX
  Filtering packets according to
    Higher layer information (IP addresses, port number…) of the packets
    MIB variable dot11EBCSContentList
  Forwarding packets to MAC
RX
  Forwarding packets to upper layers
Common to PKFA and HCFA
No encryption / decryption
Integrity check only
PKFA
Key is set by MLME-EBCSINFO.request (TX) and is gotten from eBCS Info frame (RX)
HCFA
Keys are generated in MAC (TX) and are gotten from MPDU (RX)
HLSA
Pass through
Figure 5-1—MAC data plane architecture
EBCS
Proxy
LPD/EPD
802.1AC
convergence
function
Pass through for EBCS

## Slide 9: Option 2: EBCS role
EBCS AP role
EBCS filter
(DS SAP)
(C)
(EBCS bypass)
EBCS bypass
EBCS receiver role
EBCS DL traffic
Non-EBCS traffic
EBCS DL traffic
DA address
filtering
Non-EBCS traffic
(EBCS
bypass)

## Slide 10: Define New eBCS Data frame (Copied from 11-19/1506r3)
Add a definition for Class 1 frames in 11.3.3 like following.
3) Data frames
i) Data frames between IBSS STAs
ii) Data frames within PBSS
iii) eBCS Data frames
One or more subtype value(s) for Frame Control field should be assigned.

## Slide 11: EBCS AP MIB Variables
dot11EBCSInfoInterval
dot11EBCSHCFAKeyChangeInterval
dot11EBCSHCFAHashDistance
dot11EBCSInfoTxRate
dot11EBCSDataTxRate
dot11EBCSContentList (will be added in D1.03)

## Slide 12: EBCS AP MLME SAP interfaces
MLME-EBCSINFO.request (6.3.200.2)
  Request to transmit EBCS Info frame.

## Slide 13: EBCS receiver MLME SAP interfaces
MLME-EBCSINFO.indication (6.3.200.3)
  Indicates EBCS Info frame reception.
MLME-EBCSRECEIVE.request (not in D1.02)
  Request to receive specified EBCS traffic stream.