## Slide 1: Setting of USIG Disregard Bits in TB-PPDU
Date: 2021-06-21
Authors:

## Slide 2: Abstract
USIG carries important information crucial for the successful decoding of a packet.
The reliability of USIG reception shall be much higher than data.
The USIG design is different for MU-PPDU and TB-PPDU.
  Our focus in this contribution is on TB-PPDU.
USIG in TB-PPDU has 11 Disregard bits.
  The setting of these bits has not been decided yet [1]

## Slide 3: Recap of the Issues
X0 X1 X2 X3 X4 X5
X6 X7 X8 X9 X10
Those bits are currently undefined. Leaving them completely random is not desirable:
  For example, if some of those bits are defined for R2 feature(s), R2 devices may read them and make unexpected behavior in R1-only environment
There have been two proposals for how to set those Disregard bits:
  Set all bits to “1” for implementation simplicity [2]
  Set those bits to a fixed sequence for PAPR reduction for all puncturing patterns and other settings (e.g., BSS color) in the USIG [3]
Both proposals should work for R1 indication, but both have PAPR issue.
Setting of other bits (e.g., BSS Color, ESR1, ESR2, etc.) has a significant impact on the PAPR performance.

## Slide 4: USIG Design in TB-PPDU
An alternative setting of the Disregard bits in USIG (TB-PPDU)
  One bit, e.g., X0, is used to differentiate between R1 and R2 devices (maybe named as R-bit)
  The remaining 10 bits are chosen to minimize the PAPR of the USIG (Implementation-Dependent)
  The Disregard sequence to minimize the PAPR will be a function of:
    Operating Bandwidth
    BSS Color
    Spatial Reuse (ESR1 and ESR2)
    Puncturing patterns

## Slide 5: Simulation Setup
Transmission mode: non-OFDMA
PPDU format: TB-PPDU
Bandwidth: 320-1 MHz
SR: Disallowed
Validate Bit: Set to 1
CRC: computed according to the specs (27.3.11.7.3 CRC computation [4])

## Slide 6: PAPR for Different BSS Colors
 | R = 0 |  | R = 1 | 
BSS Color | Max PAPR(dB) Disregard Bits | Min PAPR(dB) Disregard Bits | Max PAPR(dB) Disregard Bits | Min PAPR(dB) Disregard Bits
1 | 17.7 0110100000 | 10.5 1000111111 | 18.3 1011000000 | 9.8 1011110100
2 | 18.3 1000100000 | 10.1 1000001010 | 17.9 0101000000 | 10.7 0111110011
* These results are for the non-OFDMA puncturing pattern 11111111 (no puncturing) |  |  |  | 
BSS Color | Disregard = (1)1111111111 [2] (min , max) (dB) | Disregard = (0) 1111011011[3] (min , max) (dB)
1 | (11.4 , 14.5) | (9.88 , 13)
2 | (10.6 , 13.8) | (9.25 , 12.42)

## Slide 7: Conclusions
Setting of Disregard bits in the USIG significantly impacts the PAPR performance.
There is no single Disregard bits sequence that would minimize the PAPR for all BSS Colors, Bandwidths, and Puncturing Patterns.
One bit is enough to signal R1/R2 devices and the setting of the remaining 10 bits of the Disregard bits may be left for implementation.

## Slide 8: SP 1
Do you agree to define one of the 11 Disregard bits in USIG of TB-PPDU for differentiating R1 and R2?
  The position of the bit is TBD
  The setting of the remaining Disregard bits are left for implementation.
  This is for R1 only.

## Slide 9: References
[1] 802.11-20/1982r25, TGbe Motions List For Teleconferences-part 2, Alfred Asterjadhi (Qualcomm Inc.)
[2] 802.11-21/0729r2, Disregard bits in TB PPDU, Ron Porat (Broadcom)
[3] 802.11-21/0093r4, Reducing USIG PAPR via Disregard Bit Value, Shimi Shilo (Huawei)
[4] “IEEE P802.11ax™/D8.0, Amendment 1: Enhancements for High Efficiency WLAN”, 2020.