## Slide 1: 11bb current status and way forward
Date: 2021-06-28
Authors:

## Slide 2: Abstract
This contribution assesses 11bb D0.5 and recommends a way forward.

## Slide 3: Current situation
LC PHY has 3 “modes”:
  32.3.3 LC Common mode (CM), mandatory to support
  32.3.4 LC High Efficiency (HE) mode, optional to support
  32.3.6 LC Optimized (LCO) mode based on ITU G.vlc, optional to support
We have learned that defining an LC Optimized PHY within the existing 11bb LC PHY framework is more complex than anticipated
  See e.g. 11-21/382r0, 11-21/812r0, backup slide
We do not see any realistic path to complete an LC Optimized PHY in the 11bb framework

## Slide 4: Recommendations
We should remove LCO PHY from 11bb draft to allow commercialization now
We should postpone investigations of a PHY optimized for LC until P802.11be provides a firm base and consider using a different framework such as Multi-Link Operation (MLO)
Start discussions on the new project not earlier than when 11bb goes to Sponsor Ballot
  Focus efforts to get 11bb done!

## Slide 5: Backup

## Slide 6: Open points to complete integration of LCO PHY into 802.11bb
  MAC text (clauses 9 Frame formats, 10 MAC sublayer, and 11 MLME)
  Service primitive specifications for PHY SAP (8 PHY service specification), PLME SAP (6.5 PLME SAP interface), and MLME SAP (6.3 MLME SAP interface) interfaces
  MIB specification
  Channel numbering for Optimized PHY
  Integrating use of Optimized PHY + CM PHY
    How to explain “switching” between CM PHY and Optimized PHY: in the 802.11 model, there is no switching. An HE STA uses HE PHY only but is allowed to send 11a PPDUs
  Coexistence between LC Optimized mode PHY and the other PHYs
    for Clear Channel Assessment to work, Optimized PHY PPDUs must begin with legacy preamble and Signal field of the legacy preamble must use 11a modulation and coding, but the subcarrier spacing of the legacy preamble is different from that of the LC optimized PHY
    See 11-21-0382-00-00bb-discussion-on-lc-optimized-mode-coexistence-with-other-11bb-phys.pptx for details