## Slide 1: Traffic Prioritization During the Restricted TWT SPs
Date: 2021-07-25
Name | Affiliations | Address | Phone | email
Chunyu Hu | Facebook Inc. | 1 Hacker way Menlo Park, CA |  | chunyuhu07@gmail.com
M. Kumail Haider |  |  |  | 
Chitto Ghosh |  |  |  | 

## Slide 2: Abstract
Discuss the traffic prioritization rules during the restricted TWT SPs

## Slide 3: Background
D1.1 subclause 35.6.2 (Restricted TWT setup procedure) specifies TID(s) as traffic associated with the rTWT membership between the rTWT scheduling AP and the rTWT scheduled STAs
During the discussion on the rTWT setup procedure (11-21/462), the topic on traffic “restriction” or “prioritization” didn’t reach conclusion or have much time to address. This presentation revisits the topic in order to resolve this pending item and related CC36 CIDs:
  4768, 4775, 4776, 5874, 6506, 4121, 5728, 6511, 7432, 7634, 5775, 6546, 5664, 4586, 4587, 4588

## Slide 4: Problem
Notation:
  TIDs_L denotes TIDs specified by the rTWT setup procedure
  TIDs_L{AP, STA_x} is the TID set specified by the rTWT setup procedure between AP and STA_x
During the restricted TWT service periods (SPs), is there any restriction to the type of traffic to be delivered?
  Is it a “restriction” or “prioritization”?
  If any, what are the specific rules for:
    rTWT scheduling AP’s transmission?
    rTWT scheduled STA’s transmission?
    rTWT supporting non-AP STA (but not members)’s transmission?
    non-AP STAs that are not rTWT STAs’ transmission?

## Slide 5: Fairness versus Differentiation
There are many factors to take into account when restricting/limiting/prioritizing the traffic over the rTWT SPs:
  Meet purpose of rTWT: agreement between AP and STAs to delivery latency sensitive traffic when targeted time to meet starts
    For participating AP and STAs, they would and should deliver the traffic of TIDs_L first among any other pending traffic
  The rTWT SP may have additional resource in frequency/spatial resources: MU-MIMO, OFDMA
    E.g. rTWT scheduled STA supports bw80 only and AP operates at BW 160. The upper bw80 would’ve been wasted if we don’t allow AP to schedule DL traffic to other STAs out of rTWT members.
    E.g. rTWT scheduled supports NSS=1 and AP supports 4x4. The other three streams would’ve been wasted if we don’t allow AP to schedule DL traffic other STAs using MU-MIMO
    Same for DL and UL when MU-MIMO/UL-OFDMA allows more opportunities to share resources
  Power saving: rTWT STA may complete transmitting TIDs_L {AP, STA} before the SP finishes and it has frames of other TIDs pending at itself/AP. It’s more power efficient to stay awake to tx/rx them.
  Fairness: while giving “privilege” (albeit limited) to rTWT associated traffic, other STAs hope to get fair chance to rx traffic from AP e.g.
To balance all these factors, prefer to “prioritizing” traffic in TIDs_L rather than “restricting” traffic to be delivered in rTWT SPs only within TIDs_L among rTWT scheduling AP and scheduled STAs
Notes: Fairness vs differentiation or privilege -- how much privilege we give to rTWT members

## Slide 6: Traffic Prioritization Rules for rTWT SP
Discuss two types:
  Trigger enabled rTWT SPs
  Non-trigger enabled rTWT SPs
Discuss the rules for UL / DL traffic of rTWT member STAs, and non-rTWT member STAs

## Slide 7: Trigger-enabled rTWT SPs: UL Traffic (1)
For rTWT scheduling AP: what to transmit?
  Trigger frames (all supported types): basic and BSRP that are for data frame delivery or supporting it (inquiry buffer status), and other types
  Basic trigger: need to trigger selected TIDs in TIDs_L
    General rule: shall prioritize to trigger MSDUs of TIDs_L from rTWT scheduled STAs over {other TIDs of the rTWT scheduled STAs and any MSDUs of other STAs}
  BSRP: similar to above
General problem:
  Basic trigger specified <preferred AC> and doesn’t specify target TID(s)
  BSRP doesn’t specify which TID nor the response as BSR HE control field directly “answer” the question: buffer status for specified TID
  Proposal:
    1) Amend basic trigger to trigger MSDUs of specified TID(s)
    2) Amend BSRP to inquiry buffer status of specified TID(s)
    3) Design BSRP response to provide buffer status for specific TID(s)
  Following discussions assume some form of solution to this problem is there to focus on traffic prioritization rules

## Slide 8: Trigger-enabled rTWT SP: UL Traffic (2)
For rTWT scheduled STAs: what to respond?
  Responding to BSRP:
    Provide buffer status for specified TID(s) (which are supposedly associated with the rTWT membership), and optionally provide buffer status for other TID(s)
    If the buffer status for TIDs_L indicates empty buffer or rTWT scheduled STAs didn’t include buffer status for TIDs_L in responding frame, it is interpreted by the rTWT scheduling AP that the rTWT scheduled STA doesn’t have more pending buffer of TIDs_L in current rTWT SP.  AP may terminate the rTWT SP with this STA using early termination signaling
      Note: failing to receive BS response for a TID doesn’t mean the transmitter side didn’t include them (can be due to CRC error) unless AP knows it receives all MPDUs in the responding A-MPDU correctly

## Slide 9: Trigger-enabled rTWT SP: UL Traffic (3)
For rTWT scheduled STAs: what to respond?
  Responding to basic trigger (or its variant that specify target TID(s)) in order of (permitted by allowed transmission time per UL length):
    Pending MSDUs for the triggered TID(s)
      If there is no more pending MSDUs of the triggered TID, REQUIRED to indicate empty buffer status using HE-control in QoS-Null
      Pending MSDUs of TIDs_L but not trigged TID
      Pending MSDUs of TIDs not in TIDs_L, if any
If the rTWT scheduling AP receives explicit empty buffer status indication for all TIDs in TIDs_L, then AP may terminate the rTWT SP with the corresponding rTWT scheduled STA as needed (if there is enough remaining time)
  Fairness problem: a rTWT scheduled STA can continue respond to AP with TIDs not in TIDs_L and don’t give empty buffer status indication for TIDs_L to get advantage over other traffic/STAs

## Slide 10: Trigger-enabled rTWT SP: Triggering Order
(Proposal) the following rules define the order of {triggered STA, traffic identified by its TID) contained in the basic trigger frame or its variant transmitted by a rTWT scheduling AP during rTWT SPs:
  Consider three sets of (STA, TID):
    Set 1: STAs are rTWT scheduled STA (and haven’t terminated their respective SPs) and haven’t indicated empty BS for all its TIDs in TIDs_L
    Set 2: STAs are rTWT scheduled STA in PS (and haven’t terminated their respective SPs) and haven’t indicated empty BS for all its TIDs in TIDs_L
    Set 3: STAs are rTWT scheduled STAs but not in set 1 nor 2, or STAs are not rTWT scheduled STA for current SP
  Rule: AP should choose the (STA, TID/AC) to trigger first from set 1, next set 2 and lastly set 3 in priority while trying to maximizing the spatial and frequency reuse in the UL TB PPDUs

## Slide 11: Trigger-enabled rTWT: DL Traffic
AP shall prioritize any pending MSDUs of TIDs_L to rTWT scheduled STAs over any other TIDs or to other STAs in the current rTWT SP
The prioritization order is similar to triggering order described in previous slide:
  Consider three sets of (STA, TID):
    Set 1: STAs are rTWT scheduled STAs (and haven’t terminated their respective SPs) and AP has pending MSDUs of TIDs_L for them
    Set 2: STAs are rTWT scheduled STAs (and haven’t terminated their respective SPs), and AP doesn’t have any pending MSDUs of TIDs_L for them
    Set 3: STAs are not rTWT scheduled STAs for current SP, or STAs are rTWT scheduled STA but their respective SPs have been terminated
  Rule: AP should choose the traffic to transmit first from set 1, next set 2 and lastly set 3 while trying to maximizing the spatial and frequency reuse in DL SU or MU PPDU scheduling

## Slide 12: Rules (Or No Rules) for Other STAs
The non rTWT STAs for current rTWT SP can access the channel following the baseline EDCA and MU-EDCA rules, except that
  Additional channel access rules specified in subclause 35.7.3 per D1.1
Such STAs, when gaining channel access, can transmit traffic of their choices

## Slide 13: Non Trigger-enabled rTWT SPs
DL traffic prioritization: same as trigger-enabled rTWT SPs
UL traffic prioritization:
  rTWT scheduled STAs shall first schedule the transmission of MSDUs of TIDs_L.
  If there is no more pending frames of TIDs_L, the rTWT scheduled STAs shall either indicate to AP its readiness to terminate the SP, or request to terminate the SP, or stop scheduling other data frame transmission until the end of the rTWT SP or the rTWT SP is terminated

## Slide 14: Summary
Discuss the gap in trigger frame functionality: lack of TID based triggering and corresponding response
Discuss the rules for prioritizing DL/UL traffic during the trigger-enabled and non-trigger-enabled rTWT SPs