## Slide 1: Discussion of 802E Section 8
Date: 2021-07-14
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1 404 229 1672 | carol@ansley.com

## Slide 2: Abstract
This presentation discusses the recommendations of 802E as it relates to 802.11 and TGbi.
The specific discussion topics within Clause 8 of 802E are covered in detail.

## Slide 3: Agenda
Reminder of PII/PCI
Brainstorming for TGbi Topics
  Use of identifiers / correlatable parameters
  Consideration of potential observers
  Use of parameters
Discussion of potential TGbi amendment text:
  Does the group want to plan on proposing a new annex covering privacy topics as recommended by 802E?

## Slide 4: User Privacy Terms
Do we agree to discuss user privacy in terms of PII and PCI from the Recommended Practice for Privacy Considerations for IEEE 802 Technologies (IEEE Std. 802E-2020)?
Personally Identifiable Information (PII): Any data that directly or indirectly identifies a person or from which the identity or the contact information of a person can be derived.
Personally Correlated Information (PCI): Data gathered about an identified person or small group of people by observing activities (e.g., communications) or events associated with those people.

## Slide 5: Brainstorming based on Clause 8 Device Identifiers/Parameters
What identifiers are required by the service to operate?
Including predictable items: device-provided MAC address(es)
Including associated items: higher layer user IDs, device name, others?
What about location-related items? TGaz-related
Where are they stored?
For how long must they be stored? How long may they be stored?

## Slide 6: Brainstorming based on Clause 8 Parameters
aq pointed out the need for periodic resets of various parameters
Are there other parameters in the newer amendments that might also be significant?
Is there anything looking ahead to TGbe that should be considered? Is the multilink device architecture going to make it easier to gain PII or PCI about a device?

## Slide 7: Brainstorming based on Clause 8 Device Information Persistence/Storage
How long must device identifiers/parameters persist?
Can a user choose the persistence duration?
Where are potential device identifiers stored?
For how long must the identifying data be stored? How long may they be stored?

## Slide 8: Brainstorming based on Clause 8 Observation
We have had several submissions identifying scenarios that may allow an observer to identify and/or track a particular device and by extension its user.
Are there opportunities for a rogue AP to acquire additional information?
Are there opportunities for a rogue STA to acquire additional information?
For example, can a STA determine the location(s) of other STAs?
At a stadium or other large venue, could a STA that legitimately joined the BSS access PII/PCI information about other STAs also at the venue?

## Slide 9: Amendment Structure Discussion
802E recommends that 802 standards add a clause or an informative appendix specifically:
  a) “Description of privacy exposures by answering the questions in Clause 8. These answers should be documented during the development of the standard for readers of the standard. Descriptive text for these answers should be provided in the published clause or an annex in the standard.”
  b) “Guidance on possible implications for implementers of the standard as described in 8.3.”