## Slide 1: TG bh Identifiable Random MAC Address
Date: 2021-09
Authors:

## Slide 2: Intro
This is a preliminary presentation on the idea of an “Identifiable Random MAC Address”, IRMA
More work is proposed, but the initial outline is presented in order to gauge support for such a scheme.

## Slide 3: MAC Addresses
MAC Address 48-bit
Two Types:
  Fixed (Assigned)
  Random
Fixed
  Assigned MAC.
Random
  Two types,
    Non-identifiable - random, STA does not want to be known in any way
    Identifiable – random, but STA wishes to be identified/remembered by particular APs (networks)

## Slide 4: 802.11 Definitions
Identifiable Random MAC (IRM) – A random MAC scheme used by a STA that wants to be identified by the AP (network) it wishes to associate with or an AP(network) with which it wishes to exchange information.
Identifiable Random MAC Address (IRMA) – Random MAC address used by a STA using IRM
Identifiable Random MAC Key (IRMK) – a 128 bit Key used to resolve an IRMA (Note: key could be longer)
IDrand - 22 bits randomly generated bits plus 2 fixed bits (24 bit total) used to generate an IRMA
NOTE: Yes I know, these definitions are not ideal and need to be worked, but please after we have agreement on how the scheme works

## Slide 5: Identifiable Random MAC Address - IRMA
Purpose
  Prevent third-parties from tracking the STA while still allowing trusted parties to recognize the STA.
Identifiable
  Uses a key shared with trusted AP/network – IRMK
    STA generates, or
    Option is that AP could provide an IRMK to a STA, STA generates address (IRMA) using IRMK and a random number (IDrand)
  IRMA consists of 24 bit Hash, 22 bit random and 2 fixed bits*
Changing address
  Address (IRMA) may change as often as needed.
* Could look at other “splits”

## Slide 6: IRMA indication
Two basic random MAC address types:
  Random private (changes randomly, non-identifiable) (RMA?)
  Random identifiable IRMA
MAC Address is 48 bits
  Least significant bit of first octet (“I/G bit”)
    0 = unicast, 1 = multicast
  Second-least-significant bit of the first octet (“U/L bit”)
    0 = globally unique, 1 = locally administered
Random MAC is described in Clause 12.2.10 (D0.0)
  “The STA shall construct the randomized MAC address from the locally administered address space”
    Hence U/L bit set to 1, but I/G bit can be 0 or 1.
Proposal
Let I/G = 0, U/L = 1 indicate IRMA
  If legacy random MAC device sets this, no problem because capability bit not set.
Then use I/G = 1 and U/L = 1 for private random address RMA
  again, no real problem if it sets 0,1 as capability bit not set.
  If capability set, STA can still use 1,1, to indicate RMA.

## Slide 7: Steps to implement privacy
The IRMK (Identifiable Random MAC Key) ) is used in generating and resolving the IRMA (Identifiable Random MAC Address)
When first associated, AP stores STA IRMK.
The IRMK is then used to identify STA by verifying that the hash included in the private address matches the output of the local hash computation
  Details of the hash computation in a later slide
It’s important to note that the IRMK is not used to reveal the STA’s MAC or “identity” Address but rather for verification purposes only, i.e., the hash matches

## Slide 8: CAPABILITY BIT
A Capability bit is set in the STA and AP
A STA may set the IRM capability bit but still use a purely random AC (sets 1,1).
The AP looks for the IRM capability bit AND the (1,0) bits in order to look for the hash
STA sets IRM capability bit AND the (1,0) bits when it wants to be identified.
  Can still set 1,1 if it wants to indicate an RMA.
AP can use the IRM capability bit to indicate to STAs that there may be a reason to be identified, i.e. “I provide a service”

## Slide 9: IRMK and Hash function
The IRMK (Identity Resolving Key) is used in generating and resolving the IRMA.
STA generates the IRMK
  Could be constant, could vary for each SSID, could be preset.
STA shares IRMK with AP when first associated
The IRMK is used to resolve the private address of the STA
  verifies that the hash included in the private address matches the output of the local hash computation
  hash = function (IRMK, IDrand)
Since the AP has the IRMK stored locally and has access to the IDrand included as part of the MAC address in the association packets, it can perform this computation
Looking at best hash function to use.

## Slide 10: Basic scheme for 802.11 devices
STAs and APs indicate IRM capability
Note: An IRMA is identifiable by the two bits in STA’s MAC
First time association:
  When securely associated:
    If STA indicates IRM capability AND 48-bit IRMA (46 “random” + 1,0)
      AP checks to see if IRMK already stored (calculates hash with stored IRMKs)
      If not
      STA provides IRMK via request/response packets
        Option is that AP could provide an IRMK to the STA. (AP may have preferences, and if verifying, may have time out, hence may have reserved list.)
      AP stores STAs IRMK
Pre-association or when associating again, AP sees IRM capability and an IRMA. AP can calculate hash to identify STA IRMK.

## Slide 11: Advantages
A different Random MAC can be used even when returning to same ESS
  STA can re-associate with a “new” random MAC at any time
STA can choose to use private random MAC
Legacy STAs that set (1,0) but do not set IRM capability bit, are not a problem.
AP could provide an IRMK to a STA once associated and accepted (not sure on this as might be less secure if AP has some key ID configuration)
Secure way to be re-identified before association
No reference to any ‘real’ address or identification

## Slide 12: Further work intended
Need to establish and investigate following:
What is best hash function?
Is the 24/24 split the best split? what about 32/16 or other? Would that be better?
What is time/effort involved for 3rd party to find the key?
What's the chance that the AP finds the wrong key?
How does increasing the size of the key help? Is it worth it?
Is there a way to improve the security? Some sort of double key where the key changes each time in a predictable manner if you have the second key? Or some sort of rolling key?

## Slide 13: 10 criteria
Is a private address/identifier dynamic or is it just a different static address/identifier? How often does/should it change?
  Dynamic with selection of the IDrand and can change every time. The hash ID and the IRMK remain constant.
Is it invertible such that the "real" address/identifier can be determined from a private address/identifier
  There is no concept of a “real” address. The IRMK and hash identify the STA.
Does a 3rd party know whether private identifiers are used?
  Yes, the U/L and I/G bits can indicate IRM is in use
Is it assumed that only certain entities can make a binding/track someone?
  Yes the AP must support and the STA makes the decision on whether to provide the IRMK
Yes, STA makes the decision to indicate IRM capability and provide the IRMK
Is the private address/identifier bound to a secure connection or is unencrypted (poss. unassociated) use of this functionality required?
  Bound to a secure connection. Only pass IRMK when associated.
What are the assumptions on forgery of such an address/identifier? How hard does it need to be for someone to fake one?
  IRMK is well protected. 128 bit address and hash function
Are there any requirements to force STAs to do a scheme like this?
  No, entirely up to the STA
What's the probability of collision?
  Very, very, low, 1 in 2^128?
What about protecting client identities from the network?
  Actual ID is not known. Just an Identifier, i.e., the IRMK
What other requirements do we have on usage of this address/identifier (aside from “private”)?
  STA is only indicating it is the same STA as associated before. Also it can change its ID at any time.

## Slide 14: Straw Poll
Do you agree that an Identifiable Random MAC scheme, along the lines as described in <this document>, should be further investigated for possible inclusion in the TGbh Amendment?