## Slide 1: CR for Low-Latency stream identification
Date: 2021-10-14
Authors:

## Slide 2: Abstract
In this contribution, we discuss about how to identify and discriminate latency sensitive traffics, in order to be efficiently transported over 802.11be resource reservation mechanisms (e.g. rTWT).
We propose that latency sensitive streams are identified with an SCSID.

## Slide 3: Motivation
Section “35.7.2.1 Latency sensitive traffic differentiation” of 802.11be D1.1 is empty
There are inconsistencies in 802.11be D1.1 :
  Restricted TWT DL/UL TID Bitmaps (9.4.2.199 TWT element) specify TID(s) identified as latency-sensitive streams
  SCS has been recently re-introduced along with modified TSPEC specification and TCLAS classification, providing a fine identification of latency-sensitive streams.
  =>It seems that a traffic specification is provided (SCS), but no medium access means is setup for accurate transportation
Issue not yet addressed:
  There could have several LL streams on a STA, but also non-LL streams that share same TID/AC as LL streams. Non-LL streams shall not take advantage of medium access offered to LL streams., otherwise unfair !
LL stream: Low-Latency, aka. Latency Sensitive, stream/traffic

## Slide 4: Related CIDs
CID | Commenter | Clause Number | Comment | Proposed Change | 
2513 | Pascal VIGER | 35.6.2.1 | "Latency sensitive traffic differentiation" is not clear enough. As nowadays a end-device is multiple content producer, there shall exist a diferenciation of latency sensitive and not-latency-sensitive traffics (e.g. from local application) belonging to a same TID. Otherwise, considering all traffics belonging TID as identical transportation is unfair ! | as in comment. Please consider fairness by differenciating transportation of LS and non-LS traffic of a same TID | Assigned: Duncan Ho
2523 | Pascal VIGER | 35.4.2 | There is plan to add TSPEC based signaling to provide parameters that describe traffic characteristics within the SCS procedure, especially the low latency (LL) parameters, so that AP shall be able to create an optimal schedule. In order to meet those Low latency requirements, the AP shall be able to finely (or let us say only) trigger the LL data, and not all the pending data of same traffic class or TID (because the remaining traffic remaining in the TID are not-LL sensitive and shall not be conveyed with same means like rTWT). | The LL data shall be managed by SCSID identifier for the communications, that is to say the SCSID is used to discriminate LL data inside a TID and that have to be handled by LL medium access mechanisms: e.g. MU triggering, rTWT use. In complement, the LL data shall be conveyed over multiple links, independently of remaining not-LL traffic. | Assigned: Duncan Ho

## Slide 5: Discussion
3 main elements have to be considered for latency-sensitive stream:
  Buffer status report (BSR) is used to indicate to the AP the amount of data the STA has available in its queues for transmission.
    BSRs takes the form of QoS-Control with Queue Size, or BSR-Control
    BSR can be solicited by a TF
  Trigger Frame is used by AP to control medium access and trigger a specific stream
  Restricted-TWT (rTWT) : UL/DL TID bitmap are under consideration
Current issues:
  BSR:
    BSRs work at AC level (Queue Size subfield, Queue Size All subfield)
  Trigger frame :
    Today, only Preferred AC may be identified
  rTWT:
    Problem is that a TID can also contain non latency sensitive (non-LL) data, thus it is unfair to transport those non-LL data as well as highest-priority LL data.

## Slide 6: Proposal
An LL stream is individually specified by a TSPEC within an SCS Descriptor.
It is therefore required to use the SCSID to qualify the stream in both BSRs and TFs for efficient UL MU operation.

## Slide 7: Example formats to support SCSID
Another contribution discuss about providing an updated BSR for LL traffics (see [2])
Trigger Frame is updated to trigger an SCS stream (through SCSID):
  Applicable only to EHT STAs,
  “Trigger Dependent User Info” Format compatible with HE format
    B5 set to ‘1’ indicates new format, which provides SCSID value
MPDU MU Spacing factor
2
Bits:
TID Aggregation Limit
3
Reserved
1
Preferred AC
2
B0 B1
B2 B4
B5
B6 B7
MPDU MU Spacing factor
2
Bits:
SCSID
part 1
3
Presence of SCSID
1
SCSID
part 2
2
B0 B1
B2 B4
B5
B6 B7
802.11ax format when B5 is Reserved (value 0)
802.11be format when B5 takes value 1

## Slide 8
TWT IE can be adapted to identify an SCS stream:
  Applicable only to EHT STAs,
  Various location possibilities to specify an SCSID:
    inside the ‘Broadcast TWT Info’ field
    inside ‘Restricted TWT Traffic Info’ field
Request Type
2
Octets:
Target Wake Time
2
Nominal Minimum TWT Wake Duration
1
TWT Wake Interval Mantissa
2
Broadcast TWT Info
1
Restricted TWT Traffic Info
0 or 3
B0
B1
B3 B7
B2
DL TID Bitmap Valid
1
Bits:
UL TID Bitmap Valid
1
SCSID Valid
1
Reserved
5
Traffic Info Control
1
Octets:
Restricted TWT DL TID Bitmap
1
Restricted TWT UL TID Bitmap
1
SCSID
1
B0 B2
B3 B7
B8 B15
SCSID
3
Bits:
Broadcast TWT ID
5
Broadcast TWT persistence
8
Figure 9-689b—Restricted TWT Traffic Info field format
Figure 9-689c—Traffic Info Control field format

## Slide 9: Summary
This contribution discussed about the use of SCSID for latency sensitive streams.
Use of SCSID is preferred (instead of AC/TID), because it is:
  Simple and efficient, as SCSID finely identifies streams at AP and STA sides
  Transparent to HE devices, as legacy formats (BSR, TF) are kept
  Fair, as only the identified LL stream is triggered (no other data in TID/AC queue takes advantage of this medium access)

## Slide 10: Straw Poll #1
Do you support that 802.11be makes use of SCSID identification inside BSRs, TFs and rTWT elements for latency-sensitive traffics ?
  Note: result of the strawpoll aims to trigger the resolution of CIDs 2513/2523
Results: Y/N/A

## Slide 11: Reference
[1]. Draft P802.11be_D1.1
[2]. CR for Low Latency BSR: https://mentor.ieee.org/802.11/dcn/21/11-21-1577-00-00be-cr-for-low-latency-bsr.pptx