## Slide 1: Overlaid UL transmissions enabling low latency for emergency use cases
Date: 2021-11-11
Authors:

## Slide 2: Abstract
In this contribution we propose a PHY mechanism for the transmission of emergency data (or other time-critical low-latency data).

## Slide 3: Background
From the PAR:
  “5.2.b Scope of the project: … This amendment defines at least one mode of operation capable of improved worst case latency and jitter.”
  “5.5 Need for the Project: … (e.g., latency lower than 5 ms for realtime gaming).”
Several MAC contributions address low latency, e.g.,
  Restricted TWT [1]
  Modifying the STA’s behavior upon packet failures [2]
  Traffic differentiation [3] and traffic indication of low latency applications [4]
  Low latency resource agreements [5]
We believe that mechanisms in the PHY layer provide room for improvements
In this presentation we consider rare events of extremely time critical data
  For example, signaling an emergency signal (e.g. “emergency stop”) in industrial use cases

## Slide 4: Problem: Emergency traffic & Triggered Based operation
TXOP duration
Best effort: Any type of traffic without strict priority and reliability requirements
Emergency: May arrive at any time with high priority requirements
  Requires low latency, immediate transmission
AP
STA1
Best effort
STA2
Emergency
PPDU1
PPDU2
TF
PPDU1
AP
STA1
STA2
Data for PPDU2
PPDU2
BA
At worst, an ongoing TXOP delays the emergency transmission for several ms
Defer from channel access

## Slide 5: Proposal: Allow emergency traffic to be “overlaid”
High priority access allowed
The AP initiates a TB PPDU
  Triggers STA1’s transmission with a TF
  AP allows STA2 to transmit emergency data during PPDU1
Upon receiving the Trigger Frame
  STA2 understands that it is permitted to transmit an emergency packet during the ongoing TXOP
AP
STA1
Best effort
STA2
Emergency
PPDU1
PPDU2
TXOP duration
TF
PPDU1
AP
STA1
STA2
Data for PPDU2
PPDU2
BA

## Slide 6: Well balanced requirements & consequences
AP needs to permit STA2 to perform an “overlaid” transmission
  Requires adding an indication in the Trigger Frame
AP needs to continue Preamble Detection during reception of PPDU1
PPDU2 needs to be received with at least the same power as PPDU1
  ~0 dB SINR is sufficient to decode low MCS PPDUs
  Fair to assume emergency (high priority) data comes from a device with “good” connection
Parts of PPDU1 will fail, but some MPDUs may succeed
  Reasonable price to pay for prioritizing emergency data
  Can be combined with ideas in [6] to better allow for parts of PPDU1 to be successful

## Slide 7: SP1
Do you think TGbe should consider PHY features for improved emergency-traffic support in release 2?
Yes:
No:
Abstain:

## Slide 8: SP2
Do you think ”overlaid” transmissions as described in this presentation could be a candidate feature to better support emergency traffic in P802.11be TGbe release 2?
Yes:
No:
Abstain:

## Slide 9: References
[1] 11-21/34r4 Quality of Service for latency sensitive traffic
[2] 11-20/1691r2 A TXOP rule to reduce worst-case latency
[3] 11-20/1852r2 Discussion on low latency traffic
[4] 11-20/1067r8 Traffic indication of latency sensitive applications
[5] 11-20/1670r2 Low-latency resource agreements
[6] 11-21/0670r0 Further Improve Latency Performance in 11be