## Slide 1: Redundant Transmission over ML for Low Latency Traffic
Date: 2021-11-12
Authors:

## Slide 2: Background
Restricted TWT is introduced to support RTA traffic in 11be.
  rTWT will work fine for periodic RTA traffic
From AP point of view, interval of DL RTA traffic burst is changing along with the situation of the network busy status between the AP and the peer point.
Interval of some RTA UL traffic burst may be changing along with the APP running.
The data volume of RTA traffic burst may be changing along with the RTA APP running.
The rTWT SP should be set long enough to cover the interval changing or data volume of RTA traffic changing to meet the low latency requirements.
  This leads to impact to the BSS.

## Slide 3: Background
3GPP New Radio introduces PDCP PDU duplication transmission over multiple cells for URLLC (Ultra Reliable Low Latency Communications).
  Copies of a PDCP PDU are concurrently delivered to be transmitted over multiple cells and stopped as soon as there is a copy transmitted successfully.
  The latency of the PDCP PDU is the latency of the copy first successfully transmitted.
Multi-link is introduced in 11be.
  To have low latency, redundant transmission over multiple links between 2 MLDs can be utilized as a supplementary to rTWT.
  Redundant transmission over multiple links between 2 MLDs means copies of a MPDU are transmitted concurrently over multiple links between 2 MLDs.

## Slide 4: Discussion
rTWT SP can be set with a proper duration to afford most of the RTA traffic bursts and to keep the impact to the BSS small. RTA data that are not transmitted during the rTWT SP because of late arrival or bigger data volume can be redundantly transmitted over multiple links to meet the latency requirements.
MLO fits for redundant transmission over multiple links
  Acknowledgement across links
  Duplication detection
Over which links the redundant transmission is applied?
  TID mapped links, or subset of TID mapped links

## Slide 5: Proposal
Redundant transmission of MPDU over multiple links between 2 MLDs is introduced in 11be.

## Slide 6: SP1
Do you support to introduce redundant transmission of MPDU over multiple links between 2 MLDs in 11be?
  Option 1, Yes
  Option 2, No
  Option 3, Abstain