## Slide 1: CR for PAR throughput verification
Authors:
Name | Affiliations | Address | Phone | Email
Yiqing Li | Huawei | Shenzhen, China |  | liyiqing3@Huawei.com
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Ming Gan |  |  |  | 
Jian Yu |  |  |  | 
Guogang Huang |  |  |  | 
Yuxin Lu |  |  |  | 
Yousi Lin |  |  |  | 
Date: 2021-11-05

## Slide 2: CID 7619
CID | Commenter | Clause Number | Page. Line | Comment | Proposed Change | Resolution
7619 | Tomoko Adachi |  |  | Verification is needed to see how much throughput can be achieved by R1 features. By doing this, we can think of how to achieve 30 Gb/s throughput and what kind of features are required at the end in P802.11be. | As in the comment. | 

## Slide 3: PAR
Doc: 11-18-1231-06-802.11 EHT Proposed PAR[1]
  Capable of supporting a maximum throughput of at least 30 Gbps, as measured at the MAC data service access point (SAP), with carrier frequency operation between 1 and 7.250 GHz while ensuring backward compatibility and coexistence with legacy IEEE Std. 802.11 compliant devices operating in the 2.4 GHz, 5 GHz, and 6 GHz bands
  at least one mode of operation capable of improved worst case latency and jitter.

## Slide 4: How much throughput can be achieved by R1 features
R1 features that are considered in the simulation.
  Multi-Link, 4KQAM, 1024 MPDU Aggregation per A-MPDU, 320MHz
Throughput is measured at MAC data SAP.
Simulation Setup Parameters | Default value
The number of AP MLD | 1
The number of non-AP MLD | 8
The size of area | 20m*20m
Traffic type | Full buffer UL/DL traffic
Packet size | 1500 Byte per MPDU
TX power | 20dbm for AP MLD; 15dbm for non-AP MLD
NSS | 8
CWmax | 15
CWmin | 7
AIFS | 34us
The number of links | 2 (5GHz&6GHz)
TXOP | 4.096ms
RTS/CTS | on
AP 1
AP 2
STA 1
STA 2
AP MLD 1
Non-AP MLD 1
Link 1
Link 2
PPDU
PPDU
ACK
ACK
Simple scenario: 1 AP MLD and 1 non-AP MLD
Topology: 20m*20m

## Slide 5: With one R1 feature
Simulation cases | Aggregation | Link # | Bandwidth (MHz) | QAM
Case 1-1 | 256 | 1 | 160 | 1K
Case 1-2 | 1024 | 1 | 160 | 1K
Case 1-3 | 256 | 1 | 160 | 4K
Case 1-4 | 256 | 1 | 320 | 1K
Case 1-5 | 256 | 2 (160MHz for link 1 + 160MHz for link 2) | 160 | 1K
The combination of 11ax features, i.e., 256 aggregation for A-MPDU, one link with 160MHz bandwidth, 1KQAM is set as the baseline and is labeled as case 1-1.
For MU case, each non-AP MLD is 1 NSS with 8 non-AP MLDs in total.
With one R1 feature, all cases fail to reach 30Gbps.
Case 1-4 and Case 1-5 have higher throughput. 320MHz and Multi-Link features have better performance.
  The gain increases in order as 4KQAM, 1024 aggregation, 320MHz, Multi-Link.
Chart: Throughput/Mbps
| Case 1-1 | Case 1-2 | Case 1-3 | Case 1-4 | Case 1-5
DL SU | 5522.1 | 7817.58 | 6165.336 | 7938.756 | 11062.26
UL SU | 5525.1 | 7785.276 | 6174.756 | 7830.18 | 11075.652
DL MU | 7667.1 | 8475.96 | 8873.124 | 12970.968 | 15331.08
UL MU | 8384.484 | 8891.136 | 9858.912 | 15133.884 | 16762.956
Gain versus Case 1-1 | Case 1-2 | Case 1-3 | Case 1-4 | Case 1-5
DL SU | 41.57% | 11.65% | 43.76% | 100.33%
UL SU | 40.91% | 11.76% | 41.72% | 100.46%
DL MU | 10.55% | 15.73% | 69.18% | 99.59%
UL MU | 6.04% | 17.86% | 80.50% | 99.93%

## Slide 6: With two combined R1 features
Simulation cases | Aggregation | Link # | Bandwidth(MHz) | QAM
Case 2-1 | 1024 | 1 | 320 | 1K
Case 2-2 | 1024 | 2 (160MHz for link 1 + 160MHz for link 2) | 160 | 1K
Case 2-3 | 1024 | 1 | 160 | 4K
Case 2-4 | 256 | 2 (320MHz for link 1 + 160MHz for link 2) | 320 | 1K
Case 2-5 |  | 2 (320MHz for link 1 + 320MHz for link 2) |  | 
Case 2-6 | 256 | 2 (160MHz for link 1 + 160MHz for link 2) | 160 | 4K
Case 2-7 | 256 | 1 | 320 | 4K
With two combined R1 features, only case 2-5 with two links as 320MHz for UL MU has reached 30Gbps and other cases fail to reach 30Gbps.
  Due to higher transmission efficiency.
Chart: Throughput/Mbps
| Case 2-1 | Case 2-2 | Case 2-3 | Case 2-4 | Case 2-5 | Case 2-6 | Case 2-7
DL SU | 13678.896 | 15517.092 | 9166.296 | 13474.524 | 15642.528 | 12239.64 | 8571.756
UL SU | 13668.12 | 15624.708 | 9167.904 | 13360.956 | 15639.996 | 12317.376 | 8506.296
DL MU | 16883.292 | 16952.844 | 10167.852 | 20618.196 | 25922.196 | 17747.652 | 14665.824
UL MU | 17680.14 | 17783.7 | 10667.952 | 23548.656 | 30283.68 | 19722.348 | 17492.292
Gain versus Case 1-1 | Case 2-1 | Case 2-2 | Case 2-3 | Case 2-4 | Case 2-5 | Case 2-6 | Case 2-7
DL SU | 147.71% | 180.99% | 65.99% | 144.01% | 183.27% | 121.65% | 55.22%
UL SU | 147.38% | 182.80% | 65.93% | 141.82% | 183.07% | 122.93% | 53.96%
DL MU | 120.20% | 121.11% | 32.61% | 168.91% | 238.09% | 131.48% | 91.28%
UL MU | 110.87% | 112.10% | 27.23% | 180.86% | 261.19% | 135.22% | 108.63%

## Slide 7: With three or four combined R1 features
Simulation cases | Aggregation | Link # | Bandwidth (MHz) | QAM
Case 3-1 | 1024 | 1 | 320 | 4K
Case 3-2 | 256 | 2(320MHz for link 1 + 160MHz for link 2) | 320 | 4K
Case 3-3 |  | 2(320MHz for link 1 + 320MHz for link 2) |  | 
Case 3-4 | 1024 | 2(160MHz for link 1 + 160MHz for link 2) | 160 | 4K
Case 3-5 | 1024 | 2(320MHz for link 1 + 160MHz for link 2) | 320 | 1K
Case 3-6 |  | 2(320MHz for link 1 + 320MHz for link 2) |  | 
Case 4-1 | 1024 | 2(320MHz for link 1 + 160MHz for link 2) | 320 | 4K
Case 4-2 |  | 2(320MHz for link 1 + 320MHz for link 2) |  | 
With three combined R1 features, case 3-3 for UL MU, case 3-6 for MU cases have reached 30Gbps.
With four combined R1 features, case 4-2 for both MU and SU cases has reached 30Gbps.
Multiple links with 320MHz improve throughput apparently.
  Case 4-2 has 262.77%, 270.36%, 373.70%, 401.76% throughput gain in DL SU, UL SU, DL SU and UL MU respectively compared with case 1-1 with four R1 features combined.
Chart: Throughput/Mbps
| Case 3-1 | Case 3-2 | Case 3-3 | Case 3-4 | Case 3-5 | Case 3-6 | Case 4-1 | Case 4-2
DL SU | 15701.292 | 14734.092 | 17155.356 | 18322.452 | 21473.1 | 26710.884 | 24748.632 | 30416.124
UL SU | 15537.12 | 14688.96 | 16954.932 | 18302.82 | 21435.108 | 27109.2 | 24881.124 | 31052.58
DL MU | 19830.216 | 23495.076 | 29257.692 | 20341.98 | 25307.352 | 33764.376 | 30041.376 | 39717.168
UL MU | 21012.6 | 27356.004 | 34998.552 | 21331.968 | 26659.908 | 35457.072 | 31669.896 | 42069.828
Notes: Sounding overhead?

## Slide 8: Throughput performance with varying traffic rate
Adopt 1024 aggregation for A-MPDU, 2 links (320MHz for link 1 + 320MHz for link 2), 320MHz and 4KQAM in UL MU MIMO case. Vary the traffic rate and the number of non-AP MLDs.
Traffic Rate (Gbps) | 0.1 | 3.5 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22
2 non-AP MLDs | 0.19974 | 6.98244 | 8.1027 | 15.0123 | 19.6703 | 22.9616 | 25.4602 | 27.4043 | 28.9793 | 31.3975 | 32.8893 | 34.2942 | 35.0681 | 35.1356 | 35.1077
4 non-AP MLDs | 0.39984 | 13.973 | 16.0045 | 23.5776 | 29.1083 | 32.4679 | 35.4538 | 37.4762 | 38.884 | 39.2018 | 39.416 | 39.3573 | 39.178 | 39.2449 | 39.3014
8 non-AP MLDs | 0.7992 | 27.8695 | 31.5976 | 39.9895 | 41.3457 | 41.5174 | 41.8953 | 41.3567 | 41.6605 | 41.9004 | 41.6343 | 41.7427 | 41.8355 | 41.4449 | 41.5577
Chart: Traffic rate/Gbps
| 0.1 | 3.5 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22
2 non-AP MLDs | 0.19974 | 6.9824 | 8.1027 | 15.0123 | 19.6703 | 22.9616 | 25.4602 | 27.4043 | 28.9793 | 31.3975 | 32.8893 | 34.2942 | 35.0681 | 35.1356 | 35.1077
4 non-AP MLDs | 0.39984 | 13.973 | 16.0045 | 23.5776 | 29.1083 | 32.4679 | 35.4538 | 37.4762 | 38.884 | 39.2018 | 39.416 | 39.3573 | 39.178 | 39.2449 | 39.3014
8 non-AP MLDs | 0.7992 | 27.8695 | 31.5976 | 39.9895 | 41.3457 | 41.5174 | 41.8953 | 41.3567 | 41.6605 | 41.9004 | 41.6343 | 41.7427 | 41.8355 | 41.4449 | 41.5577
Traffic rate is the packet generation ratio for all links at the transmitter.
In this UL MU MIMO case, each non-AP MLD are 4 NSS when the number of non-AP MLDs is 2. Similarly, 2 NSS for each non-AP MLD when there are 4 non-AP MLDs and 1 NSS for each non-AP MLD with total 8 non-AP MLDs.
Throughput increases with increasing traffic rate until it reaches the saturation due to the limited PHY data rate since the bandwidth, MCS and NSS are fixed.
Throughput increases with increasing number of non-AP MLD due to the transmission overhead in MU cases.
  Larger number of non-AP MLD reaches throughput saturation faster.

## Slide 9: Summary
The contribution provides simulation results to show how much throughput can be achieved by R1 features.
  Multi-Link, 4KQAM, 1024 Aggregation for A-MPDU, 320MHz bandwidth
From the results, at least two links both with 320MHz and 1024 aggregation for MU case has reached 30Gbps. All four R1 features guarantee 30Gbps for SU and MU cases.
  Generally, the throughput gain increases in order as 4KQAM, 1024 aggregation, 320MHz, Multi-Link feature. Multi-Link has apparent gain while 4KQAM improvement is limited. 1024 aggregation and 320MHz have respective pros and cons.
Improving transmission efficiency results in throughput improvement. Either speeding up the transmitting procedure or increasing effective transmission can be simple but efficient ways.

## Slide 10: Reference
11-18-1231-06-802.11 EHT Proposed PAR