## Slide 1: Consideration on EDCA Operation for Restricted TWT
Date: 2021-11-15
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Lei Huang |  |  |  | 
Chaoming Luo |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
Several comments on r-TWT concern the protection of r-TWT SPs for the transmission of latency sensitive traffic, and the fairness issue for r-TWT member STAs and non-member STAs.
This document proposes a candidate mechanism to differentiate the EDCA operations during or outside of r-TWT SPs for r-TWT scheduled STAs and r-TWT unscheduled STAs.

## Slide 3: Issues
CID | Commenter | Clause | Pg/Ln | Comment | Proposed Change
5877 | Liangxiao Xin | 35.6.4 | 298.37 | Which EDCAF should be used for the channel contention of R-TWT SP? If we use the existing EDCAF, it mixes the purposes of channel contention for non-latency sensitive traffic and latency sensitive traffic | add a new EDCAF for the channel contention of R-TWT SP only.
5879 | Liangxiao Xin | 35.6.4 | 298.37 | fast channel access and the fairness issue should be considered for a R-TWT member STA. While STA should have higher priority to access the channel during R-TWT SP, it should lower its priority to access the channel outside R-TWT SP. | change the EDCA and MU-EDCA of ACs at R-TWT member STAs to accesserate their channel access during a R-TWT SP and slow down their channel access for a period of time after a R-TWT SP.
6547 | Patrice Nezou | 35.6.4 | 298.40 | A medium access mechanism has to be specified during the TWT service period. | Use dedicated EDCA parameters during the TWT service period to optimize bandwidth usage.
6356 | Mohamed Abouelseoud | 35.6.4 | 298.37 | Currently the scheduled RTWT is not guarnteed to start at the scheduled time. Non-AP EHT STAs and future 802.11 deviced can ignore the quite element and gain access to the channle. | define a procedure to increase the chance of the AP or the members of the RTWT gaining access to the channel to start the RTWT
7865 | Yonggang Fang | 35.6.4 |  | The clause 35.6.4 is about channel access rules for restricted TWT. However, no channel access rule has been defined to support time sensitive traffic to access to media in the restricted TWT SP. | Please specify channel access mechanisms and rules to be used for time sensitive traffic in restricted TWT SP.

## Slide 4: Discussion
The protection mechanism of r-TWT SPs specified in 11be Draft 1.3 seems to be not enough, which would impact the scheduled transmission of latency sensitive traffic during the r-TWT SPs.
  All STAs can still access the SP using EDCA except certain rules applied to a trigger-enabled SP
  the Non-AP EHT STAs may behave as if overlapping quiet intervals do not exist, which means that the unscheduled EHT STAs may contend for channel access during the SPs.
  the support for the quiet function with the Quiet element is also optional for the legacy STAs, which means that the legacy STAs would also contend for the channel access during the SPs when not supporting the quiet function.
  A quiet interval for this protection purpose is only 1 TU and expect a r-TWT SP is commonly at least a few msecs.
The comments made in the list of CIDs on Slide 3 are reasonable.
The NSEP priority access in 11be Draft 1.3 also specified the action frames to adjust the EDCA Parameters Set of authorized non-AP STAs for priority access, which can be regarded as a reference for the suggested function.

## Slide 5: Candidate Solution
Differentiate EDCA operations for different roles of EHT STAs supporting r-TWT in different time intervals
r-TWT scheduled STAs during the SPs
r-TWT scheduled STAs outside of SPs
r-TWT unscheduled STAs during the SPs
r-TWT unscheduled STAs outside of SPs
Note: r-TWT unscheduled STA is an EHT STA that is not a member of this SP
Add an optional mechanism for the configuration of EDCA Parameter Sets during the SPs or outside of SPs for different roles of EHT STAs
EDCA parameters of r-TWT scheduled STAs and unscheduled STAs during r-TWT SPs would lead to:
higher priority of the ACs corresponding to r-TWT UL TID(s) of r-TWT scheduled STAs
disallowed or reduced channel access for the associated MPDUs of other ACs of r-TWT scheduled STAs
disallowed channel access for r-TWT unscheduled STAs
EDCA parameters of r-TWT scheduled STAs and unscheduled STAs outside of r-TWT SPs would lead to:
disallowed or reduced channel access for the associated MPDUs of the ACs corresponding to r-TWT UL TID(s) of r-TWT scheduled STAs
lower priority or the same level of priority as r-TWT unscheduled STAs’ for channel access of the associated MPDUs of other ACs of r-TWT scheduled STAs
higher priority of channel access for r-TWT unscheduled STAs

## Slide 6: Candidate Solution
Define a new element - Restricted TWT EDCA Parameter Set element
Order | Information | Notes
<Last assigned + 1> | Restricted TWT EDCA Parameter Set | The Restricted TWT EDCA Parameter Set element is optionally present if dot11RestrictedTWTOptionImplemented is true.
Table 9-32—Beacon frame body
Table 9-39—Probe Response frame body
Order | Information | Notes
<Last assigned + 1> | Restricted TWT EDCA Parameter Set | (#5877)The Restricted TWT EDCA Parameter Set element is optionally present if dot11RestrictedTWTOptionImplemented is true.
 | Element ID | Length | Element ID extension | EDCA Parameter Set Presence Bitmap | EDCA Parameter Set for r-TWT Scheduled STAs In SPs | EDCA Parameter Set for r-TWT Scheduled STAs Outside SPs (optional) | EDCA Parameter Set for r-TWT Unscheduled STAs In SPs (optional) | EDCA Parameter Set for r-TWT Unscheduled STAs Outside SPs (optional)
Octets: | 1 | 1 | 1 | 1 | 20 | 0 or 20 | 0 or 20 | 0 or 20
Figure 9-xxx –Restricted TWT EDCA Parameter Set element format

## Slide 7: Candidate Solution
The EDCA Parameter Set for r-TWT Scheduled STAs In SPs field specifies the EDCA Parameter Set for r-TWT scheduled STA(s) during SPs by the EDCA Parameter Set element.
Mandatorily present
The EDCA Parameter Set for r-TWT Scheduled STAs Outside SPs field specifies the EDCA Parameter Set for r-TWT scheduled STA(s) outside of SPs by the EDCA Parameter Set.
Optionally present, and the default EDCA Parameter Set is used if not present
The EDCA Parameter Set for r-TWT Unscheduled STAs In SPs field specifies the EDCA Parameter Set for r-TWT unscheduled STAs during SPs by the EDCA Parameter Set element.
Optionally present, and the default EDCA Parameter Set is used if not present
The EDCA Parameter Set for r-TWT Unscheduled STAs Outside SPs field specifies the EDCA Parameter Set for r-TWT unscheduled STAs outside of SPs by the EDCA Parameter Set element
Optionally present , and the default EDCA Parameter Set is used if not present
 | Element ID | Length | Element ID extension | EDCA Parameter Set Presence Bitmap | EDCA Parameter Set for r-TWT Scheduled STAs In SPs | EDCA Parameter Set for r-TWT Scheduled STAs Outside SPs (optional) | EDCA Parameter Set for r-TWT Unscheduled STAs In SPs (optional) | EDCA Parameter Set for r-TWT Unscheduled STAs Outside SPs (optional)
Octets: | 1 | 1 | 1 | 1 | 20 | 0 or 20 | 0 or 20 | 0 or 20
Figure 9-xxx –Restricted TWT EDCA Parameter Set element format

## Slide 8: Candidate Solution
Restricted TWT service periods announcement
If there is any restricted TWT agreement set up, the EHT AP shall announce the restricted TWT service period schedule information in the broadcast TWT element that carries one or more Restricted TWT Parameter Set fields, and the optional Restricted TWT EDCA Parameter Set element contained in transmitted Management frames.
EDCA operation during or outside of restricted TWT service periods
—During the restricted TWT service periods, the r-TWT scheduled STAs update its CWmin[AC], CWmax[AC], AIFSN[AC], and TXOP[AC] state variables to the values provided in the EDCA Parameter Set for r-TWT Scheduled STAs In SPs field of the Restricted TWT EDCA Parameter Set element
—During the restricted TWT service periods, the r-TWT unscheduled STAs update its CWmin[AC], CWmax[AC], AIFSN[AC], and TXOP[AC] state variables to the values provided in the EDCA Parameter Set for r-TWT Unscheduled STAs In SPs field of the Restricted TWT EDCA Parameter Set element - optional
—Outside of the restricted TWT service periods, the r-TWT scheduled STAs update its CWmin[AC], CWmax[AC], AIFSN[AC], and TXOP[AC] state variables to the values provided in the EDCA Parameter Set for r-TWT Scheduled STAs Outside SPs field of the Restricted TWT EDCA Parameter Set element. -optional
—Outside of the restricted TWT service periods, the r-TWT unscheduled STAs update its CWmin[AC], CWmax[AC], AIFSN[AC], and TXOP[AC] state variables to the values provided in the EDCA Parameter Set for r-TWT Unscheduled STAs Outside SPs field of the Restricted TWT EDCA Parameter Set element. –optional

## Slide 9: Summary
The protection mechanism for r-TWT SPs needs to be improved for the effectiveness of r-TWT as well as considering of the fairness among R-TWT member STAs and non-member STAs.
This document proposes a candidate mechanism to differentiate the EDCA Parameter Sets during or outside of Restricted TWT SPs adopted by r-TWT scheduled STAs and r-TWT unscheduled STAs.

## Slide 10: SP 1
Do you agree that a mechanism to differentiate the EDCA Parameter Sets during or outside of Restricted TWT SPs adopted by r-TWT scheduled STAs and r-TWT unscheduled STAs is specified in R1?
Liuming Lu (OPPO)

## Slide 11: SP 2
Do you agree that a mechanism to differentiate the EDCA Parameter Sets during or outside of Restricted TWT SPs adopted by r-TWT scheduled STAs and r-TWT unscheduled STAs is specified in R2?
Liuming Lu (OPPO)