## Slide 1: Regulatory concern of 11bc in Japan
Date:2021-11-30
Authors:

## Slide 2: Abstract
This document describe a regulatory concern of 11bc in Japan.

## Slide 3: Operation mode
Japanese radio regulations defines five commutation operation methods as follows.
1. Single-way
  A Single-way system is a system in which only transmissions are made to a single receiver.
2. Simplex
  Simplex transmission is a method of communication in which transmissions are made alternately in opposite directions.
3. Duplex
  A duplex system is one in which transmissions are made simultaneously in opposite directions.
4. Half-Duplex
  A half-duplex system is a system in which the transmission is simplex at one end of the communication channel and duplex at the other end.
5. Simultaneous communication system
  A simultaneous communication system means a communication system in which only the transmission of a call with the same content is made to two or more specific receiving facilities simultaneously.

## Slide 4: Equipment regulation or wireless LAN system
The WLAN system shall be operated in single-way, simplex, duplex, half-duplex, or combination of those.
Simultaneous communication system is not adopted for WLAN.
There are no any reasons why a simultaneous communication system is not adopted.
No one expected to use WLAN for simultaneous communication systems when this regulation was drafted.
The equipment regulation is a regional (country)specific issue.
At least Japan has this issue at this moment, and FCC does not have it.
In Japan, we are discussing with MIC and, they may change the regulation to address the market requirement.

## Slide 5: Request for information
Call for relevant information in other regulatory area.