## Slide 1: PHY Type Subfield
Date: 2022-01-17
Authors:

## Slide 2: Abstract
This presentation is a discussion material for PHY Type subfield in the EBCS ANQP element and the EBCS Info frame.

## Slide 3: Why need PHY Type Subfield?
To advertise TX rate to receivers
  TX rate format depends on PHY type.
In 2.4GHz / 5GHz / 60GHz band
  Need to specify PHY type.
In other bands
  No need to specify PHY type?
  Should we consider future extension of the band usage?
    New PHY will be defined in the same band.

## Slide 4: Proposed Resolution
Remain PHY Type subfield.
Restrict the PHY types depend on the operating band.
Value | Operating band |  |  |  |  |  |  |  |  |  | 
Value | TV white spaces | Sub-1 GHz (excluding TV white spaces) | 2.4 GHz | 3.6 GHz | 4.9 GHz | 5 GHz | 6 GHz | 45 GHz | 60 GHz | Chinese 60 GHz | Light
0 | TVHT | S1G | DSSS, HR/DSSS, OFDM, ERP | OFDM | OFDM | OFDM | Reserved | CMMG | DMG | CDMG | LC
1 | Reserved | Reserved | HT | Reserved | Reserved | HT | Reserved | Reserved | EDMG | Reserved | Reserved
2 | Reserved | Reserved | Reserved | Reserved | Reserved | VHT | Reserved | Reserved | Reserved | Reserved | Reserved
3 | Reserved | Reserved | HE | Reserved | Reserved | HE | HE | Reserved | Reserved | Reserved | Reserved
4-255 | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved

## Slide 5: Example Use Case in a Stadium
AP
.11a STA
.11ac STA
EBCS Info (OFDM)
EBCS Data frame for traffic 1 (Video streaming, VHT)
EBCS Data frame for traffic 2 (Video streaming, VHT)
EBCS Data frame for traffic 3 (Stadium Directory, OFDM)
I cannot consume video streaming but I can consume stadium directory.
I can consume video streaming and stadium directory.
VHT is used to transmit video streaming to reduce air-time occupation.