## Slide 1: WLAN SENSING USE CASES
Date: 2022-01-17
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Use Cases to consider (when initiator=transmitter)
Sensing Initiator
Sensing Transmitter
Sensing PPDU transmission
Sensing measurements transmission
Sensing Initiator
Sensing Transmitter
Use Case 1: (supported by current SFD)
AP= sensing initiator/transmitter
11bf compatible STA=sensing responder/receiver
Sensing measurements (e.g. CSI) fed back to initiator
Sensing result (e.g. breathing, fall-down) computed by initiator based on sensing measurements
Use Case 2: (yet to be supported by SFD)
AP= sensing initiator/transmitter
11bf compatible STA=sensing responder/receiver
No sensing measurements (e.g. CSI) feedback
Sensing results computed by responder based on sensing measurements. The results may be used by responder or sent elsewhere.
Sensing Responders
Sensing Receivers
Sensing Responders
Sensing Receivers

## Slide 3: Use Cases to consider (when initiator=transmitter)
Sensing Responder
Sensing Receiver
Sensing PPDU transmission
Sensing measurements transmission
Sensing Initiator
Sensing Transmitter
Use Case 3: (supported by current SFD)
AP=sensing responder/receiver
11bf compatible STA=sensing initiators/transmitters
Sensing measurements (e.g. CSI) fed back to initiator
Sensing results (e.g. breathing, fall-down) computed by initiator based on sensing measurements
Use Case 4: (yet to be supported by SFD)
AP=sensing responder/receiver
11bf compatible STA=sensing initiators/transmitters
No sensing measurement (e.g. CSI) feedback
Sensing results computed by responder (AP) based on sensing measurements.
Sensing Initiator
Sensing Transmitter
Sensing Responder
Sensing Receiver

## Slide 4: Use Cases to consider (when initiator=receiver)
Sensing Initiator
Sensing Receiver
Sensing PPDU transmission
Sensing measurements transmission
Use Case 5: (supported by current SFD)
AP=sensing initiator/receiver
11bf compatible STA=sensing responders/transmitters
Sensing measurements obtained at initiator
Sensing results (e.g. breathing, fall-down) computed by initiator based on sensing measurements
Sensing Responder
Sensing Transmitter
Use Case 6: (supported by current SFD)
AP= sensing responder/transmitter
11bf compatible STA=sensing initiators/receivers
Sensing measurements obtained at initiator
Sensing results (e.g. breathing, fall-down) computed by initiator based on sensing measurements
Sensing Initiator
Sensing Receiver
Sensing Responder
Sensing Transmitter

## Slide 5: Use Cases to consider (SBP)
Sensing Initiator
Sensing Transmitter
Sensing PPDU transmission
Sensing measurements transmission
Use Case 7: (supported by SFD)
Sensing by Proxy (SBP)
AP= sensing initiator/transmitter
11bf compatible STA=sensing responder/receiver
Sensing measurements (e.g. CSI) fed back to SBP-requesting STA
Sensing Responder
Sensing Receiver
SBP requesting STA
SBP request
Sensing Initiator
Sensing Receiver
Use Case 8: (supported by SFD)
Sensing by Proxy (SBP)
AP= sensing initiator/receiver
11bf compatible STA=sensing responder/transmitter
Sensing measurements (e.g. CSI) fed back to SBP-requesting STA
Sensing Responder
Sensing Transmitter
SBP requesting STA

## Slide 6: Use Cases to consider (SBP)
Sensing Initiator
Sensing Transmitter
Sensing PPDU transmission
Sensing measurements transmission
Use Case 9: (yet to be supported by SFD)
Variant of SBP in Case 7.
No sensing measurement (e.g. CSI) feedback
Sensing results computed by responders based on sensing measurements.
Sensing Responder
Sensing Receiver
SBP requesting STA
SBP request
Sensing Initiator
Sensing Transmitter
Use Case 9b: (yet to be supported by SFD)
Similar to Case 9, but with PPDU broadcasted with identical sensing measurement setup.
No sensing measurement (e.g. CSI) feedback
Sensing results computed by responders based on sensing measurements.
Sensing Responder
Sensing Receiver
SBP requesting STA
Broadcast
Broadcast

## Slide 7: Straw Poll (SP1)
Do you agree that 802.11bf should support Case 2 in Slide 2?
Yes
No
Abstain

## Slide 8: Straw Poll (SP2)
Do you agree that 802.11bf should support Case 4 in Slide 3?
Yes
No
Abstain

## Slide 9: Straw Poll (SP3)
Do you agree that 802.11bf should support Case 9 in Slide 6?
Yes
No
Abstain

## Slide 10: Straw Poll (SP4)
Do you agree that 802.11bf should support Case 9 with broadcast (i.e. Case 9b), and Case 2 with broadcast?
Yes
No
Abstain