## Slide 1: Proposed 11bi Requirements
Date: 2022-01-18
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Johannes Berg |  |  |  | 
Ilan Peer |  |  |  | 
Ido Ouzieli |  |  |  | 
Emily Qi |  |  |  | 
Ehud Reshef |  |  |  | 
Necati Canpolat |  |  |  | 
Daniel F Bravo |  |  |  | 
Robert Stacey |  |  |  | 
Alexander Danny |  |  |  | 
Ben-Ari Danny |  |  |  | 
Preston Hunt |  |  |  | 
Notes: September 2012

## Slide 2: Background
11bi has settled down on issues to be resolved [1] and the template of the requirements document [2]
We discuss the proposed requirements for issue 2 (Avoid Element Fingerprint) and issue 3 (STA MAC address persistence within an ESS) [1] in this submission

## Slide 3: Issue 2: Avoid Element Fingerprint
Element fingerprint is one of the key issues that motivate the formation of 11bi
  A large number of elements carried in an unprotected management frame may provide sufficient entropy as a fingerprint of a device/user [1]
  From the client’s perspective, Probe Request frame, (Re)Association Request frame carry the largest number of elements in clear including all capabilities, operation parameters, or vendor specific indication, so we focus on these two frames first
For Probe Request frame, due to the potential usage of broadcast address, we think the easiest approach is simply not to provide unnecessary elements like capabilities, operation parameters, or vendor specific elements in the Probe Request frame
  Note that 11aq only considers the Probe Request frame issue of SSID and suggests to avoid sending specific SSID in Probe Request frame or use passive scanning. However, when wildcard SSID is used with broadcast address in active scanning, a rich number of elements may still exist
  Also note that 11be [3] mandates non-AP STA not to include unnecessary elements already, so we believe most of the elements are not needed to be included in Probe Request frame anyway
Proposed requirement:
  11bi shall define a mechanism for the 11bi non-AP STA to refrain from transmitting Probe Request frames containing elements except TBD element(s)

## Slide 4: Issue 2: Avoid Element Fingerprint
For (Re)Association Request frame, since the purpose of the frame is to establish association, elements like capabilities and operation parameters are required to make sure that the negotiation will work
Instead of considering each element individually and providing separate solutions, we think the best solution is simply to encrypt the Frame Body field of the (Re)Association Request frame [4]
  It is demonstrated in [4] that existing symmetric crypto like GCMP can directly be used without the needs of trusted public key distribution, which is hard [4], and the associated asymmetric crypto
  Reusing existing symmetric crypto also avoids significant hardware change, which we think maybe a significant barrier for 11bi technique to be widely accepted
  Since (Re)Association Request/Response exchange maybe embedded with additional negotiation that enable tracking (ex. Additional elements containing information with high specificity, e.g. for link enablement, will also be sent per draft amendments under development, e.g. 11be[1]), once we can encrypt the Frame Body field of the (Re)Association Request frame, it is then natural to encrypt the Frame Body field of the (Re)Association Response frame,
Proposed requirements:
  11bi shall define a mechanism to encrypt the Frame Body field of the (Re)Association Request frame
  11bi shall define a mechanism to encrypt the Frame Body field of the (Re)Association Response frame
  The mechanism defined in 11bi to encrypt the Frame Body field of the (Re)Association Request/Response frame shall use existing cryptographic encapsulation mechanisms (e.g. GCMP 256) in 802.11 specification

## Slide 5: Issue 3: STA MAC address persistence within an ESS
11aq mandates that a single MAC address is retained by the client for the duration of its connection across an ESS, which enables tracking [1]
Ideas [5,6,7] have been proposed to resolve the issue by decoupling the MAC address required for ESS connection and the MAC address used for over the air transmission, and we believe that this is the ideal solution to address the issue
  We call the MAC address to be used by the ESS “private MAC address” and can simply be provided in the (Re)Association Request frame
  The (Re)Association Request frame can be protected, which is already feasible by the proposed mechanism for issue 2, so that 3rd party can not see the carried private MAC address for tracking
  The private MAC address can be different for different ESS
  This is also needed if we want to randomize over the air MAC address (A1, A2) post association without further higher layer change
Proposed requirements:
  11bi shall define a private MAC address that is used by the 11bi non-AP STA or 11bi non-AP MLD for the DS (further details provided in the following slides)
  11bi shall define a mechanism to carry the private MAC address of 11bi non-AP STA or 11bi non-AP MLD in encrypted (Re)Association Request frame
  11bi shall define a mechanism to randomize over the air MAC address of the 11bi non-AP STA or 11bi non-AP MLD (carried in Address 1 field or Address 2 field of the MAC header) during BSS transition

## Slide 6: Summary of the Proposed Requirements
 | Requirement | Issue / Use Case Reference | Status | Information
1 | 11bi shall define a mechanism for the 11bi non-AP STA to refrain from transmitting Probe Request frames containing elements except TBD element(s) | I2 Avoid Element Fingerprint | Proposed | Proposed
2 | 11bi shall define a mechanism to protect the Frame Body field of the (Re)Association Request frame | I2 Avoid Element Fingerprint | Proposed | Proposed
3 | 11bi shall define a mechanism to protect the Frame Body field of the (Re)Association Response frame | I2 Avoid Element Fingerprint | Proposed | Proposed
4 | The mechanism defined in 11bi to protect the Frame Body field of the (Re)Association Request/Response frame shall use existing cryptographic encapsulation mechanisms (e.g. GCMP 256) in 802.11 specification | I2 Avoid Element Fingerprint | Proposed | Proposed
5 | Details in the next slide | I3 STA MAC address persistence within an ESS | Proposed | Proposed
6 | 11bi shall define a mechanism to carry the private MAC address of 11bi non-AP STA or 11bi non-AP MLD in protected (Re)Association Request frame | I3 STA MAC address persistence within an ESS | Proposed | Proposed
7 | 11bi shall define a mechanism to randomize over the air MAC address of the 11bi non-AP STA or 11bi non-AP MLD (carried in Address 1 field or Address 2 field of the MAC header) during BSS transition | I3 STA MAC address persistence within an ESS | Proposed | Proposed

## Slide 7: Revision for 5
11bi shall define a private MAC address that is used by the 11bi non-AP STA or 11bi non-AP MLD for the DS and can be different for different ESS.
The private MAC address of a 11bi non-AP STA or a 11bi non-AP MLD also shall not be carried in the MAC header of the frame and shall not be carried in the frame body of a frame without protection
  if the frame is transmitted by the 11bi non-AP STA or any non-AP STA affiliated with the 11bi non-AP MLD or
  if the frame is transmitted by the 11bi AP to the 11bi non-AP STA or by any AP affiliated with a 11bi AP MLD to any non-AP STA affiliated with the 11bi non-AP MLD
11bi non-AP STA or 11bi non-AP MLD can decide the lifetime of the private MAC address

## Slide 8: Conclusion
We discuss the proposed initial sets of requirements for issue 2 (Avoid Element Fingerprint) and issue 3 (STA MAC address persistence within an ESS) [1]
For issue 2, we focus on the proposed requirements for Probe Request frame and (Re)Association Request/Response frame, which contains a rich number of elements for Element Fingerprint
  Refrain from including elements in Probe Request frame except TBD element(s)
  Protect the Frame Body field of the (Re)Association Request/Response frame using existing cryptographic encapsulation mechanisms (e.g. GCMP 256) in 802.11 specification
For issue 3, we propose to define private MAC address and carry that in the Frame Body field of the encrypted (Re)Association Request frame

## Slide 9: Reference
[1] 11-21-641r6 Proposed Issues
[2] 11-21-1848r2 Requirements Document
[3] Draft P802.11be_D1.31
[4] 11-21-839r0 Privacy Enhancement to avoid Element Fingerprint
[5] 11-21-1395r2 View on Private Identifier
[6] 11-21-1328-00 Changing STA MAC addresses per association and SA/DA hiding
[7] 11-21-1539-00 TGbi - Enhancing Privacy – Rotating MAC addresses over the air

## Slide 10: Appendix – Examples in [4] to demonstrate feasibility to have Protected (Re)Association Request/Response
First, develop a standardized “private limited connection” to generate first-time PMKSA using existing authentication/association procedure
Second, change MAC address and use authentication exchange (ex open) with PMKID in authentication frame to identify PMK and derive a key
Third, use the derived key to protect the following (Re)Association Request/Response frame using existing standardized methods
Fourth, utilize any PMKID privacy enhancement method. Repeat later.
STA
AP
User MAC address 1
Private limited connection to generate first-time PMKSA/PMK and PMKID1
User MAC address 2
Open Authentication with PMKID1
Protected (Re)Association Request/Response
AP uses PMKID privacy enhancement mechanism
STA uses PMKID privacy enhancement mechanism