## Slide 1: Discussion on Measurement Setup ID Setting in SBP Case
Date: 2022-01-28
Authors:
Name | Affiliation | Address | Phone | Email
Pei Zhou | OPPO |  |  | zhoupei1@oppo.com
Chaoming Luo |  |  |  | 
Lei Huang |  |  |  | 
Ning Gao |  |  |  | 

## Slide 2: Background
According to [1] and [2], the following Measurement Setup ID related rules/contents are agreed by TGbf:
  The Measurement Setup ID identifies the attributes/parameters agreed upon between the initiator and one or more responders.
  According to [2] and [3], the following SBP related rules/contents are agreed by TGbf:
  An optional sensing by proxy (SBP) procedure is defined in which:
    An “SBP request” consists of a non-AP STA sending an SBP Request frame to an SBP-capable AP STA.
      A STA that sends an SBP Request frame to invoke SBP (and, as a result, WLAN sensing) is denoted by “SBP requesting STA”.
    An AP STA that receives an SBP request shall send to the SBP requesting STA an SBP Response frame to accept or reject the request.
    An AP STA that accepts an SBP request shall initiate a WLAN sensing procedure with one or more non-AP STAs using operational parameters derived from those indicated within the SBP Request frame.
      Whether the SBP requesting STA participates or not in the WLAN sensing procedure as a sensing responder is TBD.
    Measurement results obtained in a WLAN sensing procedure resultant from an SBP request shall be reported to the SBP requesting STA.

## Slide 3: Measurement Setup in SBP Case
According to [3], STA 3 (as SBP Requesting STA) requests AP (as Sensing Proxy) to perform sensing measurement for it through SBP Request frame.
  SBP Requesting STA (e.g., STA 3) is not Sensing Initiator.
  SBP Responding STA (i.e., AP) is Sensing Initiator.
Then, AP (as Sensing Initiator) initiates Measurement Setup with one or more STA(s) and assigns Measurement Setup ID.
This contribution discusses how to assign Measurement Setup ID for the SBP Requesting STA.

## Slide 4: Measurement Setup ID Setting Methods
Method 1: AP assigns the Measurement Setup ID for SBP requesting STA after successful Measurement Setup.
Example:
  SBP Request:
    SBP requesting STA (e.g., STA 3) requests AP as Sensing Proxy to perform WLAN Sensing through SBP Request frame;
  SBP Response:
    The AP that receives an SBP request shall send to STA 3 an SBP Response frame to accept or reject the request;
  The AP that accepts an SBP request shall initiate measurement setup with one or more STAs and assign a Measurement Setup ID (e.g., Measurement Setup ID = x);
  SBP Confirm:
    If AP successfully finishes measurement setup, it shall notify STA 3 its assigned Measurement Setup ID is x through SBP Confirm frame (TBD);
    If AP fails the measurement setup, expiration of the predefined inactivity time or SBP Confirm frame (TBD) from AP may terminate the measurement setup.
Key point: SBP Confirm frame transmission is mandatory.

## Slide 5: Measurement Setup ID Setting Methods
Method 2: AP shares the Measurement Setup ID in its SBP Response frame ahead of time.
Example:
  SBP Request:
    SBP requesting STA (e.g., STA 3) requests AP as Sensing Proxy to perform WLAN Sensing through SBP Request frame;
  SBP Response:
    The AP that receives an SBP request shall send to STA 3 an SBP Response frame to accept or reject the request;
    The AP that accepts an SBP request shall pre-assign the Measurement Setup ID (i.e., x) for STA 3 and include the ID in SBP Response frame;
  Then, AP initiates Measurement Setup with one or more STAs and assign the same Measurement Setup ID (e.g., Measurement Setup ID = x) as the pre-assigned one;
  SBP Termination (optional):
    If AP fails the measurement setup, AP shall send a termination frame (TBD) to terminate the SBP procedure (and the pre-assigned Measurement Setup ID).
    Note: The pre-assignment of Measurement Setup ID has no influence to the WLAN Sensing procedure.
  Key points: Termination frame transmission is optional.

## Slide 6: Summary
We discussed two methods of assigning Measurement Setup ID for the SBP Requesting STA:
  Method 1: AP assigns the Measurement Setup ID for SBP requesting STA after successful measurement setup.
  Method 2: AP shares the Measurement Setup ID in its SBP Response frame ahead of time.
  Method 2 is preferred because it is simpler.

## Slide 7: SP
Which option do you prefer when defining the method of assigning Measurement Setup ID for the SBP Requesting STA in Sensing by proxy (SBP) procedure?
  Option 1: AP assigns the Measurement Setup ID for SBP requesting STA after successful measurement setup.
  Option 2: AP shares the Measurement Setup ID in its SBP Response frame ahead of time.
Option 1/Option 2/Abstain

## Slide 8: Reference
[1] 11-21-1701-01-00bf-measurement-setup-termination.pptx
[2] 11-21-0504-04-00bf-specification-framework-for-tgbf.docx
[3] 11-21-1692-04-00bf-enhancing-client-based-sensing-sensing-by-proxy.pptx